## Slide 1: Harmonized Sensing NDPA
Date: 2022-09-28
Authors:
Name | Affiliation | Address | Phone | Email
Junghoon Suh | Huawei |  |  | junghoon.suh@huawei.com
Yan Xin |  |  |  | Yan.Xin@huawei.com
Osama AboulMagd |  |  |  | Osama.AboulMagd@huawei.com

## Slide 2: Proposed Harmonized Sensing NDPA
B0
(Ranging)
Bits
:
1 1 6
Sounding Dialog
Token Number
B2
B7
STA Info # 1
STA Info # n
FCS
MAC
Header
Sounding
Dialog
Token
Octets
:
4 4
B1
(HE)
Measurement Instance ID
1 0
Common Info Field 1
Common Info Field 2
……….
4 4
4
AID:
2045
I2R NDP
TX Power
R2I NDP
Target RSSI
Disambi-
guation
Measurement
Set-up ID
B0
B11
B31
B10
B18
B19
B26
B27
B28
AID:
2042
BW of
NDPA
Punctured
Sub-channel
Disambi-
guation
Reserved
B0
B11
B31
B10
B14
B15
B26
B27
B28
SP 1
SP 2
AID 11
Partial BW
Feedback
R2I N_STS
R2I Rep
I2R N_STS
Sensing
Sensing
Disambi-
guation
I2R Rep
SP 3
SP 4/5
B0
B11
B26
B10
B16
B17
B19
B22
B23
B20
SP 4/5
B25
B27
B28
B31
B30

## Slide 3: SP 1
Do you agree to indicate the Measurement Set-up ID in the Special STA Info Field of Sensing NDPA ?
  B28 to B31 are used for the indication of Measurement Set-up ID
  AID for Special STA Info Field is 2045
  Yes
  No
  Abs

## Slide 4: SP1-2
How many bits do you prefer for the Measurement Set-up ID?
  Option 1: 3 bits
  Option 2: 4 bits
  Option 3: 1 byte
  Abs
  Option 1: 12
  Option 2: 7
  Option 3: 1
  Abs: 7
  No answer: 6

## Slide 5: SP1-1
Do you agree to indicate the TX Power Control in the TB case of the Special STA Info Field with AID 2045 of Sensing NDPA ?
  R2I NDP Target RSSI subfield is Reserved
Yes
No
Abs
Unanimously supported

## Slide 6: SP1-3
Do you agree to indicate the Measurement Set-up ID and Sensing indications in the Special STA Info Field of Sensing NDPA ?
  B28 to B30 are used for the indication of Measurement Set-up ID
  B31 is used to indicate the Sensing NDPA
  AID for Special STA Info Field is 2045
  Yes
  No
  Abs

## Slide 7: SP 2
Do you agree to indicate the BW and Preamble Puncturing Patterns of the Sensing NDPA in a subfield of the Common Info field 2?
  AID for Common Info Field 2 is 2042
  Yes
  No
  Abs

## Slide 8: Partial BW FB provides more effective and flexible Preamble Puncturing than Static Puncturing Patterns
Non-OFDMA Preamble Puncturing Patterns in EHT NDP are not flexible and there are very few 40 MHz or 80 MHz non-contiguous preamble puncturing across 320 MHz
Partial BW FB effectively provides more flexible preamble Puncturing
Example
  Even the STA in 80 MHz Operating Channel Width can participate in the 320 MHz sounding
  The STA in 160 MHz Operating Channel Width can participate in the 320 MHz sounding and with the second 40 MHz and the fourth 40 MHz preambles punctured  40 MHz non-contiguous preamble puncturing is not possible in the Static Preamble Puncturing (non-OFDMA Preamble Puncturing)

## Slide 9: Partial BW FB in EHT NDPA

## Slide 10: Punctured Sub-channel (Non-OFDMA Preamble Puncturing) in EHT NDP

## Slide 12: SP 3
Which one of the followings do you prefer?
  Option 1: Disallow the Partial BW Feedback in the Sensing NDPA
    The Operation BW of each responder should be aligned with the BW of EHT NDP PPDU (which is 320 MHz)
    LTF Offset subfield of Ranging NDPA shall be set to “Reserved”
  Option 2: Allow only the same Partial BW Feedback patterns for 320 MHz of the EHT NDPA in the Sensing NDPA
    LTF Offset subfield of Ranging NDPA shall be repurposed for the Partial BW Feedback
    B11 to B16 of the STA Info Field are used for this indication
  Option 1
  Option 2
  Abs

## Slide 13: SP 4
Which one of the followings do you prefer ?
  Option 1: The following Sensing NDP PPDU type can be implied through the BW indication in the SERVICE field of NDPA
  Option 2: The following Sensing NDP PPDU type may be explicitly indicated in the NDPA
  Option 1
  Option 2
  Abs

## Slide 14: SP 5
Which one of the following do you prefer to indicate the Sensing NDPA in the STA Info Field in order to distinguish from the Ranging NDPA?
  Option 1: Both B26 and B31 shall be used for this indication
  Option 2: B26 is the Sensing subfield and B31 is set to “Reserved”
  Option 3: B31 is the Sensing subfield and B26 is set to “Reserved”
  Option 1
  Option 2
  Option 3
  Abs