## Slide 1: Discussion on Device ID renaming
Authors:

## Slide 2: Status of discussion
Device ID has been used to denote the identifier of the STA which may be transmitted/provided to/by the AP.
Several proposals for changing its naming have been discussed
Persistent Opaque Identifier
Persistent Identifier
A mix of both, POI when talking about MAC layer and over the air, PI when talking outside
There is unfinished discussion on what and where the ID is opaque

## Slide 3: Notes on current draft
IEEE 802.11bh D0.2 points the following regarding the Device ID:
9.4.2.296a – Device ID element
  “The ID Blob field contains an opaque identifier from an AP in the ESS. “
12.7.2 EAPOL-Key frames
  “The ID Blob field contains an opaque identifier from an AP in the ESS.”
Annex Z Example opaque device identifier scheme
  Z.1 : “Opaque identifiers are generated and processed by APs. To a non-AP STA they are indistinguishable from a random string and have no significance.”
Current draft does not cover any of the solutions using MAC addresses in the frame to identify the device
  MAAD/RAAD/Transient ID… -> Not clear to me what is the Device ID here

## Slide 4: ID Opaqueness as per current draft
Application layer generates an ID which is sent to the AP’s SME
AP’s SME opaques it and sends it to the STA
STA’s SME always uses opaque ID and stores opaque ID, it does not know what is inside
If needed, the STA will send back the opaque ID to the AP, AP’s SME will de-opaque it and may send it to higher layers and generate a new one for the STA
Therefore:
  ID at STA is always opaque (POI)
  ID in the wireless medium is always opaque (POI)
  ID at AP is opaque (POI), it is only not opaque at application layer (PI)

## Slide 5: Interacting with higher layers, an example
How can a higher layer introduce meaning in the ID
  User opts-in to the tracking going into a web portal (e.g., hotel site, parental-control portal)
  Application infrastructure sends an initial opaque identifier to STA application layer
    This can be done via higher layer or the app infrastructure may ask the AP to provide ID to STA at this moment. -> Anyway this ID will be opaque
  If needed, STA sends opaque identifier to AP
  AP’s SME de-opaques the identifier and may send it to higher layers
  AP may send a new identifier to STA

## Slide 6: Conclusion
We have two flavours of the Device ID
  Opaque identifier, always used at STA, generated by AP
  Not opaque identifier, stored at AP and/or infrastructure (e.g., admission control server)
    At IEEE 802.11 level, it never leaves the SME
Proposal (I still think my proposed naming is good)
  POI: Persistent Opaque Identifier (Device ID at IEEE 802.11 level)
  PI: Persistent Identifier (Device ID when exchange between higher layers/application) and APs SMEs.

## Slide 7: Straw poll
Shall the group adopt the following nomenclature:
  POI: Persistent Opaque Identifier (use of identifier within IEEE 802.11 scope)
  PI: Persistent Identifier (identifier when exchange between higher layers/application) and APs SMEs.

## Slide 8: Backup

## Slide 9: The Device ID in current spec (my view, may be wrong)
Non-AP STA SME
Non-AP STA MAC
AP STA SME
AP STA MAC
MLME-ASSOCIATE.request (DeviceID)
Association Request (Device ID)
MLME-ASSOCIATE.indication (DeviceID)
MLME-ASSOCIATE.response (DeviceID)
MLME-ASSOCIATE.confirm (DeviceID)
Association Response (Device ID)

## Slide 10: The Device ID in current spec (my view, may be wrong)
Non-AP STA SME
Non-AP STA MAC
AP STA SME
AP STA MAC
MLME-ASSOCIATE.request (DeviceID)
Association Request (Device ID)
MLME-ASSOCIATE.indication (DeviceID)
MLME-ASSOCIATE.response (DeviceID)
MLME-ASSOCIATE.confirm (DeviceID)
Association Response (Device ID)
If Device ID present, always opaque
If Device ID present, always opaque

## Slide 11: The Device ID in current spec (my view, may be wrong)
Non-AP STA SME
Non-AP STA MAC
AP STA SME
AP STA MAC
MLME-ASSOCIATE.request (DeviceID)
Association Request (Device ID)
MLME-ASSOCIATE.indication (DeviceID)
MLME-ASSOCIATE.response (DeviceID)
MLME-ASSOCIATE.confirm (DeviceID)
Association Response (Device ID)
If Device ID present, always opaque
If Device ID present, always opaque
Something
Something
Device ID1
Device ID2

## Slide 12: The Device ID in current spec (my view, may be wrong)
Non-AP STA SME
Non-AP STA MAC
AP STA SME
AP STA MAC
MLME-ASSOCIATE.request (DeviceID)
Association Request (Device ID)
MLME-ASSOCIATE.indication (DeviceID)
MLME-ASSOCIATE.response (DeviceID)
MLME-ASSOCIATE.confirm (DeviceID)
Association Response (Device ID)
If Device ID present, always opaque
If Device ID present, always opaque
Something
Something
Device ID1
Device ID2
Device ID1==Device ID?
Device ID2==Device ID?

## Slide 13: The Device ID in current spec (my view, may be wrong)
Non-AP STA SME
Non-AP STA MAC
AP STA SME
AP STA MAC
MLME-ASSOCIATE.request (DeviceID)
Association Request (Device ID)
MLME-ASSOCIATE.indication (DeviceID)
MLME-ASSOCIATE.response (DeviceID)
MLME-ASSOCIATE.confirm (DeviceID)
Association Response (Device ID)
If Device ID present, always opaque
If Device ID present, always opaque
Something
Something
Device ID1
Device ID2
Device ID1==Device ID?
Device ID2==Device ID?

## Slide 14: The Device ID in current spec (my view, may be wrong)
Non-AP STA SME
Non-AP STA MAC
AP STA SME
AP STA MAC
MLME-ASSOCIATE.request (DeviceID)
Association Request (Device ID)
MLME-ASSOCIATE.indication (DeviceID)
MLME-ASSOCIATE.response (DeviceID)
MLME-ASSOCIATE.confirm (DeviceID)
Association Response (Device ID)
Are these Device IDs the same?
If Device ID present, always opaque
Something
Something
Device ID1
Device ID2
Device ID1==Device ID?
Device ID2==Device ID?

## Slide 15: The Device ID in current spec (my view, may be wrong)
Non-AP STA SME
Non-AP STA MAC
AP STA SME
AP STA MAC
MLME-ASSOCIATE.request (DeviceID)
Association Request (Device ID)
MLME-ASSOCIATE.indication (DeviceID)
MLME-ASSOCIATE.response (DeviceID)
MLME-ASSOCIATE.confirm (DeviceID)
Association Response (Device ID)
If Device ID present, always opaque
If Device ID present, always opaque
Something
Something
Out of scope, Device ID1 for SME is opaque?
Out of scope, for SME is opaque?
Device ID1

## Slide 16: Ideas for decisions
Based on our discussion
Shall we have different naming for Device ID coming from external entity, SME and over the air?
Is the Device ID always opaque within 11bh scope?