## Slide 1: Pre-Association Management Frame Protection
Date: 2022-10-12
Authors:

## Slide 2: Abstract
Some requirements in requirements document (22/1848r16) specify protection for management frames.
Some of them are management frames from associated STA, some of them are management frames from unassociated STA.
There should be more protection mechanism for management frames from unassociated STA (preferably, pre-association management frames).
-> pre-association management frames has a high risk to be manipulated, especially because the non-AP STA and AP do not authorize each other in pre-association.

## Slide 3
5 | 11bi shall define a mechanism for a CPE Client and CPE AP to protect the (Re)Association Request/Response. | I2 | Approved | Proposed – 22/109r3 (10 March 2022) Approved (Motion #16, July 13, 2022)
20 | 11bi shall define a mechanism for the 11bi non-AP STA to refrain from transmitting Probe Request frames containing elements except TBD element(s) | I2 | Approved | Proposed – 22/109r3 (10 March 2022; SP Y15, N7, A14) Note: tracks with R3 Approved (Motion #13, 13 May 2022)
21 | 11bi shall define a mechanism to protect the Frame Body field of the (Re)Association Request frame | I2 | Approved | Proposed – 22/109r3 (10 March 2022) To be motioned –agreed by unanimous consent 4/21/2022 Approved (Motion #13, 13 May 2022)

## Slide 4
22 | 11bi shall define a mechanism to protect the Frame Body field of the (Re)Association Response frame | I2 | Approved | Proposed – 22/109r3 (10 March 2022) To be motioned –agreed by unanimous consent 4/21/2022 Approved (Motion #13, 13 May 2022)
24 | 11bi shall define a mechanism to carry the DS MAC address of a 11bi non-AP STA or an 11bi non-AP MLD in a protected (Re)association Request frame (and any other TBD protected management frames) from the 11bi non-AP STA to a 11bi AP or from the 11bi non-AP MLD to a 11bi AP MLD. | I3 | Approved | Proposed – 22/109r3 (10 March 2022) Approved (Motion #16, July 13, 2022)
26 | 11bi shall define an optional protected version of the following unicast management frames between a CPE AP and an associated CPE Client: • Notify Channel Width frame • SM Power save frame | I3 | Approved | Proposed – 22/623r2 (14 April 2022) Approved (Motion #16, July 13, 2022)

## Slide 5
52 | 11bi shall define a mechanism for an 11bi non-AP MLD to request capabilities and operation parameters of APs affiliated with the associated 11bi AP MLD using a protected request/response action frame. | I2, I6, I7 | Approved | Proposed 22/1306r2 (14 Sept 2022) Straw poll – unanimous consent 14 Sept 2022 Approved (Motion #20, 14 Sept 2022)
53 | 11bi shall define a mechanism that will allow a non-AP STA to verify the identity of a known AP before association (without exposing its identity). |  | Approved | Proposed 22/1376r0 (25 August 2022) Straw poll 12Y, 4N, 3A; 15 Sept. 2022 Approved (Motion #25, 15 Sept 2022)

## Slide 6
Proposal for Requirements Document
54 | 11bi shall define a mechanism that will allow an AP to verify the identity of a known non-AP STA before association (without exposing its identity).
Do you think this requirement should be added to Requirements Document (22/1848) ?