## Slide 1: Resolution for CID19 and CID20
Date: 2022-10-11
Authors:

## Slide 2: Abstract
CID19 and CID20 focus on
  PASN (Pre-Association Security Negotiation) and
  FTM (Fine Tuning Measurement)
Defined in 802.11az - Enhancements for positioning (draft)
And
  WUR (Wake Up Radio) maybe? – defined in 802.11ba - Wake-Up Radio Operation
This document proposes a solution for CID19 and CID20

## Slide 3
CID | Commenter | Comment | Subclause | Proposed Change
19 | Jonathan Segev | It is not clear how the Device ID mechanism supports unassociated PASN operation. the PASN operation is required to support management procedure that do not require data transfer, examples are FTM and 11ba. | 12.2.11 | Add support for Device ID in PASN.
20 | Jonathan Segev | The mechanism for device ID should be such that to a single network a device with an on going unassociated session should be identifiable as single device to the network (ESS). An example of such operation is the need to two way report for FTM; The client STA reports measurement conducted to each individual AP while the multiple outstanding FTM sessions are in progress, the NW is able to associate the measurement from multiple sessions to be attributed to a single client and thus can identify client location. This client may not be associated to the network. | 12.2.11 | Add a functionality that allows a device to be identified to the ESS as a single entity.

## Slide 4
Recap
PASN (Pre-Association Security Negotiation): establishing a PTKSA and the corresponding shared keys between a PASN capable STA and AP (defined in 11az).
Conventional PMK and PTK Generation
PASN PMK and PTK Generation

## Slide 5
Recap
PASN (Pre-Association Security Negotiation): It consists of three Authentication frames.
PTK
PTK

## Slide 6
Recap
FTM (Fine Timing Measurement): The FTM procedure allows a STA to determine its range relative range and its direction to or from another STA using Time Of Flight (TOF) time difference of arrival and phase measurement. Basically, determining location.
Unassociated STA FTM procedure
Associated STA FTM procedure
Unassociated STA never goes into 4-way HS, so it will never get device ID in 4-way HS.
-> unassociated STA with RMA will never be identified
PMK
PTK
PMK&PTK

## Slide 7
Recap
FTM (Fine Timing Measurement): Multi-session FTM in ESS is also possible.
APs (AP1, AP2, AP3 et.) belong to the same ESS.
Non-AP STA may establish multiple FTM sessions with multiple APs for location purposes.
Non-AP STA may use different RMAs in different sessions to avoid being tracked.
ESS

## Slide 8
Solution for CID19
Exchange the Device ID in authentication frame exchange in PASN.
Use already existing IE (“Device ID IE” defined for FILS) in Authentication frames
AP assigns device ID in Authentication Msg2
Non-AP STA provides device ID in Authentication Msg1
Since Authentication Frame Body is not encrypted, it is better to use opaque ID (derived from Device ID) in Device ID IE.

## Slide 9
Solution for CID19
Signaling Flow
Non-AP STA
AP
Authentication Msg1
Authentication Msg2 (aaa)
Authentication Msg3
FTM Procedure
Authentication Msg1 (aaa)
Authentication Msg2 (bbb)
Authentication Msg3
FTM Procedure
1st Assoc
2ndAssoc
Device ID = 111 -> Opaque ID = aaa
Device ID = 222 -> Opaque ID = bbb

## Slide 10
Solution for CID20
Same as CID19 but assign a Device ID for each FTM session in ESS (AP1, AP2, …)
Non-AP STA
AP1
AP2
AP3
FTM Session3
FTM Session1
FTM Session2
Device ID1 – Auth Msg2
Note that
- the current bh D0.2 assigns one device ID per ESS,
- this solution assigns one device ID per session in ESS
- The generated device ID will be used in the next session
Device ID1 – Auth Msg1
Device ID2 – Auth Msg2
Device ID2 – Auth Msg2
Device ID3 – Auth Msg3

## Slide 11
Thanks 