## Slide 1: Discussion on LB266 CR for CID 13942
Date: 2022-10-17
Authors:
Name | Affiliation | Address | Phone | Email
Yanyi Ding | Panasonic Corporation |  |  | yanyi.ding@sg.panasonic.com
Rojan Chitrakar |  |  |  | 
Yoshio Urabe |  |  |  | 
Rajat Pushkarna |  |  |  | 

## Slide 2
CID 13942
CID | Clause | Category | Page | Comment | Proposed change
13942 | 35.5.2.4 | T | 489.29 | In 26.5.2.5 UL MU CS mechanism, it is regulated that in a TB UL MU transmission, if CS requirement is indicated, ED-based CCA shall be performed by STAs on 20MHz subchannels overlapping the allocated RU/MRU. If any of the 20MHz subchannels is detected as busy, STA does not transmit TB PPDU at the allocated RU/MRU. Large-size RU/MRU is wasted even if a small number of 20MHz subchannels is detected as busy. (Refer to 20/1886r1 for more details.) | STAs should be enabled to adapt allocated RU/MRU according to ED-based CCA results. Commenter will bring a contribution.

## Slide 3
Background
In TB UL MU transmission described in 26.5.2.5, if CS requirement is indicated in the Trigger frame, ED is used to sense the medium by STAs on 20MHz subchannels overlapping the allocated RU/MRU.
If any of the 20MHz subchannels is indicated as busy by ED-based CCA or virtual CS, the STA does not transmit TB PPDU at the allocated RU/MRU.
Whole allocated large-size RU/MRU is wasted even if only a small number of 20MHz subchannels are detected as busy, which would degrade system throughput.

## Slide 4
Recap of the proposed solution
In 20/1886r1 we analyzed the problem and proposed an RU Adaptation procedure to address it.
In an RU adaptation procedure, a non-AP STA may puncture allocated RU/MRU according to the state of the medium. (Not applicable to MU-MIMO transmission)
  Only the RU/MRU is punctured, other parameters for TB UL transmission remain unchanged.
In this case, the waste of large-size RU/MRU can be avoided.
Example

## Slide 5
SP Result

## Slide 6
Punctured RU/MRU
Associated Punctured RU/MRU is defined for each large-size RU/MRU
  Associated Punctured RU/MRU is a set of possible options of punctured RU/MRU where the STA shall choose from when a large-size RU/MRU is allocated.
  Some restrictions may be enforced, for example, a threshold for the size.
Example (the size of associated punctured RU/MRU shall not be smaller than 50% of the size of allocated RU/MRU)
BW (MHz) | Large-size RU/MRU | Associated Punctured RU/MRU
40, 80, 160, 320 | RU484 | RU484, RU242 (2 options)
80, 160, 320 | RU242+RU484 | RU242+RU484, RU484
80, 160, 320 | RU996 | RU996, RU242+RU484 (4 options), RU484 (2 options)
160, 320 | RU484+RU996 | RU484+RU996, RU996, RU484+RU242 (4 options)
… | … | ...
* When part of the allocated RU/MRU which is detected as idle does not match or cover any of its associated punctured RU/MRU, the allocated RU/MRU shall not be punctured.

## Slide 7
Signaling options
Signaling options for the EHT TB PPDU to indicate punctured RU/MRU.
  Option 1: no explicit signaling
    Blind decoding/ Signal detection of pre-EHT modulated fields in all 20MHz subchannels.
    No change for signalings of EHT TB PPDU; rules of AP decoding EHT TB PPDU will be changed.
  Option 2: explicit signaling
    TB puncturing is explicitly signaled in U-SIG field of EHT TB PPDU
    Signalings of EHT TB PPDU will be changed; minor change for rules of AP decoding EHT TB PPDU.

## Slide 8
Example Explicit Signalings
Following the example in slide#6, for the largest size MRU (3×996+484-tone), there are 14 options for Associated Punctured RU/MRU, thus 4 bits are needed to indicate the punctured RU/MRU.
A Punctured RU/MRU subfield in U-SIG field of EHT TB PPDU, together with allocated RU/MRU, indicates the punctured RU/MRU.
Allocated RU/MRU | Value of the Punctured RU/MRU subfield | punctured RU/MRU
RU996 | 0 | 1st RU242+2nd RU484 within the RU996
 | 1 | 2nd RU242+2nd RU484 within the RU996
 | 2 | 3rd RU242+1st RU484 within the RU996
RU996 | 3 | 4th RU242+1st RU484 within the RU996
 | 4 | 1st RU484 within the RU996
 | 5 | 2nd RU484 within the RU996
 | 6-14 | Reserved
 | 15 | Allocated RU
RU484+RU996 | 0 | RU996 of the RU484+RU996
 | 1 | 1st RU242+2nd RU484 within RU996 of allocated RU
 | 2 | 2nd RU242+2nd RU484 within RU996 of allocated RU
 | 3 | 3rd RU242+1st RU484 within RU996 of allocated RU
 | 4 | 4th RU242+1st RU484 within RU996 of allocated RU
 | 5-14 | Reserved
 | 15 | Allocated RU
… | … | ...

## Slide 9
Example Explicit Signalings
Field | Bits | Subfield
U-SIG-1 | B0-B2 | PHY Version Identifier
 | B3-B5 | BW
 | B6 | UL/DL
 | B7-B12 | BSS Color
 | B13-B19 | TXOP
 | B20-B25 | Disregard Punctured RU/MRU
U-SIG-2 | B0-B1 | PPDU Type and Compression Mode
 | B2 | Validate
 | B3-B6 | Spatial Reuse 1
 | B7-B10 | Spatial Reuse 2
 | B11-B15 | Disregard
 | B16-B25 | CRC+Tail
In the U-SIG field, the first Disregard subfield can be reused for Punctured RU/MRU subfield.
Further limitation may be applied to associated punctured RU/MRU, to ensure the U-SIG field content is identical in all non-punctured 20 MHz subchannels within each 80 MHz segment and avoid impact on R1 STAs.

## Slide 10
Discussion
As discussed in 20/1886r1, the RU adaptation procedure can improve throughput of TB UL MU transmission with large-size RU/MRU.
Changes in spec may include:
  STA/AP rules description to 35.5.2 EHT MU Operation
  Signalings in Trigger frame
  Signalings in EHT TB PPDU (if signaling option 2 is adopted)
  Capabilities elements.
If adopted, the feature will be optional. R1 STAs will not be affected.

## Slide 11
SP#1
Do you agree that 11be should support RU adaptation procedure?
  Non-AP STAs may puncture allocated RU/MRU for EHT TB PPDU according to ED-based CCA results when it is not MU-MIMO transmission.
Y/N/A:

## Slide 12
SP#2
Which signaling option do you prefer for punctured EHT TB PPDU?
  Option 1: no explicit signaling (AP may decode the EHT TB PPDU by blind decoding or preamble detection)
  Option 2: explicit signaling (AP may decode the EHT TB PPDU following TB puncturing information in U-SIG field)
Option 1/Option 2/A: