## Slide 1: CSD Configuration for Sensing
Date: 2022-10-06
Authors:
Name | Affiliations | email
Qinghua Li | Intel | Qinghua.li@intel.com
Cheng Chen |  | Cheng.chen@intel.com
Hao Song |  | Hao.song@intel.com
Juan Fang |  | 
Robert Stacey |  | 

## Slide 2: Outline
CSD Recap
Problem statement
Proposed solution
Summary

## Slide 3: CSD Recap (1/3)
Two types of CSD, per-antenna and per-stream
Per-stream CSD 1
D
Per-antenna CSD 1
Per-stream CSD 2
Per-antenna CSD 2
Per-antenna CSD 3

## Slide 4: CSD Recap (2/3)
Single stream transmission with only per-antenna CSD
Per-antenna CSD 1
Per-antenna CSD 2
Per-antenna CSD 3

## Slide 5: CSD Recap (3/3)
Per-stream CSD values are specified in the spec
Per-antenna CSD values are specified for single stream transmission, but they are up to implementation for multi-stream transmission in which case Rx doesn’t know the CSD values applied at Tx as specified in
19.3.11.11.2 Spatial mapping

## Slide 6: Problem Statement
Per-antenna CSD causes the overlapping of two sets of multipaths such that the path of interest can be interfered by overlapping paths
Rx can’t tell whether a detected path was delayed or not such that the sense of distance may be wrong
Wrong sense of multipath spread
Path covered by overlapping

## Slide 7: Proposed Solution
Per-antenna CSD should not be applied to the long training field of 11bf sounding NDP
  Multipaths between each Tx-Rx antenna pair should be observed without interferences from the other pairs
For multi-antenna sounding, per-stream CSD should be used. Namely, for N Tx antennas to sound the channel, N’ x N’ P-matrix encoded LTF with per-stream CSDs should be used, where N’ is the P-matrix size greater or equal to N.
Similar approach is adopted by 802.11az ranging by setting the spatial mapping matrix to be the identity matrix, as pointed out by Christian Berger

## Slide 8: CSD of 11az Ranging NDP
27.3.18a.1 HE Ranging NDP

## Slide 9: Conclusions
Per-antenna CSD causes the overlapping and shift of multipath that degrade the detection of the interested path or the sense of distance
For 11bf multi-antenna sensing, only per-stream CSD should be used, which is similar to 11az

## Slide 10: Straw Poll 1
Do you support that per-antenna CSD shall not be used in 11bf NDP LTF for multi-antenna sounding?
Y/N/A

## Slide 11: Straw Poll 2
Do you support that
  for sub 7 GHz sensing, the spatial mapping matrix shall be set to the identity matrix, which is specified in 27.3.18a.1 HE Ranging NDP of 802.11az spec ?
Y/N/A

## Slide 12: Backup

## Slide 13: CSD Setting in 11me Spec (1/2)

## Slide 14: CSD Setting in 11me Spec (2/2)