## Slide 1
Auth-Assoc Privacy Protection
Date: 2022-10-12
Authors:

## Slide 2: Introduction
Requirements 1, 2, 4, 5 in https://mentor.ieee.org/802.11/dcn/21/11-21-1848-16-00bi-requirements-document.docx describe privacy protection for Authentication/Association.
We likely want to leverage existing security protocols to establish security associations when 11bi services are offered rather than define a new one.
It would also be good to provide a mechanism that allows 11bi and non-11bi STAs to connect to the same BSS
This contribution discusses a mechanism to protect Auth/Assoc/4-way as an overlay to existing security mechanisms.

## Slide 3: Basic Requirements
The mechanism would be discovered through capabilities advertised by the AP. Could be aligned to privacy capabilities advertisement for 11bi.
The new protocol would be overlayed over existing authentication protocols:
  Open/EAP, FT, SAE, FILS, PASN(?)
  This protocol would just protect Auth/Assoc/{4-way}
  The other protocols would continue to be used to establish the SA for the connection.
The protocol would create a protected link. It would not establish trust.
The negotiated keying material could be used to protect other 11bi frames if it makes sense (until the SA is in place)

## Slide 4: Example Privacy Key Negotiation Protocol
The security protocol could be based on DH overlayed on Auth/Assoc.
NOTE: The message flow below only includes the privacy key derivation for the frames indicated.
STA
AP
STA generates P_s, p_s
AP provisioned with P_a, p_a
STA discovers that AP’s 11bi privacy capabilities
STA obtains AP’s public key – through discovery (e.g. ANQP) or offline mechanisms
802.11 Authentication( SHA256(P_a), P_s, [Snonce, A_s]K1)
STA generates A_s, a_s
M = p_s * P_a
K1 = HKDF(<>, “intermediate key one”, M.x)
802.11 Authentication( SHA256(P_s), SHA256( [Snonce, Anonce, B_a, {A_auth} KE]K2)
AP generates B_a, b_a
M = p_a * P_s
K1 = HKDF(<>, “intermediate key”, M.x)
N = b_a * P_s
k2 = HKDF(<>, “intermediate key two”, N.x)
L = ((p_a +b_a) modulo q) * P_s)
KE = HKDF(I-nonce | R-nonce, “Priv Key”, M.x | N.x | L.x)
A_auth = H (I-nonce | R-Nonce | P_s.x | P_a.x | 0)
802.11 Association Request( SHA256(P_a), [S_auth] K2, {ASSOC PAYLOAD}KE)
N = a_s * B_a
k2 = HKDF(<>, “intermediate key two”, N.x)
L = p_s * (P_a + B_a)
KE = HKDF(I-nonce | R-nonce, “Priv Key”, M.x | N.x | L.x)
STA validates A_auth
S_auth = H (I-nonce | R-Nonce | P_s.x | P_a.x | 0)
AP validates S_auth
AP generates Association Response frame
802.11 Association Response {ASSOC PAYLOAD}KE)

## Slide 5: Other notes on authentication protocol
The protocol could be defined to precede the authentication frame exchanges in the case of FT, FILS, PASN
The third message could be carried over the second frame transmitted by the STA – regardless of whether it was an authentication frame or an association request frame.
Do we need to protect the authentication frames or just association?