## Slide 1: On energy harvesting and the differentiation with RFID
Date: 2022-10-25
Authors:
October 2022
Name | Affiliation | Address | Phone | Email
Weijie Xu | OPPO |  |  | xuweijie@oppo.com
Yinan Qi |  |  |  | v-qiyinan@oppo.com
Doc.: IEEE 802.11-22/1799r0

## Slide 2
Characteristics of RFID
  RFID has already been widely used in many verticals. The essential function of RFID is identification.
  Key techniques include RF energy harvesting and backscattering.
    active RFID can also use a battery
  Ultra-low complexity and Ultra-low cost.
    Currently, the cost can be as low as ~0.03 $.
    Very simple RF and baseband circuits with limited memory (~x KB).
  Limited performance, efficiency and reliability.
    Communication distance less than 10 meters
    limited number of RFID devices can be processed per second
October 2022
Doc.: IEEE 802.11-22/1799r0
Weijie Xu(OPPO)
Slide 2

## Slide 3
Constraints of RFID
    Only support single-tag connection at one time and NOT able to communicate to with multiple RFID tags simultaneously.
    No power management, i.e., only operating instantly with harvested power
    Reader talks first since the RFID tag requires RF power and carriers.
    Performs CSMA by reader.
    Very low system efficiency
      Although multiple RFID channels in a band, FDM is Not supported due to ultra-low complexity of RFID tags (e.g., no channel level filtering)
    Strong interference between DL/UL due to full-duplex operation.
      Communication distance can be significantly improved with separate transmitter and receiver of the reader
October 2022
Doc.: IEEE 802.11-22/1799r0
Weijie Xu(OPPO)
Slide 3

## Slide 4
What can be leaned from RFID?
  Techniques to achieve battery-free.
    RF energy harvesting etc.
  Techniques to achieve ultra-low complexity and ultra-low power consumption.
    Backscattering
    Ultra-low power circuit
    Low order modulation
  Techniques to go beyond the constraints of RFID
    Balance between the cost and the performance shall be the objective
October 2022
Doc.: IEEE 802.11-22/1799r0
Weijie Xu(OPPO)
Slide 4

## Slide 5
Aspects differentiating AMP IoT from RFID
    The target use cases for AMP IoT and RFID are different.
      Reusable AMP devices in use cases including logistics, supply chain, smart manufacturing, smart home, positioning, agriculture, etc.
        Higher complexity and higher power consumption (but less than 1mw) than that of RFID is allowable.
    Higher performance than RFID is expected for AMP IoT
      Support longer communication distances, up to 200 meters for outdoor scenario
      Support higher system capacity, e.g., enabling multiple channel multiplexing
      Support higher reliability
    It can enable the communication between AMP IoT devices and smart phone (non-AP STA).
October 2022
Doc.: IEEE 802.11-22/1799r0
Weijie Xu(OPPO)
Slide 5

## Slide 6
Energy harvesting
  A variety of ambient power sources, e.g., RF radio waves, temperature difference, vibration, light etc. can be used for AMP IoT.
    Only one type of power source may be utilized for one AMP IoT device in one use case
  How to perform energy harvesting can be up to implementation.
  If RF power is used, the AP needs to send RF power signals to the AMP devices. A dedicated power link may be needed to provide this RF power signals.
    It can be further discussed how to provide this power link, whether it needs to be specified or up to implementation.
October 2022
Doc.: IEEE 802.11-22/1799r0
Weijie Xu(OPPO)
Slide 6

## Slide 7
Summary
    In this submission, the following are present:
      The merits and constraints of RFID.
      What can be learned from RFID
      Aspects differentiating AMP IoT from RFID
      Energy harvesting
October 2022
Doc.: IEEE 802.11-22/1799r0
Weijie Xu(OPPO)
Slide 7