## Slide 1: New Use Case for AMP IoT Devices: Smart Grid
Date: 2022-10-25
Authors:
Doc.: IEEE 802.11-22/1800r0
October 2022
Name | Affiliation | Address | Phone | Email
Yinan Qi | OPPO |  |  | v-qiyinan@oppo.com
Weijie Xu |  |  |  | xuweijie@oppo.com
Xu Zhao | Beijing Smart Chip Microelectronics Technology Co., Ltd. |  |  | zhaoxu@shchip.sgcc.com.cn

## Slide 2: Background
Following use cases have been discussed in earlier meetings
  Use case 1 Smart manufacturing: inventory/attendance check, real-time inspection and tracing, asset tracking/positioning, and industrial environment/production line sensing and monitoring [1]-[2]
  Use case 2 Data center: environmental monitoring, facility monitoring and asset management [3]
  Use case 3 Smart home: asset management, home environment monitoring and home security [1].
  Use case 4 Logistics and warehouse: goods tracking and inventory check [1]
  Use case 5 Smart agriculture: monitoring of soil moisture, soil fertility, temperature, wind speed, plant growth etc., and controlling of the agricultural facilities [1]
  Use case 6 Indoor positioning: positioning in giant shopping mall, factories, warehouses, etc. [4]
New use case
  Use case 7 Smart Power Grid: Sensing of sound, heat, pressure, etc., smart meter to achieve awareness of device/equipment status
Doc.: IEEE 802.11-22/1800r0
October 2022

## Slide 3: Smart Power Grid: State of the Art
State of the Art
  Large-scale application of power sensors in power transmission, substation and power distribution has been realized.
  The wide deployment of hundreds of sensors to detect leakage current, vibration and pressure, enabling the collection of electrical, non-electrical, environmental data.
Tower Tilt Partial Discharge Water in cabinet Wire Icing
Doc.: IEEE 802.11-22/1800r0
October 2022

## Slide 4: Smart Power Grid: State of the Art
State of the Art
  Collet various physical quantities such as sound, light, electricity, heat, magnetism, force and other physical quantities of power equipment during operation to achieve awareness of device/equipment status.
  Support the comprehensive perception and intelligent application of information in the production and operation process of the smart power grid.
Fig. Smart Power Grid with sensing and metering [5]
Doc.: IEEE 802.11-22/1800r0
October 2022

## Slide 5: Smart Power Grid: Main Issues
Main Functionalities
  Real-time monitoring of power grid equipment status and operating environment;
  Timely discovering and handling potential safety hazards in the overhaul and operation and maintenance of power equipment.
Current Issues
  Demand for equipment status awareness has increased sharply;
  Diversification of urban and rural areas;
  High cost and poor deployment flexibility.
  Difficult to maintain the sensing network with active devices driven by conventional battery
  Low flexibility of communication rate, transmission distance and power sensing services
Doc.: IEEE 802.11-22/1800r0
October 2022

## Slide 6: Use Case 7-1: Substation Status Sensing and Metering
Services and applicable scenarios
  Sub-station plays a vital role in the electrical power system to guarantee the continuity of the electrical power supply.
  Massive number of sensors and meters to monitor temperature, humidity, etc.
  Service area: <50 000 m2
Requirements
  Massive deployment: ultra-low cost and massive connection
  Inaccessible location: maintenance-free and battery-less for long service time
  Data rate: 20kbps
Doc.: IEEE 802.11-22/1800r0
October 2022
  Coverage: 10-30 m for indoor case and up to 100 meters for outdoor

## Slide 7: Use Case 7-2: High Voltage Transmission Lines Sensing and Monitoring
Services and applicable scenarios
  High voltage transmission lines deliver electricity over long distances to reduce the amount of energy lost during the distance. .
  Sensing and monitoring of high voltage transmission lines and towers for operation faults such as power leakage, tower tilting, etc.
Requirements
  Inaccessible location: maintenance-free
  Long service time: battery-less with ultra low power consumption
  Data rate: 3kbps
  Coverage: 200 m for outdoor case
China's State Grid plans to invest more than 150 billion yuan ($22 billion) in the second half of 2022 in ultra high voltage (UHV) power transmission lines
Doc.: IEEE 802.11-22/1800r0
October 2022

## Slide 8: Summary
This submission presents
  New use cases: Smart Power Grid
  Current issues and expectation
  Services and applicable scenarios
  Typical requirements
Doc.: IEEE 802.11-22/1800r0
October 2022

## Slide 9: Reference
IEEE 802.11-22/0963r0, Use Cases for AMP IoT Devices.
IEEE 802.11-22/1339r0, Use Cases of smart manufacturing.
IEEE 802.11-22/1341r1, Use Cases of Data Center Infrastructure Management.
IEEE 802.11-802.11-22/1559r0, Updated Use Cases for AMP IoT Devices
M. El Brak, S. El Brak, and D. Benhaddou, “Wireless Sensor Network applications in smart grid,” in Proc. of 2014 International Renewable and Sustainable Energy Conference (IRSEC)
Doc.: IEEE 802.11-22/1800r0
October 2022