## Slide 1: Next Gen After 11be: Band and Complexity Discussion
Date: 2022-11-15
Authors:

## Slide 2: Outline
Band Support – Products Progression
802.11 Complexity Progression
Discussion and Conclusions

## Slide 3: Band Support – Products Progression
Technologies requiring major hardware modifications (e.g. new band support, additional or more complex antennas) have historically seen very slow uptake
Technologies with major MAC/PHY development but more limited hardware modifications have been immediately successful
Technology | Ratified | 100Mu Smartphone Shipments | Scope of Product Hardware Changes
5 GHz | 1999 | 2011* | Additional antenna and diplexer
MIMO | 2009 | 2015 | Two additional antennas and one diplexer
60 GHz/802.11ad | 2012 | N/A | Additional chip(s), module, antenna array
160 MHz | 2013 | Expected 2023 | Front-end and antenna re-design for 6 GHz
Technology | Ratified | 100Mu Smartphone Shipments | Scope of Product Hardware Changes
802.11ac | 2013 | 2013 | Minor front-end changes for 256-QAM/80 MHz
802.11ax | 2019 | 2019** | Minor front-end changes for 1024-QAM***
* PC shipments exceeded 100Mu earlier than 2011, but when smartphones became a major product category, they only supported 2.4 GHz for several years
** 80 MHz/5 GHz only
*** Numerous suppliers enabled proprietary 1024-QAM for 802.11ac; no changes were required in those cases to enable 802.11ax

## Slide 4: 802.11 Complexity Progression
Mainstream WLAN started with 20 MHz and single antenna - 11b, 11g
Dimensions increased
  Wider BWs in 11a
  MIMO in 11n
Dimensions further progressed in 11ac/ax/be
  Up to 320 MHz BW
  Up to 16 antennas
Progression of these specifications translated into products
  8 antenna APs
  3 and 4 antenna STAs
  320 MHz BWs

## Slide 5: Regression Seems to Have Taken Place
What happened to 8 antenna APs?
  Seem to be scaling back
  4 antenna AP are becoming a norm
  8 Antenna APs are rare (some in Enterprise)
What happened to 3 and 4 Antenna STAs?
  Diminished, very few products in the market
  2 antenna STAs are currently a norm

## Slide 6: Possible Reasons for Regression?
Peak throughputs strong
  Mainly exceeding data-rate feeds into homes
Availability of new 6GHz band
  Less congestion
  Better system throughput
Decrease in latency and throughput increase through MLO
  EMLSR, STR, NSTR, ….
Cost

## Slide 7: Discussion and Conclusions (1)
New spectrum adoption takes time, 1.2 GHz of spectrum was made available in many regions of the world just recently
It will take at least one more generation of WLAN to start utilizing this new spectrum fully and effectively
It is very hard to visualize, successfully (market adoption) adding new mmWave modem to WLAN at this point given cost trends, complexity trends, and 6GHz spectrum availability
Sub-7GHz products have yet to see widespread adoption of MLO, 3-4 antenna STAs, 8 antenna APs and 320 MHz BWs – ~8x throughput gain over today’s mainstream
Before all this happens there seem to be no need to re-develop mmWave technology

## Slide 8: Discussion and Conclusions (2)
mmWave technology may gain traction in the future, but as we see it not in UHR
  mmWave Complexity/Cost
    Antenna arrays
    Front ends
    PHY (much more than just up-clocking of existing .11 PHY), MAC
    RF, antennas, beamforming/tracking - (most complexity)
Multiple presentations in WNG and UHR SG show numerous features/techniques that address QoS, Latency, Reliability, Security, Channel Access, Throughput, Range, etc.
  Combined with enhancements such as extended MLO, 3-4 antenna STAs, 8 antenna APs and 320 MHz BWs, will result in a very strong UHR standard and products
  (enhancements + UHR) complexity/cost << (mmWave) complexity/cost

## Slide 9: Discussion and Conclusions (3)
Leave mmWave technology for the next decade in order not to risk evolution path of mainstream WLAN
Better to use resources to improve mainstream WLAN