## Slide 1: Reuse of HE (TB) ranging NDP and EHT sounding NDP in 802.11bf
Date: 2022-11-07
Authors:
Name | Affiliation | Address | Phone | Email
Yan Xin | Huawei Technologies | Ottawa, Ontario |  | yan.xin@huawei.com
Junghoo Suh |  |  |  | Junghoon.suh@Huawei.com
Narengerile |  |  |  | narengerile@huawei.com
Stephen McCann |  |  |  | stephen.mccann@huawei.com
Ross Jian Yu |  |  |  | ross.yujian@huawei.com

## Slide 2: Background
Motion #141 on the usage of the NDP formats for 802.11bf sub-7 GHz sensing passed by unanimous consent [1]. The motion text is referred as:
Further questions
  The HE Ranging NDP and HE TB Ranging NDP formats shall be used for 802.11bf sub-7 GHz sensing when PPDU BW ≤ 160 MHz
  The EHT sounding NDP format (including specified preamble puncturing patterns) shall be used for 802.11bf sub-7 GHz sensing when PPDU BW = 320 MHz
  Note: which preamble puncturing patterns to be supported are TBD.
Can the HE (TB) ranging NDP be applicable to both TB sensing measurement instance and non-TB sensing measurement instance when PPDU BW ≤ 160 MHz?
Can the EHT sounding NDP be applicable to both TB sensing measurement instance and non-TB sensing measurement instance when PPDU BW = 320 MHz?

## Slide 3: SR2SI NDP and SI2SR NDP transmissions in 802.11bf
TB sensing measurement instance
Non-TB sensing measurement instance
As defined in 11.21.18.7 Non-TB sensing measurement instance [2], a non-TB sensing measurement instance is applied to the case that an AP is the sensing responder, and a non-AP STA is the sensing initiator. Both SI2SR NDP and SR2SI NDP are required to be transmitted in a non-TB sensing measurement instance.
As defined in 11.21.18.6 TB sensing measurement instance [2], a TB sensing measurement instance is applied in the case that an AP is the sensing initiator, and one or more non-AP STAs are the sensing responders. Therefore, in the TF sounding phase of a TB sensing measurement instance, when the Sensing Sounding Trigger frame indicating only one responder is received, that responder transmits an SR2SI NDP; when the Sensing Sounding Trigger frame is transmitted to more than one responder, multiple responders receiving the Sensing Sounding Trigger frame transmit SR2SI NDPs.
- In the NDPA sounding phase, the initiator (i.e., AP) transmits the SI2SR NDP to one or more responder(s) (i.e., non-AP STAs).

## Slide 4: Consideration of HE (TB) Ranging NDP for 802.11bf sensing
Comparison of 802.11bf sensing [2] and 802.11az ranging in sub-7 GHz [3]
Propose to apply
- the HE TB Ranging NDP to the TF sounding phase in a TB sensing measurement instance when PPDU BW ≤ 160 MHz;
- the HE Ranging NDP to the NDPA sounding phase in a TB sensing measurement instance when PPDU BW ≤ 160 MHz;
- the HE Ranging NDP to the non-TB sensing measurement instance when PPDU BW ≤ 160 MHz.
- A sensing initiator and a sensing responder play a similar role as a ranging initiator and a ranging responder, respectively;
- The TF sounding phase and NDPA sounding phase in a TB sensing measurement instance specified in [11.21.18.6, 2] are similar to the TF sounding and the ranging NDPA sounding in measurement sounding phase of TB ranging [11.21.6.4.3.3, 3], respectively.
- The non-TB sensing measurement instance specified in [11.21.18.7, 2] is similar to the sounding phase in non-TB ranging measurement [11.21.6.4.4, 3].

## Slide 5: EHT sounding NDP transmission in 802.11be
Transmission of EHT sounding NDP by an SU beamformer
Transmission of EHT sounding NDP by an MU beamformer
As specified in 35.7.2 EHT sounding protocol [4], the SU Beamformer can be either an EHT AP or an EHT non-AP STA. So is the SU Beamformee. Therefore, the EHT sounding NDP can be transmitted in either DL or UL by an SU Beamformer.
As specified in 35.7.2 EHT sounding protocol [4], “An MU beamformer is an EHT AP” and “An EHT AP does not support operation as an MU beamformee”. Therefore, a non-AP EHT STA does not support operation as an MU beamformer. The EHT sounding NDP can be transmitted by an EHT MU beamformer (i.e., EHT AP) in the DL, but cannot be transmitted from EHT non-AP STAs to an EHT AP for UL MU-MIMO.

## Slide 6: Consideration of EHT sounding NDP for 802.11bf TB sensing
NDPA sounding phase in TB sensing measurement instance
the EHT sounding NDP (including specified preamble puncturing patterns), when PPDU BW = 320 MHz, to a TB sensing measurement instance only in the NDPA sounding phase as the SI2SR NDP .
Propose to apply
TF sounding phase in TB sensing measurement instance
Discussion on 22/1819r0 in TGbf
Implementation concerns have been raised during the discussion for the TF sounding case in TB sensing measurement instance when applying the EHT sounding NDP.

## Slide 7: Consideration of EHT sounding NDP for 802.11bf non-TB sensing
Propose not to apply
the EHT sounding NDP in the non-TB sensing measurement instance.
Non-TB sensing measurement instance [2]
Discussion on 22/1819r0 in TGbf
Implementation concerns have been raised during the discussion for the non-TB sensing measurement instance when applying the EHT sounding NDP.

## Slide 8: SP1
Do you agree to reflect the following text in the Sensing NDP PDT?
  To apply the HE TB Ranging NDP to the TF sounding phase in a TB sensing measurement instance when PPDU BW ≤ 160 MHz;
  To apply the HE Ranging NDP to the NDPA sounding phase in a TB sensing measurement instance when PPDU BW ≤ 160 MHz;
  To apply the HE Ranging NDP to the non-TB sensing measurement instance when PPDU BW ≤ 160 MHz.
Yes:
No:
Abstain:

## Slide 9: SP2
Do you agree to reflect the following text in the Sensing NDP PDT?
To apply the EHT sounding NDP (including specified preamble puncturing patterns), when PPDU BW = 320 MHz, only to a TB sensing measurement instance in the NDPA sounding phase as the SI2SR NDP.
Yes:
No:
Abstain:

## Slide 10: References
[1] IEEE 802.11-20/1874r78, TGbf motion list
[2] IEEE P802.11bf/D0.3
[3] IEEE P802.11az/D7.0
[4] IEEE P802.11be/D2.2