## Slide 1: TG me Discussion on CCK deprecation
Date: 2022-11
Authors:
Name | Company | Address | Phone | email
Graham Smith | SRT Group | Sunrise , FL |  | gsmith@srtrl.com

## Slide 2: Introduction
Clause 16 HR/DSSS (11b)
  5.5 and 11Mbs using CCK
  introduced in 1999
  entered Standard 2001
Clause 18 ER PHY (ERP - 11g)
  Entered Standard in 2003
  6, 12, 18, 24, 36 and 54 Mbps
Both are backward compatible with Clause 15 DSSS

## Slide 3: Compare
RX sensitivities*
OFDM 802.11g mode at 12 Mbps typically -90 dBm
OFDM 802.11g mode at 6 Mbps typically -93 dBm
CCK 802.11b mode at 11 Mbps typically -89 dBm
CCK 802.11b mode at 5.5 Mbps typically -90 dBm
TX Power* (North America and Australia):
802.11b mode for 1 - 11 Mbps typically 23 dBm
802.11g mode for 6 - 54 Mbps typically 20 dBm
  Note: 6 and 12 Mbps could be higher as EVM requirement is much less than 54 Mbps
Basically – similar RF performance
  Not looking at interference or multipath where OFDM is possibly better.
    “CCK is prone to narrowband interference”
* https://kb.netgear.com/1006/RF-transmit-power-and-receive-sensitivity-data-for-the-FWG114Pv2

## Slide 4: Rate adaptation
Rate Fall back (1) 24, 12, 6, 2, 1 Mbps
Rate Fall back (2) 24, 11, 5.5, 2, 1 Mbps
Why use (2)?
  Interested to know what is common practice
Begs the questions
  “When is 5.5 or 11 Mbps used?”
  “Would we miss them?”
  “Do we need a CCK modem in addition to the DSSS and OFDM?”

## Slide 5: What about low-rate devices?
11b only devices?
Need DSSS and CCK?
What if DSSS and ERP (i.e., OFDM 6, 12 only)?
  6 and 12 Mbps OFDM can use same high TX power as 1, 2Mbps
  OFDM has good interference and multipath protection

## Slide 6: Low-Rate devices (11b only)
What about ERP protection?
“Use Protection” bit in ERP IE
ERP-DSSS (does not need protection)
  Begins with an 802.11b compatible header
ERP-OFDM protection
  Precedes packets with CTS-to-Self (at 2 Mbps).
BUT
If DSSS/OFDM device, then the OFDM preamble is understood.
  No real need for ERP protection
  If 11b ONLY devices still around (in the short term), then could still set the “Use Protection” bit in ERP IE

## Slide 7: So, what if we set Clause 16 to “Deprecated”?
Without doubt, “standard” chip sets better off as no need to include CCK modem.
  Even with no CCK modem, a “legacy” device transmitting CCK is understood and protected because of the DSSS preamble.
Gives time for any 11b-only IoT chip vendors to replace CCK modem with the OFDM modem.
  BTW, this improves performances as no need for “Set Protection”, or ERP-DSSS or CTS-to-self.

## Slide 8: Possible Actions
Poll if there is interest in pursuing this.
  Do you agree with the presented points?
  Do you agree worthwhile pursuing?
Issue a notice? See what comes back.
Enquire how many 11b only devices out there without OFDM – how old/new?
  On understanding that they are still protected from devices with no CCK modem.
Ask for comments from general membership and liaisons (Wi-Fi Alliance, WBA)