## Slide 1: Considerations on PHY Designs for mmWave Band
Date: 2022-11-13
Authors:
Name | Affiliation | Address | Phone | Email
Eunsung Park | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | esung.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
Several contributions considered mmWave band operation as one of the potential features for UHR [1-6]
  Various benefits and target objectives were presented
  Reusing existing PHY designs was dealt with as a way to enable mmWave band operation in some of the contributions
There are still some issues to be discussed even when reusing existing PHY designs
  In [6], several aspects such as hardware challenges, CFO and phase noise were discussed
In this contribution, we present our considerations on several PHY designs such as numerology, SU / MU MIMO, PPDU format and MCS for mmWave band operation
  As to the numerology, we consider three aspects as follows
    Bandwidth, guard interval and subcarrier spacing

## Slide 3: Numerology
We have 1x and 4x numerologies which are based on 11ac and 11be, respectively
  One of them can be reused to determine tone plans and symbol structures in a mmWave band for a simple implementation
There are several differences between 1x and 4x numerologies
  We deal with these three aspects to discuss which numerology is proper
 | 1x numerology (11ac) | 4x numerology (11be)
Bandwidth (FFT size) | M: 20 MHz, 40 MHz, 80 MHz (64, 128, 256) O: 160 MHz (512) | M: 20 MHz, 40MHz, 80 MHz (256, 512, 1024) O: 160 MHz, 320 MHz (2048, 4096) Note: 160 MHz is mandatory for AP
Guard Interval | M: 0.8 us O: 0.4 us | M: 0.8 us, 1.6 us, 3.2 us
Subcarrier spacing | 312.5 KHz | 78.125 KHz
M: mandatory
O: optional

## Slide 4: Numerology: Bandwidth (1/2)
Background
  Upclocked bandwidths can be used to offer better throughput
    In [4], 160 to 1280 MHz bandwidths were considered and it seems that 8 times upclocking is applied to the conventional bandwidths
    In 5G NR, up to 400 MHz with 60 / 120 / 240 KHz subcarrier spacing is supported for FR2 (mmWave band) while up to 100 MHz with 15 / 30 / 60 KHz subcarrier spacing is supported for FR1 (sub-6 GHz)
  In 11ay, bandwidths from 2.16 to 8.64 GHz with FFT sizes from 512 to 2048 are defined
Pros and Cons
  1x numerology may have less hardware complexity because of the smaller FFT size
  4x numerology can support much wider bandwidth assuming the same upclocking because it supports up to 320 MHz

## Slide 5: Numerology: Bandwidth (2/2)
Feasibility
  Upclocking may further increase the complexity since much faster hardware processing is needed due to a high sampling rate
  Considering the bandwidths and FFT size defined in 11ay, reusing both 1x and 4x numerologies with 8 times upclocking may be feasible from the hardware perspective
    1x numerology with 8 times upclocking leads to bandwidths from 160 to 1280 MHz with FFT sizes from 64 to 512
    4x numerology with 8 times upclocking leads to bandwidths from 160 to 2560 MHz with FFT sizes from 256 to 4096
    It seems that more than 8 times upclocking is possible
Further required work
  Implementation aspects and challenges need to be investigated to determine proper upclocked bandwidths

## Slide 6: Numerology: Guard Interval (1/2)
Background
  GI mitigates inter-symbol interference (ISI) caused by delay spread at the expense of overhead
    In 11ay, 36.36 ns guard interval (GI) is defined
    Assuming 8 times upclocking, 1x and 4x numerologies have 0.1 / 0.05 us GI and 0.1 / 0.2 / 0.4 us GI, respectively
Pros and Cons
  1x numerology has an overhead reduction option of 0.05 us GI
    Note that this does not mean 1x numerology is better in terms of the overhead, and, basically, 4x numerology has less overhead because of a longer symbol period
    0.05 us GI is the most similar value to the GI defined in 11ay
  4x numerology is more robust against ISI since it has various wide GI options

## Slide 7: Numerology: Guard Interval (2/2)
Feasibility
  Many research papers [7-10] showed that in 60 GHz, most of the delay spreads are measured within 0.1 us even in NLoS environments no matter if it is indoor or outdoor
    0.1 us GI may be enough, i.e., 1x numerology with 8 times upclocking may be feasible
    In LoS, delay spreads are measured around 10 ns, and thus, 0.05 us may be applicable
Further required work
  Delay spread impact should be investigated under various GIs
    Based on the investigation, possible GIs can be determined and wider or shorter GI can be further introduced to effectively mitigate ISI or to further reduce overhead
    Additional GIs cause a slight modification of existing PHY designs, and thus, impacts on implementation also need to be checked

## Slide 8: Numerology: Subcarrier Spacing (1/2)
Background
  There are several impairment factors which cause inter-carrier interference (ICI)
    The wider subcarrier spacing, the more robust against ICI
    In 11ay, 5.156 MHz subcarrier spacing is defined
  In a mmWave band, phase noise has a more harmful effect than that in a sub-7 GHz band due to frequency multipliers of local oscillators and phase noise floor in a wide bandwidth [11]
Pros and Cons
  1x numerology which has a wider subcarrier spacing may be better in terms of ICI
  4x numerology which has a narrower subcarrier spacing resulting in a longer symbol period has less GI overhead and better throughput

## Slide 9: Numerology: Subcarrier Spacing (2/2)
Feasibility
  Considering the subcarrier spacing defined in 11ay, around 5 MHz subcarrier spacing may be feasible
    16 and 64 times upclocked bandwidths are needed for 1x and 4x numerologies, respectively, which yield 5 MHz subcarrier spacing
    4x numerology may need too much increase in hardware complexity
Further required work
  Overall impacts of impairment factors causing ICI should be identified under various subcarrier spacing values
    Based on the investigation, possible subcarrier spacing values can be determined which are directly related to upclocking

## Slide 10: Numerology: Summary
Summary for numerology
  Overall, 1x numerology has relatively low complexity whereas 4x numerology has better throughput
  Many factors such as complexity, impairments, performance, and so on are involved in determining reasonable numerology
    Further investigation is required for detailed designs
 | 1x numerology (11ac) | 4x numerology (11be) | Required work
Bandwidth (FFT size) | Relatively less complex | Higher throughput | Hardware complexity
Guard Interval | Maybe feasible in terms of ISI (assuming 8 times upclocking) | More robust against ISI | Delay spread impact
Subcarrier spacing | More robust against ICI | Less GI overhead and better throughput | Phase noise impact

## Slide 11: SU / MU MIMO
Background
  In 11ay, SU MIMO and DL MU MIMO are optionally supported up to 8 spatial streams (SS) by using array antennas with polarization based on a beamforming training procedure and only SU transmission with 1 SS is mandatory
Feasibility
  Basically, SU transmission with 1 SS can be supported based on a simple sector sweep method
  Although we can also consider SU MIMO and DL MU MIMO by reusing the beamforming training procedure defined in 11ay or introducing a new design, to minimize the implementation burden and complexity, it would be better to adopt these schemes later
Further required work
  A simple sector sweep method needs to be designed for SU transmission with 1 SS
  We can further check on whether the MIMO and MU transmission schemes are needed in UHR considering the complexity, objectives and use cases
  Additionally, feasibility of UL MU MIMO and DL/UL MU OFDMA can be also investigated for future expansion if needed

## Slide 12: PPDU Format (1/2)
Background
  When it comes to the design of PPDU format, coexistence and backward compatibility is one of the important factors
    UHR PPDU for sub-7 GHz also needs to begin with the legacy preamble
  Whereas these factors may be less important in a mmWave band because of a low interference nature with directional antennas and large signal attenuation
Feasibility
  Although there are 11ad / 11ay STAs currently in 60 GHz, we might not have to care about them too much thanks to the mmWave band properties mentioned above
  Hence, UHR PPDU in a mmWave band can start with UHR STF followed by UHR LTF, UHR SIG and Data field
    Each field can reuse existing field designs especially for STF and LTF
    This format can diminish the overhead but additional implementation is required for a different PPDU format from the sub-7 GHz one
    In addition, training fields can be added at the end of the PPDU for beam refinement similar to 11ay

## Slide 13: PPDU Format (2/2)
Further required work
  Reasonable PPDU formats should be discussed
    To minimize the implementation burden and complexity, we can focus only on SU transmission and we can additionally consider the MU transmission later if needed
  An additional PPDU which is used only for the sector sweep and beam refinement can be considered for overhead reduction
    It may be different from SU PPDU
    Efficient training field designs may be necessary and it can reuse existing STF / LTF designs as a simple approach

## Slide 14: MCS
Background
  Since mmWave band operation is vulnerable to the phase noise which degrades EVM, it may be difficult to apply high MCSs without an additional increase in hardware cost / complexity
    Although 11ay supports up to 64 QAM, only BPSK and QPSK are mandatory for the EDMG SC mode
Feasibility
  Similar to 11ay, only some low MCSs can be chosen as (conditional*) mandatory MCSs even though MCSs up to 64 QAM and 256 QAM are mandatory in 11ac and 11be, respectively
    Although this may degrade the throughput, we have several alternatives to compensate it, e.g., wider bandwidths and multi-link operation
Further required work
  Phase noise and EVM impact should be investigated according to various MCSs
    Based on the investigation, possible MCSs can be determined
  We can further check on whether high MCSs are needed in UHR considering the complexity, objectives and use cases
* If we decide to adopt mmWave band operation, we also need to determine whether it is mandatory or optional

## Slide 15: Conclusion
We have provided our considerations on several PHY designs such as numerology, SU / MU MIMO, PPDU format and MCS for mmWave band operation
  We can reuse existing PHY designs in sub-7 GHz as much as possible for simplicity, but there are still several issues
  To determine details of each design, many factors such as impairments, performance, complexity, etc., need to be further discussed
  To minimize the implementation burden and complexity, it would be better to focus on simple features
    Some other complex features can be considered in the next UHR

## Slide 16: References
[1] 11-22-0046-01-0wng-next-generation-after-802-11be
[2] 11-22-0729-01-0wng-next-generation-after-802-11be-follow-up
[3] 11-22-1083-01-0wng-next-generation-sg-formation
[4] 11-22-1595-01-0uhr-some-questions-to-answer-in-the-sg
[5] 11-22-1580-01-0uhr-aperspectiveonproposeduhrfeaturesforenterpriseusecases
[6] 11-22-1395-00-0uhr-thoughts-on-high-frequency-band
[7] H. Xu, V. Kukshya, and T. S. Rappaport, “Spatial and Temporal Characteristics of 60-GHz Indoor Channels”, IEEE J. Sel. Areas Commun., vol. 20, no. 3, pp. 620–630, Apr. 2002.
of 60-GHz indoor channels,”
[8] S. Salous, S. M. Feeney, X. Raimundo, and A. A. Cheema, “Wideband MIMO Channel Sounder for Radio Measurements in the 60 GHz Band”, IEEE Tran. Wireless Commun., vol. 15, no. 4, pp. 2825-2832, Apr. 2016
[9] X. Wu, C.-X. Wang, J. Sun, J. Huang, R. Feng, Y. Yang, and X. Ge, “60-GHz Millimeter-Wave Channel Measurements and Modeling for Indoor Office Environments”, IEEE Trans. Antennas Propag., vol. 65, no. 4, pp. 1912- 1924, Apr. 2017
[10] V. Raghavan, A. Partyka, L. Akhoondzadehasl, A. Tassoudji, O. Koymen, and J. Sanelli, “Millimeter Wave Channel Measurements and Implications for PHY Layer Design”, IEEE Trans. Antennas Propag., vol. 65, no. 12, pp. 6521-6533, Dec. 2017
[11] 11-15-0866-04-00ay-11ay-evaluation-methodology