## Slide 1: Encrypted Information Element for Obfuscated beacon
Date: 2022-11-14
Authors:

## Slide 2: Abstract
Current contribution describes an information element allowing an encryption of a set of “legacy” IEs for beacon obfuscation.

## Slide 3: Overview
11bi requirement document [1] includes a requirement (Req 50) on the BPE AP that shall provide a Beacon frame with a subset of encrypted or obfuscated, TBD, fields.
In addition, same requirement indicates that this BPE Beacon frame shall contain fields and have a structure that allows associated BPE clients to minimize the power consumption for BPE Beacon frame reception.
Previous contribution [2] provides a new format for the BPE Beacon frame, but without a structure that allows associated BPE clients to minimize the power consumption for BPE Beacon frame reception
Current contribution proposes a new information element allowing the encryption of a set of one or more IEs into an encrypted portion and that includes a mechanism to reduce processing at the receiving station.

## Slide 4: 11bi requirement
50 | 11bi shall define a BPE Beacon frame that includes a secure mechanism to identify a BPE AP and/or a network that includes that BPE AP. 11bi shall extend the BPE Beacon frame with a subset of encrypted or obfuscated, TBD, fields and define a mechanism for the BPE AP to transmit the new type of Beacon frame. The BPE Beacon frame shall contain fields and have a structure that allows associated BPE clients to minimise the power consumption for BPE Beacon frame reception. | I6 | Approved | Proposed 22/1306r2 (14 Sept 2022) Straw poll – unanimous consent 14 Sept 2022 Approved (Motion #20, 14 Sept 2022)

## Slide 5: Encrypted Information Element Container 1/2
Element ID
Length
Element ID Extension
Encrypt. scheme
content
Padding
Hash
For example : Two first octets of the result of the SHA-256 algorithm applied to the content of the encrypted part
Encrypted part
(encryption key, for instance GTK)
Variable padding (either in length or in content or both)
New IE : “Container IE” because it comprises, in its information part, others IEs.
Container IEs are then embedded in the body or payload of the management frame.
Beacon frame body
Container IE

## Slide 6: Encrypted Information Element Container 2/2
Element ID
Length
Element ID Extension
Encrypt. scheme
content
Padding
Hash
Encrypted part
Allows a receiving station to skip the Container IE when a previous management frame already provided it.
This reduces complexity at the receiving station or stations by easily determining whether the decoding of the encrypted part is useful or not.
The Container IE allows the station to obfuscate the contained elementary IEs, hence to reduce risks that fingerprinting correlates the management frame with another management frame transmitted by the same station
Beacon frame body
This allows the receiving or addressed station or stations to correctly decode the content of the Container IE. Furthermore, different encryption schemes may be used for different Container IEs.
A variable padding (either in length or in content or both) substantially impacts the fingerprint of the corresponding Container IE. A change over time may for example be made upon RCM-based changing the MAC address of the station or any other privacy parameter

## Slide 7: Benefits
Contributes to make fingerprinting more difficult
Helps to reduce processing at the receiving station
provides the AP with more options to manage the various IEs to be embedded in a frame.

## Slide 8
Straw Poll #1
Do you support the specification of an encrypted container information element as described in slide 5?
Yes
No
Abstain

## Slide 9: References
[1] IEEE 802.11-21/1848r16 : Requirements Document
[2] IEEE 802.11-22/1306r3 : BPE Beaconing And Discovery Requirements