## Slide 1: mmWave operation in UHR
Date: 2022-11-15
Authors:
Name | Affiliation | Address | Phone | Email
Laurent Cariou | Intel | 2111 NE 25th Ave, Hillsboro OR 97124, USA | +1-503-712-5560 | laurent.cariou@intel.com
Robert Stacey |  |  |  | robert.stacey@intel.com
Carlos Cordeiro |  |  |  | carlos.cordeiro@intel.com
November 2022

## Slide 2: Summary
There have been several contributions to explain the importance to include mmWave operation in the scope of UHR (See 22/1093r1 22/729r1 22/030r1 22/046r1, ...)
A SP was ran on Oct 24th: Do you agree that mmWave operation is a promising feature for UHR? Result: Y52/N18/A17
We also presented in doc 22/1595r01 the assumptions that we have for defining mmWave operation and the limited scope that we envision for UHR
In spite of it, we have received requests to clarify in further details this limited scope (what would need to be defined for mmWave operation)
  Many are interested in mmWave operation, but want assurances that the scope would indeed be limited
  This short contribution is addressing this request

## Slide 3: Principle for inclusion of mmWave in UHR’s scope
The key principle is to limit the scope of mmWave in UHT to the minimum necessary to enable a lower band PHY to operate in mmWave (proposal in next slide)
This limited scope is critical to not only ensure minimal standard changes, but also minimal implementation complexity and larger market adoption
Leave optimizations and enhanced features for generations after UHR
  Pave the way for long term evolution of 802.11 and its market adoption
  Potential for enhanced features for multiple generations
In other words: just focus on the least complexity solution in UHR to enable operation in the band
  So much benefits for UHR KPIs by just doing that
November 2022

## Slide 4: What is the minimum necessary feature set to enable mmWave in UHR?
Only an SU PPDU format
  Reusing as much as possible lower band PPDU design
A limited set of bandwidth (between 160 and 1280MHz for instance)
  Reusing lower band channel bonding. For example:
Build on the MLO framework which can easily be extended to support other bands
A simple beamforming training solution
  Basic sector sweep, with help/support from lower band (using MLO framework), and reusing NDP frames
Basic MAC rules for operation on mmWave band
  Simplified assuming no mmWave-only devices and networks
  Simplified using MLO framework
No other features needed
 | 20 | 40 | 80 | 160
NDFT | 64 | 128 | 256 | 512
ΔF | 312.5KHz |  |  | 
TDFT | 3.2μs |  |  | 
Ts | 50ns | 25ns | 12.5ns | 6.25ns
TGI | TDFT/4 = 0.8μs |  |  | 
NGI | 16 | 32 | 64 | 128
11ac PHY numerology
 | 160 | 320 | 640 | 1280
NDFT | 64 | 128 | 256 | 512
ΔF | 2.5MHz |  |  | 
TDFT | 0.4μs |  |  | 
Ts | 6.25ns | 3.12ns | 1.56ns | 0.78ns
TGI | TDFT/4 = 100ns |  |  | 
NGI | 16 | 32 | 64 | 128
mmWave PHY numerology
x8

## Slide 5: Other clarifications
The proposal is not to use 11ad/ay
  Define new waveform reusing lower band PHY …
New channelization based on min BW of around 160 MHz
Not considering backward compatibility with 11ad/ay, but basic coexistence (likely energy detection-based)
mmWave operation defined as an optional feature in UHR
November 2022

## Slide 6: Conclusions
We see strong potential in including mmWave operation in UHR
  mmWave provides a path to bring meaningful improvements and longevity to 802.11
Thanks to a mmWave PHY design reusing lower band design, we are simplifying the standard and implementation work and bringing complexity to levels that we believe are realistic for high-end Wi-Fi devices (e.g., dual radio devices)
Thanks to MLO framework,
  We can further reduce standard and implementation work
  We provide important tools to help with power consumption and blockage issue in mmWave band
We want to get agreement early on regarding the principle for the scope of mmWave inclusion in UHR, i.e., to define only what is necessary to enable basic operation (through limitations in PAR)
November 2022