## Slide 1: UHR Rate-vs-Range Enhancement with Relay
Date: 2022-11-13
Authors:

## Slide 2: Introduction
Ultra High Reliability SG (UHR SG) was approved in July meeting with objectives [1] to
  improve reliability
  increase throughput at different SNR levels
  reduce latencies, etc.
Some potential technologies are listed in [1~8].
  Multi-AP coordination, managed P2P, link adaptation, etc.
In this presentation, we investigate relay communications to enhance Rate-vs-Range (RvR) performance for UHR.

## Slide 3: Content
Relay communications and use cases
UHR relay design objectives
Goodput analysis

## Slide 4
Relay Communications
Higher propagation loss  lower rates:
Boost throughput at range or extend range  need relay
  Relays retransmits/amplifies the source packet, multi-hop link
  Prominent per-hop SNR gain
    ~10dB better SNR with relay in the middle (pathloss exponent 3.5 for indoor)
    Extra SNR gain if relay avoids obstacles, e.g. 15~20dB loss per-wall
  Increase end-to-end throughput or extend range
Design challenges:
  End-to-end channel reservation, latency/jitter: multiple channel accesses
  Relay processing delay and overhead
Direct link
Relay link
Source STA
Relay STA
Dest. STA
PPDU-1
PPDU-2
B
C

## Slide 5: Existing “Relay” Solutions
WiFi extender (repeater/booster)
  Leverage the wireless distribution system (WDS) protocol
    Implements both client and (soft-) AP functions
  For the relay solution with co-channel wireless connection to main AP
    User experience suffers from end-to-end QoS (latency, jitter, throughput) due to hop-by-hop channel access and transmission control (BA/Security/etc.)
    Internal relay forwarding processing can be long
  Advanced solutions with wired backhaul or dual-radio hardware is expensive
WiFi mesh router (e.g. EasyMesh program)
  Similar client + AP design, but with better AP networking control
    Support coverage expansion for large area with full function APs
  Co-channel wireless backhaul also has end-to-end QoS challenges due to nature of independent hop-by-hop control
  Wired backhaul or dual-radio design provides better QoS with higher cost
Standards: 802.11ah/ad relay operation
  Logical relay AP, relay STA and relay function defined
  Hop-by-hop channel access and BA/ACK agreement
  TXOP sharing with incomplete support

## Slide 6: Relay Use Cases
Examples:
  Home network dead/weak-spots: garage/attic/den/crawlspace, etc.
    Smart home: HD cameras in front-door/backdoor, drone cameras, etc.
  Automotive: trailer/RV rear/side cameras/sensors to dashboard
Boost effective throughput or extend connection for specific device(s) at medium to low SNR
  Complimentary to the AP network coverage
Left: [9]
Right: [10]
x
x

## Slide 7: Objectives of UHR Relay
Enhanced end-to-end QoS
  Boost throughput with latency similar or better than that of direct link
  Enhance TXOP sharing control at transmitter
  Simplify end-to-end transmission control/management
    Limit relay processing to lower MAC and PHY
  One relay is practical, may not general N-hop relay.
Low cost
  non-AP STA level of complexity with relay protocol add-on
  No AP function needed at the relay to manage the end STAs
    Limited number of end STAs to be supported
Easy setup: “plug and play”
  Simple protocol for fast relay discovery, connection and management
  Dedicated relay device or regular non-AP STA with relay function

## Slide 8: Relay Topology
  Case 1: Throughput/Reliability enhancement
    Ex: APrSTASTA1, STA1 is within the one-hop communication range, and rSTA relaying to boost end-to-end throughput
  Case 2: Range extension
    Ex1: APrSTASTA2, STA2 able to receive beacon and DL traffic, it shows “connected” on device, but not able deliver UL traffic. Relay can resolve DL/UL power asymmetry to extend coverage to STA2 with bi-directional traffic.
    Ex2: AP rSTA STA3, STA3 is out of AP’s one-hop range, and relay can help extend AP’s coverage.
rSTA
STA1
STA2
One-hop beacon coverage
AP
STA3

## Slide 9: Relay Link Analysis
End-to-end goodput comparison: Relay link vs Direct link
  Goodput = 1/(1/Goodputhop1+1/ Goodputhop2)
    Goodputhop = PhyRatehop*(1-PERhop)
  Effective rate without MAC overhead, good approximation for long packet
RvR analysis: rate vs pathloss
  SNR = Tx power – PL – Noise floor
    Fixed 20dBm Tx power at both source and relay, Noise Figure=5dB
    PL: 11n pathloss model with pathloss exponent of 3.5
  In some analysis, 10dB obstacles/blockage in direct link is assumed
  PER: 80MHz, 1SS, EHT SU PPDU, 4xLTF, MCS0~11
Direct link
Relay link
Source STA
Relay STA
Dest. STA
PPDU-1
PPDU-2
B

## Slide 10: Goodput: Relay link vs Direct Link
  Prominent goodput benefits in the region < 150Mbps (~MCS4 for direct link)
    Relay link: 20% to 200% end-to-end throughput gain
  For relay placed in the middle, 10dB range extension benefits below MCS0
  In real deployment, more benefits can be achieved if relay can avoid obstacles
Range Extension
Goodput Improvement

## Slide 11: Goodput: Impact of Relay Placement
  For different relay deployment, with optimal rate selection, goodput benefits are similar, but range extension is limited for non-symmetric case
S
D
R
R
R
0.5 0.6 0.7
S
D
R
R
R
0.5 0.6 0.7

## Slide 12: Summary
RvR enhancement is one of the objectives for UHR generation
Relay can boost throughput and extend range at medium to low SNR regions
  Complimentary to any AP network
  Support specific applications: e.g. IoT, Automotive, etc.
Suggest for UHR to define relay protocols to provide better end-to-end QoS with simple relay processing

## Slide 13: References
[1] 11-22/0708r3, beyond be-next step
[2] 11-22/32, Next Gen After 11be
[3] 11-22/46, Next generation after 802.11be
[4] 11-22/30, Look ahead to next generation
[5] 11-22/418, Considerations of Next Generation Beyond 11be
[6] 11-22/932, Thoughts on Beyond 802.11be
[7] 11-22/685, Discussion on next generation Wi-Fi
[7] 11-22/694, Thoughts on Next Gen WLAN
[8] 11-22/965, View on Beyond BE
[9] https://www.hcc.net/2020/02/the-best-location-for-your-router-for-actually-good-wi-fi/
[10] http://www.4ucam.com/Wired-Dual-Cam-7-inch-Backup-5th-wheel-RV-Truck-Trailer-Rear-View-IR-Night-Vision-CCD-license-plate-camera.html
[11] https://www.wi-fi.org/discover-wi-fi/wi-fi-easymesh

## Slide 14: Appendix

## Slide 15: Throughput: Impact of Payload
  Throughput = Npld/Tend-2-end*(1-PERhop1)*(1-PERhop2)
    Tend-2-end includes airtime of channel contention, control frames and data frames
  For larger payload size, throughput benefits are very similar to goodput.
  For smaller payload size, relay shows throughput benefits in relatively lower SNR region; but the range extension region is the same.

## Slide 16: Relay vs Multi-AP
MAP: premium solution for coverage
  Enhancement to Mesh AP/Enterprise AP for large coverage area
  Network coverage expansion with advanced AP coordination functions
  Support large number of devices
  Support high throughput applications (>100Mbps)
Relay: complimentary to any AP network coverage
  Boost throughput or extend connection to specific devices at locations with medium to low SNR.
  Support applications with medium to low throughput requirements
  Enhancement/simplification to existing WiFi wireless extender/booster