## Slide 1: Seamless Roaming for UHR
Date: 2022-11-02
Authors:

## Slide 2: Problem Statement
UHR is aiming for providing better support for applications that require low-latency with high reliability. One area to enhance is mobility support
Currently, when the STA roams between multiple APs, the STA needs to re-associate with the target AP and perform 4-way handshake, typically taking 10s of ms
The network needs to switch the data path in a break-before-make manner, which creates data interruption and extra delay during handover

## Slide 3: Current Roaming
When the link with AP1 deteriorates and the signal with AP2 grows stronger, the STA roams to AP2 (another case is network-directed roaming using the BSS Transition Mgmt to trigger roaming)
The STA performs:
  Reassociation
  Security
  BA sessions re-establishment, etc.
The network performs:
  Switching the data path between the gateway and the AP from AP1 to AP2
The above steps create a delay of 10s of ms
AP
1
AP
2
STA
Backhaul
STA

## Slide 4: Considerations of Solution
Should be simple
  E.g., Rely on existing frameworks as much as possible
Should be flexible
  To cover different use cases such as home, enterprise, warehouse, etc.
Should be scalable
  To support mobility within a network consisting of large number of APs

## Slide 5: An Example Solution
The 11be MLO framework already allows a non-AP MLD to switch links with minimal signaling overhead and delay
  E.g., by making the non-collocated APs as affiliated APs of a single AP MLD (see next slide)
This approach would enable seamless transition to another AP with no (or minimal) communication interruption by allowing make-before-break data path switch

## Slide 6: Example Topology
Reuse MLO architecture, allowing non-collocated APs to be affiliated with the AP MLD
Affiliated APs
(non-collocated)
AP MLD (logical entity, physically could be co-located with any of the AP below for each client)
AP1
AP2
AP3
APn
STAx
STAy
Router
Data path
Note: SN/PN assignment, encryption are still performed at each AP inline with the existing MLO architecture

## Slide 7: Transition Steps
Before transition
  STA is active with AP1
  Data path is routed to AP1
  AP1 hosts MLD context for the client
During transition
  STA is active with both AP1 and AP2
  AP1 duplicates/forwards packets to AP2 (optional)
  Both AP1 & AP2 sends packets to client independently
After transition
  STA is no longer active with AP1
  Data path re-routed to AP2
  AP2 keeps the MLD context for the client
AP MLD (logical entity)
AP1
AP2
STAx
Affiliated APs
(non-collocated)
Router
Data path
1
2
2
STAx
3
MLD Association (auth, assoc., BA context etc.) is maintained during transition from AP1 to AP2

## Slide 8: Conclusion
We introduced the problems of roaming and presented a simple, flexible, and scalable example solution