## Slide 1: Seamless Roaming for UHR
Date: 2023-02-26
Authors:

## Slide 2: Problem Statement
UHR is aiming for providing better support for applications that require low-latency with high reliability. One area to enhance is mobility support
Currently, when the STA roams between multiple APs, the STA needs to re-associate with the target AP and perform 4-way handshake, typically taking 10s of ms
The network needs to switch the data path in a break-before-make manner, which creates data interruption and extra delay during handover

## Slide 3: Current Roaming
When the link with AP1 deteriorates and the signal with AP2 grows stronger, the STA roams to AP2 (another case is network-directed roaming using the BSS Transition Mgmt to trigger roaming)
The STA performs:
  Reassociation
  Security
  BA sessions re-establishment, etc.
The network performs:
  Switching the data path between the gateway and the AP from AP1 to AP2
The above steps create a delay of 10s of ms
AP
1
AP
2
STA
Backhaul
STA

## Slide 4: Considerations of Solution
Should be simple
  E.g., Rely on existing frameworks as much as possible
Should be flexible
  To cover different use cases such as home, enterprise, warehouse, etc.
Should be scalable
  To support mobility within a network consisting of large number of APs

## Slide 5: An Example Solution
The 11be MLO framework already allows a non-AP MLD to switch links with minimal signaling overhead and delay
  E.g., by making the non-collocated APs as affiliated APs of a single AP MLD (see next slide)
This approach would enable seamless transition to another AP with no (or minimal) communication interruption by allowing make-before-break data path switch

## Slide 6: Example Topology
Reuse MLO architecture, allowing non-collocated APs to be affiliated with the AP MLD
Affiliated APs
(non-collocated)
AP MLD (logical entity, physically could be co-located with any of the AP below for each client)
AP1
AP2
AP3
APn
STAx
STAy
Router
Data path
Note: SN/PN assignment, encryption are still performed at each AP inline with the existing MLO architecture

## Slide 7: Transition Steps
Before transition
  STA is active with AP1
  Data path is routed to AP1
  AP1 hosts MLD context for the client
During transition
  STA is active with both AP1 and AP2
  AP1 duplicates/forwards packets to AP2 (optional)
  Both AP1 & AP2 sends packets to client independently (optional)
After transition
  STA is no longer active with AP1
  Data path re-routed to AP2
  AP2 keeps the MLD context for the client
AP MLD (logical entity)
AP1
AP2
STAx
Affiliated APs
(non-collocated)
Router
Data path
1
2
2
STAx
3
MLD Association (auth, assoc., BA context etc.) is maintained during transition from AP1 to AP2

## Slide 8: Conclusion
We introduced the problems of roaming and presented a simple, flexible, and scalable example solution

## Slide 9: Follow-up from IEEE meeting in November (Bangkok) Q&A

## Slide 10: Further Discussion on AP MLD
Is the contribution suggesting a different kind of AP MLD (upper and lower MACs)?
  No, all main functionalities of the AP MLD remain the same as defined in 11be
    Maintains the context of association, security, BA sessions, etc
Is the AP MLD moving when the client roams from one AP to another AP?
  No, all the APs that enable seamless roaming experience are expected to be affiliated with the same AP MLD
See the following slides to illustrate the above

## Slide 11: UHR AP MLD
Logically X + Y1 + Y2 = AP MLD
Functionalities can be implemented at different locations – no restrictions (flexible enough to allow different backhaul architectures)
  Extreme case: X can be implemented inside Y1/Y2

## Slide 12: Before Transition (logical perspective) - Link 2 is inactive

## Slide 13: During Transition (logical perspective) - Both links are active
* This example assumes both links are active but we also allow only one link is active

## Slide 14: During Transition (Physical perspective) - Both links are active
* MLD upper MAC sublayer is active on Link 1

## Slide 15: After Transition (logical perspective) - Only Link 2 is active

## Slide 16: Further Discussion on Scaling
How does scaling work with many APs?
  Only a handful of APs (in the vicinity of the STA) need to be aware of the STA’s presence and ready for roaming
  The STA only needs to learn the presence of those APs (but need not have all those APs as setup links)

## Slide 17: Further Discussion on Link ID
Concern raised: how to signal so many links since the current link ID is only 4 bits
Answer:
  In a lot of cases (e.g., home network) the current link ID is enough
  When needed, we may extend the Link ID. One example is to define a Colocated set ID as follows:
    E.g., a floor has 100 11be physical APs, one collocated ID is assigned to each AP (colocated ID = 1, 2, …100)
      Note this is different than the AP MLD ID, which is the id of a specific AP MLD in a physical AP, which can host multiple AP MLDs (e.g., one for Home users and one for Guests)
    Define an “Extended link ID” as the tuple (Colocated set ID, link ID)

## Slide 18: Further Discussion in Duration
How long is the typical transitional period where multiple APs may be active?
  Implementation dependent but ideally short (10s of ms) to enhance reliability with minimal load impact to the network