## Slide 1: Seamless Roaming for UHR
Date: 2023-03-02
Authors:

## Slide 2: Problem Statement
UHR is aiming for providing better support for applications that require low-latency with high reliability. One area to enhance is mobility support
Currently, when the STA roams between multiple APs, the STA needs to re-associate with the target AP and perform 4-way handshake, typically taking 10s of ms
The network needs to switch the data path in a break-before-make manner, which creates data interruption and extra delay during handover

## Slide 3: Current Roaming
When the link with AP1 deteriorates and the signal with AP2 grows stronger, the STA roams to AP2 (another case is network-directed roaming using the BSS Transition Mgmt to trigger roaming)
The STA performs:
  Reassociation
  Security
  BA sessions re-establishment, etc.
The network performs:
  Switching the data path between the gateway and the AP from AP1 to AP2
The above steps create a delay of 10s of ms
AP
1
AP
2
STA
Backhaul
STA

## Slide 4: Considerations of Solution
Should be simple
  E.g., Rely on existing frameworks as much as possible
Should be flexible
  To cover different use cases such as home, enterprise, warehouse, etc.
Should be scalable
  To support mobility within a network consisting of large number of APs

## Slide 5: An Example Solution
The 11be MLO framework already allows a non-AP MLD to switch links with minimal signaling overhead and delay
  E.g., by making the non-collocated APs as affiliated APs of a single AP MLD (see next slide)
This approach would enable seamless transition to another AP with no (or minimal) communication interruption by allowing make-before-break data path switch

## Slide 6: Example Topology
Reuse MLO architecture, allowing non-collocated APs to be affiliated with the AP MLD
Affiliated APs
(non-collocated)
AP MLD (logical entity, physically could be co-located with any of the AP below for each client)
AP1
AP2
AP3
APn
STAx
STAy
Router
Data path
Note: SN/PN assignment, encryption are still performed at each AP inline with the existing MLO architecture

## Slide 7: Transition Steps
Before transition
  STA is active with AP1
  Data path is routed to AP1
  AP1 hosts MLD context for the client
During transition
  STA is active with both AP1 and AP2
  AP1 duplicates/forwards packets to AP2 (optional)
  Both AP1 & AP2 sends packets to client independently (optional)
After transition
  STA is no longer active with AP1
  Data path re-routed to AP2
  AP2 keeps the MLD context for the client
AP MLD (logical entity)
AP1
AP2
STAx
Affiliated APs
(non-collocated)
Router
Data path
1
2
2
STAx
3
MLD Association (auth, assoc., BA context etc.) is maintained during transition from AP1 to AP2

## Slide 8: Conclusion
We introduced the problems of roaming and presented a simple, flexible, and scalable example solution

## Slide 9: Updates since the IEEE meeting in November 2022 (Bangkok) with Q&A follow-up

## Slide 10: Further Discussion on AP MLD
A different kind of AP MLD (upper and lower MACs)?
  The main functionalities of the AP MLD remain the same as defined in 11be
    Maintains the context of association, security, BA sessions, etc
Is the AP MLD moving when the client roams from one AP to another AP?
  No, all the APs that enable seamless roaming experience are expected to be affiliated with the same AP MLD
  Only the context and (physical) MAC-SAP are moving (following the non-AP MLD)

## Slide 11: SMD AP MLD
Logically X + Y1 + Y2 = Single Mobility Domain AP MLD (SMD AP MLD)
Functionalities can be implemented at different locations – no restrictions (flexible enough to allow different backhaul architectures)
  Note: X can be implemented inside Y1/Y2

## Slide 12: Comparison between AP MLD and SMD AP MLD
Functionalities | AP MLD | SMD AP MLD (for UHR clients that support seamless roaming)
Affiliation of APs | All affiliated APs are colocated | Not all affiliated APs are colocated
Authentication, association context, security context, BA sessions, SN/PN maintenance, encryption of unicast frames | Done at the Upper MAC sublayer (i.e., AP MLD) | Same (i.e., at the upper MAC sublayer of SMD AP MLD)
AID, Link ID | Scope is per AP MLD One AID per assoc | Scope is per colocated set. Optionally > 1 AID per assoc (when concurrent non-colocated links is supported by the backhaul)
Group addressed frames delivery | Done at the Lower MAC sublayer | Same (confined within the colocated set)

## Slide 13: Operation of Different Types of Non-AP MLDs
Functionalities | EHT non-AP MLD/UHR non-AP MLD that does not support SMD | UHR non-AP MLD that supports SMD
(Re)Association | Always with an AP MLD | Always with an SMD AP MLD
Roaming between non-colocated APs | Always between AP MLDs. (re)Assoc required. New PTKs, BA sessions, security context re-established | No (re)Assoc. Uses ML Reconfig to add/remove APs. PTK, PN/SN, BA sessions, security context are maintained and not reset (completely transparent to the non-AP MLD)
The non-AP MLD is served by | Only the colocated APs affiliated to the same AP MLD | Colocated APs and (optionally) non-colocated APs affiliated with the SMD AP MLD
AID assignment | One AID per collocated AP set | One AID per collocated AP set. If client is served by more than one collocated set concurrently (optional), then client identified via a tuple - (Colocated set ID, AID)
Link identification | Link ID | (Colocated set ID, link ID) tuple

## Slide 14: Different Types of Non-AP MLDs

## Slide 15: Before Transition (logical perspective) - Link 2 is inactive

## Slide 16: During Transition (logical perspective) - Both links are active

## Slide 17: During Transition (Physical perspective) - Both links are active

## Slide 18: Further Discussion on Scaling
How does scaling work with many APs?
  Only a handful of APs (in the vicinity of the STA) need to be aware of the STA’s presence and ready for roaming
  The STA only needs to learn the presence of those APs (but need not have all those APs as setup links)

## Slide 19: Further Discussion on Link ID
Concern raised: how to signal so many links since the current link ID is only 4 bits
Answer:
  In a lot of cases (e.g., home network) the current link ID is enough
  When needed, we may extend the Link ID. One example is to define a Colocated set ID as follows:
    E.g., a floor has 100 11be physical APs, one collocated ID is assigned to each AP (collocated ID = 1, 2, …100)
      Note this is different than the AP MLD ID, which is the id of a specific AP MLD in a physical AP, which can host multiple AP MLDs (e.g., one for Home users and one for Guests)
    Define an “Extended link ID” as the tuple (Colocated set ID, link ID)

## Slide 20: Further Discussion on AID
Consider expanding AID space, even for baseline (good for IoT scenarios)
If keeping the same AID space, one option is to assign the client one AID per Colocated set
  Colocated set contains the affiliated APs that are located at the same physical AP that are used to serve the non-AP MLD (via a single MAC-SAP)
  Need to specify the Colocated set where this new AID applies
  A client can be assigned a list of (Colocated set ID, AID) depending on its location

## Slide 21: Further Discussion in Duration
Duration of using multiple APs?
  No limitations but ideally short (10s of ms) to enhance reliability with minimal load impact to the network