## Slide 1: More info about UHR PAR with updates
Date: 2022-11-08
Authors:
Name | Affiliation | Address | Phone | Email
Ming Gan | Huawei |  |  | ming.gan@huawei.com
David Xun Yang |  |  |  | 
Edward Au |  |  |  | 
Osama AboulMagd |  |  |  | 
Michael Montemurro |  |  |  | 
Stephen McCann |  |  |  | 
Yan Xin |  |  |  | 
Shimi Shilo |  |  |  | 

## Slide 2: Introduction
In the last UHR SG meeting, the scope below was discussed in UHR PAR document[1]
  Throughput: a) support a maximum aggregated throughput of at least 100 Gbps; b) at least two times improvement in the aggregated throughput for all signal to noise ratio (SNR) levels
  Improve worst case latency and jitter, satisfying real-time applications requirements
  Improve reliability of WLAN connectivity
  Backward compatibility and coexistence: a) enable backward compatibility and coexistence with legacy IEEE 802.11 devices, operating in frequency bands between 1 and 7.250 GHz; b) enable backward coexistence with legacy IEEE 802.11 devices operating in frequency bands between 42.5 and 71 GHz
  Moreover, throughput, latency and reliability improvement is not only for a single BSS, but also for multiple non-collocated BSSs
  In this contribution, we provide more thoughts about it and update the corresponding PAR text

## Slide 3: Throughput Improvement
It is feasible to support a maximum aggregated throughput of at least 100 Gbps with the following UHR scenario
Two times improvement in the aggregated throughput, also includes the client’s throughput improvement proposed by [2]
Band | Bandwidth | MCS | SS # | GI | Throughput
2.4 GHz | 20 MHz | 4096 QAM, 5/6 | 8 | 0.8 us | 1376.8 Mbps
5 GHz | 160 MHz | 4096 QAM, 5/6 | 8 | 0.8 us | 11529.6 Mbps
6 GHz | 320 MHz | 4096 QAM, 5/6 | 8 | 0.8 us | 23059.2 Mbps
60 GHz (reusing 11ac PHY) | 2560 MHz | 64 QAM, 5/6 | 8 | 0.05 us | 83200 Mbps
Sum |  |  |  |  | 119.2Gbps
Bandwidth | MCS | SS | GI | Throughput | 2x Throughput
320 MHz | 4096 QAM, 5/6 | 2 | 0.8 | 5764.8 Mbps | 11.5 Gbps

## Slide 4: Latency and Reliability
As reference [3] mentions, “reliability” should be considered together with the low latency/jitter and mobility.
Moreover, both the RTA report[4] and industrial PLC (programmable logic controller) use case[5] propose latency requirements at some certain percentiles
Given the above facts, the PAR section about latency and reliability is updated as following
  This amendment defines at least one mode of operation capable of improved latency bound and jitter in the 99 to 99.9999th percentiles compared to 802.11be, satisfying real-time applications requirements for high reliability in the presence of overlapping BSSs and for seamless BSS transitions within an ESS.
Applications and Requirements | Class A | Class B | Class C
Applications | Interactive video, soft-real-time control, mobile robotics, Automated Guided Vehicles (AGV) | AR/VR, remote HMI, hard-real-time cyclic control, machine tools, production lines | Hard-real-time isochronous control, motion control, printing, packaging
Latency bound | 50 -10 ms | 10 – 1 ms | 1ms – 250 µs
Reliability | 99% - 99.9% | 99.9% - 99.99% | >99.999%
Note-The reliability is defined as the percentage of packets expected to be received within the latency bound.

## Slide 5: Backward compatibility and coexistence
Regarding mmWave bands, it is a good starting point for UHR.
Agree to reuse the existing PHY designs to enable mmWave.
  Reuse 802.11ac numberology with X times upclocking
Backward compatibility is not considered within mmWave bands given that the preferred solution is to reuse existing PHY designs
On the other hand, energy detection can still be used for coexistence, with limited commercial 802.11ad/ay products (if any).

## Slide 6: Multi-AP coordination
The mmWave band can provide channels with large bandwidths for frequency reuse in dense scenarios.
In addition to the use of the mmWave band; multi-AP coordination, such as Co-SR, can also provide minor improvement on frequency use.
Hence, the corresponding PAR text is updated as follows, without emphasizing the mmWave band:
  In addition to further improvements of throughput and latency within a single basic service set (BSS), this amendment also focuses on improving the throughput, latency and reliability of multiple non-collocated BSSs in dense scenarios via a) in-band and optionally out-of-band (including via 802.3) AP MLD coordination for interference reduction, and b) the frequency reuse of channels with bandwidths larger than 40 MHz.

## Slide 7: Summary
This contribution suggests some PAR updates, based on the group’s recent discussions, proposing that a consensus can be reached.

## Slide 8: SP
Do you agree to include throughput, latency/jitter and reliability as objectives in the scope of project of the EHT PAR document?

## Slide 9: References
[1] 11-22-1518-01-0uhr-802-11-uhr-sg-proposed-par
[2] 11-22-0046-01-0wng-next-generation-after-802-11be
[3] 11-22-1493-01-0uhr-use-cases-for-wi-fi-business-solutions-in-uhr
[4] 11-18-2009-06-0rta-rta-report-draft
[5] 11-22-0458-01-0wng-looking-ahead-to-next-generation-follow-up