## Slide 1: Enhanced Trigger-Based Uplink Transmission
Date: 2022-11-10
Authors:

## Slide 2: Abstract
This contribution discusses enhanced trigger-based transmission for UHR.
Reducing latency is one of the major goals for UHR.
Enhancing the trigger-based solution for uplink transmission may help to achieve the low latency goal for UHR

## Slide 3: Introduction
UHR [1]During the WNG session in July 2022 plenary meeting, a motion was passed to form the Ultra High Reliability (UHR) study group (SG) to develop PAR for the “beyond be” 802.11 WLAN.
The major emphasis of the Next-Gen WLAN will be on [1]
  Improve reliability
  Reduce latencies
  Increase manageability
  Increase throughput, including at different SNR levels
  Reduce device-level power consumption
Several contributions regarding low latency are already presented in UHR SG [2]-[4].

## Slide 4: Trigger-Frame rules in IEEE 802.11
  A trigger frame (TF) allocates resources for and solicits one or more TB PPDU transmissions.
  The TF also carries other information required by the responding STA to send a TB PPDU.
  TF is needed to signal the non-AP STAs to begin UL transmission of their data with their assigned resource units (RU)s.
  An AP sends a TF to initiate UL MIMO operation using UL OFDMA or UL MU-MIMO transmissions.
  The TF identifies non-AP-STAs participating in UL MU operation and assigns RUs and/or spatial streams to these STAs.
Trigger Frame
TB PPDU
Multi-STA
BlockAck
SIFS
TB PPDU
SIFS
AP
STA 1
STA 2
TXOP

## Slide 5: Multiple Uplink Transmissions in a TXOP
In existing standard (802.11 ax/be architecture) in a TXOP
  Needs multiple TFs to allocate resources for initial transmission and transmission afterward.
  Granting multiple uplink transmissions is based on transmitting multiple TFs.
  It increases overhead due to multiple trigger frame transmission in uplink.
Trigger Frame
TB PPDU
Multi-STA
BlockAck
SIFS
TB PPDU
SIFS
SIFS
Trigger Frame
TB PPDU
SIFS
BA
AP
STA 1
STA 2
TXOP
SIFS

## Slide 6: Enhanced Trigger-based Transmission (1)
We propose to allocate multiple UL transmissions using a single TF.
It will improve system efficiency in terms of latency.
For example,
  One TF carries the information for the STAs to have multiple UL transmissions.
  Removal of multiple TFs and SIFSs reduces latency.
  Reliability can also be increased if the subsequent PPDU retransmits the same data.

## Slide 7: Enhanced Trigger-based Transmission (2)
  Option 1: Multiple UL transmission in a single TF.
Trigger Frame
TB PPDU
Multi-STA
BlockAck
SIFS
TB PPDU
SIFS
SIFS
Trigger Frame
TB PPDU
SIFS
BA
AP
STA 1
STA 2
TXOP
Trigger Frame
TB PPDU
Multi-STA
BlockAck
SIFS
TB PPDU
SIFS
SIFS
TB PPDU
SIFS
BA
AP
STA 1
STA 2
TXOP
SIFS
Schedule STA 1 for multiple transmission
Schedule STA 2 for a single transmission
Remove the next TF

## Slide 8: Enhanced Trigger-based Transmission (3)
  Option 2: Multiple UL transmission with no Multi-STA BlockAck between PPDUs in a single TF
Trigger Frame
TB PPDU
Multi-STA
BlockAck
SIFS
TB PPDU
SIFS
SIFS
Trigger Frame
TB PPDU
SIFS
BA
AP
STA 1
STA 2
TXOP
Trigger Frame
TB PPDU
SIFS
TB PPDU
SIFS
TB PPDU
SIFS
BA
AP
STA 1
STA 2
TXOP
SIFS
Signal STA 1 for multiple transmission
Signal STA 2 for a single transmission
No Multi-STA BlockAck transmission

## Slide 9: Comparison of Estimated TXOP Duration
Assumptions
N: # of STAs =2, MCS0 (for Non-HT), MCS7 (for EHT)
Bandwidth = 80 MHz
Payload Size = 100 Octets, 500 Octets, 1000 Octets
Tones
  484 Tones for EHT TB PPDU (Data Rate = 146.3 Mb/s)
Preamble Duration
  20 μs (Non-HT)
  48 μs (EHT)
EHT TB PPDU Data Duration
  Ceiling((#Octets*8 /Data Rate) / 16) * 16 µs
  Trigger frame duration:
    [{(16+9+6*N+6) Bytes * 8+16+6}/(48*1/2)]*4 μs +20 μs (Non-HT Preamble Duration)
  TB PPDU duration:
    48 μs (EHT Preamble Duration) + EHT TB PPDU Data Duration
    Multi-STA BA frame duration [6] :
    Ceiling[{(22+12N)*8+16+6}/(48*1/2)]*4 μs+ 20 μs (Non-HT Preamble Duration)
    BA frame Duration [6]:
    Ceiling{(32*8+16+6)/(48*1/2)}*4 μs+ 20 μs (Non-HT Preamble Duration)
SIFS = 16 μs
Type | 100 Octets |  | 500 Octets |  | 1000 Octets | 
 | Duration (μs) | Gain compared to the existing trigger-based transmission | Duration (μs) | Gain compared to the existing trigger-based transmission | Duration (μs) | Gain compared to the existing trigger-based transmission
Existing Trigger-based Transmission | 502 |  | 546 |  | 600 | 
Enhanced Trigger-based Transmission (Option 1) | 405 | 19.3 % | 449 | 17.8 % | 503 | 16.2 %
Enhanced Trigger-based Transmission (Option 2) | 304 | 39.4 % | 348 | 36.3 % | 402 | 33 %

## Slide 10: Summary
We discussed the potential enhanced trigger-based transmission for UL transmission to meet the low latency target of UHR.
We envision that enhanced trigger-based transmission has the potential to reduce latency.

## Slide 11: Straw Poll
Do you think that trigger-based transmission in the baseline specs (ax/be) may be modified to improve latency in UHR SG/TG?
  Yes:
  No:
  Abstain:

## Slide 12: References
[1] E. Jeon et al., “Beamforming Improvement for UHR,” https://mentor.ieee.org/802.11/dcn/22/11-22-1392-00-0uhr-beamforming-improvement-for-uhr.pptx.
[2] W. B. Lee et al., “Latency Reduction Scheme for UHR,” https://mentor.ieee.org/802.11/dcn/22/11-22-1393-00-0uhr-latency-reduction-scheme-for-uhr.pptx.
[3] T. Shu, “Requirements of Low Latency in UHR,” https://mentor.ieee.org/802.11/dcn/22/11-22-1519-00-0uhr-requirements-of-low-latency-in-uhr.pptx.
[4] L. Lu, “Multi-AP Coordination for Low latency Traffic Delivery,” https://mentor.ieee.org/802.11/dcn/22/11-22-1519-00-0uhr-requirements-of-low-latency-in-uhr.pptx
[5] Draft “IEEE Standard for Information Technology–Telecommunications and Information Exchange between Systems - Local and Metropolitan Area Networks–Specific Requirements - Part 11: Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications,” IEEE P802.11-REVme/D2.0, pp. 1–5797.
[6] J. Kim et al., “A Method of transmitting Multi-STA Block ACK,” https://mentor.ieee.org/802.11/dcn/15/11-15-1330-00-00ax-a-method-of-transmitting-multi-sta-block-frame.pptx