## Slide 1: Thoughts on UHR Features
Date: 2022-11-11
Authors:

## Slide 2
Abstract
In this contribution we share some thoughts on UHR features based on a set of UHR requirements.

## Slide 3: Introduction (1)
  802.11 has approved to form UHR SG to formulate PAR and CSD for next generation major revision of PHY and MAC
  UHR requirements have been discussed in both WNG and UHR SG
    Some proposals for UHR requirements in the WNG contributions [1-5]
    PAR proposals in UHR SG [6,7]
    Other presentations in UHR SG
  Some common requirements are:
    Improved latency (< 1ms [2], <0.1ms [3], <10 ms [6])
    Improved throughput (>100 Gbps [1][6][7], > 2x 11be [2], 10 Gbps [3])
    Improved mobility and coverage [1][3][4]
  Reliability has also been mentioned in a number of contributions [7,8,9]
    It would be good to provide detailed requirement for reliability

## Slide 4: Introduction (2)
  We have shared our thoughts on UHR requirements in a previous contribution [8]
    QoS Improvement
      Support of low latency &
      High reliability
    Per link throughput improvement
    Better integration of various 802.11 technology from different amendments
  In addition, power saving has been raised as a requirement by several contributions [10,11]
    Power consumption is always an important requirements for battery life and to satisfy potential regulatory rules
  In this contribution, we share our views on some of the UHR features needed to satisfy these requirements

## Slide 5: Requirements for UHR
Some requirements for UHR from [8]
QoS improvement
  Low latency support (~0.5 ms)
  High reliability (99.999999%)
Per Link throughput improvement (2 Gbps per user aggregated over all links)
Power Saving
Better integration of 802.11 technologies from various amendments

## Slide 6: QoS Improvement
QoS improvements needs a multi-facet solutions including:
Network efficiency improvement
  Multi-AP/Multi-MLD coordination, e.g.:
    Coordinated transmission: OFDMA, beamforming, joint transmission
    Coordinated multi-link
    Coordinated spatial reuse
    Coordinated handover
Reliability improvement
  Restriction of traffic rather than prioritization of high priority traffic
  Better usage of 6GHz
  Hybrid ARQ (may require significant change to current MAC/PHY design)

## Slide 7: QoS Improvement (2)
Overhead reduction
  PHY Design improvement: e.g., preamble design
  16 SS requires significant training overhead
    Better sounding protocols and PPDU designs to reduce overhead
  Efficient multi-AP/multi-MLD sounding procedure
  More efficient UL traffic indication

## Slide 8: Per link Throughput Improvement
Some potential technologies that may meet such demand:
  16 spatial streams
  Even wider bandwidth in 6GHz band
  Hybrid ARQ

## Slide 9: Power Saving
Listening mode of STAs contributes considerable amount of time overall in a real-life network and contributes significant amount of power consumption [10]
One way to mitigate the large power consumption is to wake up the device when needed
  802.11ba provides power saving using Wake Up Radios
Integrate 11ba PPDU in UHR PPDU
  Particularly when A-PPDU will be designed for UHR, a potential 11be R2 feature
  This will also allow better integration of various 802.11 amendments

## Slide 10: Summary of features
 | Low Latency | High Reliability | Throughput | Power Saving | Multi-amendment Integration | Handover/ Roaming
MAP/MMLD | Yes | Yes | Yes | Yes |  | yes
Coord. ML | Yes | Yes | Yes | Yes |  | 
>320 MHz |  | Yes | yes |  |  | 
Overhead Reduction | Yes |  | Yes | Yes |  | 
16 SS |  |  | Yes |  |  | 
11ba/UHR PPDU |  |  |  | Yes | yes | 
HARQ | Yes | Yes | Yes |  |  | 

## Slide 11: Thoughts on mmW band for UHR
mmW band may be helpful to achieve UHR requirements when available
  Pro: Large bandwidth available, hence benefit throughput when available
  Con:
    Cannot guarantee low latency due to beam searching and refinement procedures
    Cannot guarantee reliability due to propagation characteristics in mmW bands
    May be very power consuming
    High PAPR
UHR SG should carefully weigh the pros and cons before deciding on mmW feature

## Slide 12: Conclusions
In this contribution, we share our thoughts on requirements and potential technologies for Next Gen WLAN
  MAP
  Coord. ML
  > 320 MHz
  Overhead reduction
  16 SS
  11ba/UHR PPDU
UHR should carefully consider pros and cons for
  mmW
  HARQ
Recommend UHR SG to formulate clearly the requirements in PAR, in particular, the reliability requirement

## Slide 13
References
[1] 11-22/0030, Look ahead to next generation
[2] 11-22/0032, Next Gen After 11be
[3] 11-22/0046, Next Generation After 802.11be
[4] 11-22/0059, Beyond ‘be’
[5] 11-22/458, Looking ahead to next generation: follow up
[6] Towards 6G: Evolution of Key Performance Indicators and Technology Trends, 2nd 6G Wireless Summit, March 2020
[7] 11-22/1518, UHR SG Proposed PAR
[8] 11-2/1750r0, PAR Proposal
[8] 11-22/694 Thoughts on Next Gen WLAN
[9] 11-22/685, Discussion on next generation Wi-Fi
[10] 11-22/1414 Low Power Listening Mode
[11] 11-22/1790 Green AP and resilience requirements for home networks