## Slide 1: PPDU Design for Short Frames
Date: 2022-11-09
Authors:

## Slide 2: Abstract
Many frames in 802.11ax and 802.11be that are important in maintaining high throughput and efficiency have a short duration
  Trigger Frames
  Initial Frame exchanges for EMLSR
  QoS Null Data frames for A-Control information transport.
  Short Low Latency Frames
Many are sent using Non-HT PPDUs for backward compatibility and ease of decoding. However Non-HT PPDUs lack many features of EHT PPDUs.
With UHR, it is expected that these frames will continue to play a vital role.
  More trigger frames (e.g. Multi-AP transmissions [1])
  A-PPDU Announcement/Trigger Frame [2]
  Initial Control Frames for Low Power Listening Mode [3]
In this proposal, we discuss the possibility of supporting a new PPDU format dedicated for short frames for UHR.

## Slide 3: Non-HT PPDU for Short Frames
Short frames are typically sent using non-HT PPDUs for backward compatibility, preamble efficiency and ease of decoding.
STF
LTF
L-SIG
DATA
However, it has some limitations
Not forward compatible to future standards (i.e. does not have a U-SIG)
Incomplete bandwidth signaling.
No puncturing signaling.
Many important information are in the MAC layer (e.g. Receive Address, BSSID, etc.)
Does not support LDPC, DUP mode, for range extension.

## Slide 4: EHT PPDU for Short Frames
One way to address some of the problems when transmitting short frames is to use EHT PPDUs (i.e. EHT MU PPDU). However, EHT PPDUs are more appropriate for transmitting large PPDUs and/or MU transmissions.
- OFDMA, MIMO, and MCS related features require numerous SIG fields to indicate but are not necessary when transmitting short frames.
Receiving short frames transmitted with EHT PPDUs require the receivers to operate at full power (see [4]). This limits its use for EMLSR or in Low Power Listening mode.
Receiving short frames with EHT PPDUs also have a higher latency due to the larger FFT size and longer preambles.

## Slide 5: UHR PPDU for Short Frames
We believe it is a good time to discuss support for an enhanced PPDU for Short frames.
The UHR PPDU for Short Frames may include
- low power decodability
- short preamble (i.e. some PHY features will not be supported)
- high bandwidth capable for high reliability or low latency
For mmWave UHR, a low rate Control PPDU format (similar to 802.11ad/ay’s Control PPDU format) may be needed to address the range issue before beamforming training is established.
Header Block
Preamble
Data
AGC subfields
TRN subfields

## Slide 6: UHR PPDU for Short Frames
STF
LTF
L-SIG
DATA
RL-SIG
U-SIG
UHR-SIG
1. STF, LTF, L-SIG, RL-SIG, are exactly the same as in the EHT.
2. U-SIG indicates UHR as PHY Version Identifier
3. All SIG fields and Data have the same numerology (i.e. subcarrier spacing, FFT size) as the legacy LTF.
4. Support only SISO (No extra UHR STFs/LTFs are needed)
optional

## Slide 7: Wider Bandwidth Support for Short Data Frames
Non-HT PPDUs have a short efficient preamble. However, it doesn’t support features necessary for transmissions in wider bandwidth.
With a wider bandwidth support, the DATA field can be encoded as a non-Duplicated PPDU, or a UHR Duplicated PPDU (i.e. with explicit signaling)
STF
LTF
L-SIG
DATA
STF
LTF
L-SIG
RL-SIG
STF
LTF
L-SIG
RL-SIG
STF
LTF
L-SIG
RL-SIG
STF
LTF
L-SIG
RL-SIG
STF
LTF
L-SIG
DATA
RL-SIG
STF
LTF
L-SIG
RL-SIG
STF
LTF
L-SIG
RL-SIG
STF
LTF
L-SIG
RL-SIG
Duplicate
Duplicate
Duplicate
BW=80MHz
Duplicate
BW=80MHz
Non-Duplicate
For Low Latency Application
For High Reliability
DATA
U-SIG
U-SIG
U-SIG
U-SIG
U-SIG
U-SIG
U-SIG
U-SIG

## Slide 8: PPDU Overhead Comparisons
Assumptions
PPDU Bandwidth = 80MHz
Payload Size = 150 Octets, 1500 Octets
Tones
  48 Tones for Non-HT (Data Rate = 54 Mb/s)
  996 Tones for EHT MU PPDU (Data Rate = 306.3 Mb/s)
  52 x 4 Tones for Short UHR PPDU (Data Rate = 65 x 4 Mb/s)
Preamble Duration
  20 µs for Non-HT
  56 µs for EHT MU PPDU
  32 µs for Short UHR PPDU
Data Duration
  Ceiling((#Octets x 8 /Data Rate) / 4) * 4 µs for Non-HT and Short UHR PPDU
  Ceiling((#Octets x 8 /Data Rate) / 16) * 16 µs

## Slide 9: PPDU Overhead Comparisons
 | Preamble Duration | 150 Octet PPDU | 1500 Octet PPDU
Non-HT PPDU | 20 µs | 44 µs | 244 µs
EHT MU PPDU | 56 µs | 72 µs | 104 µs
Short UHR PPDU | 32 µs | 40 µs | 80 µs
The Proposed UHR PPDU for short frames is more efficient with short frames. For longer frames, the EHT MU PPDU is more efficient.
However, unlike the Non-HT PPDU, the Short UHR PPDU can take advantage of the large bandwidth to increase its data rate. This can further shorten the latency for medium length frames.

## Slide 10: Summary
Many frames in 802.11 that are important in maintaining high throughput and efficiency have a short duration. A PPDU designed for Short Data Frames can enhance the benefits of these frames.

## Slide 11: References
[1] https://mentor.ieee.org/802.11/dcn/18/11-18-1982-01-0eht-consideration-on-multi-ap-coordination-for-eht.pptx
[2] https://mentor.ieee.org/802.11/dcn/20/11-20-0674-01-00be-forward-compatible-ofdma.pptx
[3] https://mentor.ieee.org/802.11/dcn/22/11-22-1414-01-0uhr-low-power-listening-mode.pptx
[4] https://mentor.ieee.org/802.11/dcn/20/11-20-0562-02-00be-enhanced-multi-link-single-radio-operation.pptx