## Slide 1: AIML Model Sharing Use Case
Date: 2022-11-10
Authors:

## Slide 2
Abstract
In this contribution, we discuss a use case to support AIML in IEEE 802.11 networks.

## Slide 3: Introduction
The AIML TIG was established by a WG motion in May 2022 [1] to:
  describe use cases for Artificial Intelligence/Machine Learning (AI/ML) applicability in 802.11 systems and
  investigate the technical feasibility of features enabling support of AI/ML.
So far contributions presented have been focusing on apply AI/ML algorithm to improve the performance of 802.11 systems
The TIG may benefit to look at use cases that explore enabling support of AI/ML in 802.11 networks

## Slide 4: Model Sharing to Support AI/ML (1)
AI/ML model building and deployment has been discussed in [2]
  Case 1: Centralized AI/ML model training
    STAs to provide training data to a central point, e.g., an AP, or a server e.g., where AI/ML model is trained
    The central point distributes the global model to all participating devices
  Case 2: Distributed AI/ML model training
    All participating devices, such as STAs or APs, are capable of computing models and share data to all participating devices so that each device can train the global model
      This scenario may be too taxing for 802.11 devices since it requires a large amount of data to be exchanged over the air and requires high computation power at each device
  Case 3: Hybrid AI/ML model training
    3a. All participating devices, such as STAs or APs, are capable of computing models and share their local models to a centralized point to train the global model
    3b. All participating devices, such as STAs or APs, are capable of computing models and share local models to all participating devices so that each device can compute the global model

## Slide 5: Model sharing requirements to support AI/ML
Model sharing is essential to enable AI/ML in 802.11
  Case 1: Centralized AI/ML model training
    The central point distributes the global model to all participating devices, likely DL, from AP to STAs
  Case 2: Distributed AI/ML model training
    May not be suitable for 802.11 networks
  Case 3: Hybrid AI/ML model training
    3a. All participating devices share local models to a centralized point:
    All devices, likely in UL, share their local models to a centralized point
    The central point distributes the global model to all participating devices, likely DL, from AP to STAs
    3b. All participating devices, such as STAs or APs, share local models to all participating devices
    All devices, likely in UL and DL, share their local models to each other

## Slide 6: Enabling AI/ML Model sharing in 802.11 (1)
Model sharing to enable AI/ML in 802.11 is best achieved through broadcast
  Broadcast enables the most efficient distribution of models to a large number of users
802.11bc has been designed to provide enhanced broadcast services (EBCS)
  Provides EBCS in both UL and DL
  Provides EBCS for both associated or unassociated STAs/APs
802.11bc may be leveraged to provide efficient model sharing to enable AI/ML
AI/ML model sharing is agnostic of how the model is being used
  The AI/ML model may be trained and used to improve 802.11 performance
  The AI/ML model may be trained and used for other type of applications independent of the 802.11 networks
    Autonomous driving, video compression, human-machine interface, etc.

## Slide 7: Enabling AI/ML Model sharing in 802.11 (2)
The following need to be specified depending on how the AI/ML model is used:
  Architecture that enables AL/ML model sharing
  Signaling and protocol related to AI/ML model sharing support/capability indication
  Signaling and protocol related to AI/ML model sharing management

## Slide 8: Conclusion
We have proposed a use case to support AI/ML model sharing in order to enable AIML in 802.11 networks
Leveraging EBCS (Enhanced Broadcast Services) as defined in 802.11bc would provide an efficient way of AIML model sharing in both UL and DL
We provided some analysis for standard impact for this use case

## Slide 9
References
[1] 11-22/597r3: May 2022 Working Group Motions, May 18, 2022
[2] 11-22/1443, Wi-Fi Meets ML: Re-thinking Next-generation Wi-Fi Networks

## Slide 10: Straw Poll
Do you agree that AIML model sharing should be considered as a use case for AIML TIG?
  Y/N/Abs: