## Slide 1: On the necessity of separating MAC protocols into data and control planes
Authors:
Name | Affiliations | Address | Phone | Email
Zhongjiang Yan | Northwestern Polytechnical University | No. 127, West Youyi Rd., Xian, Shaanxi, China |  | zhjyan@nwpu.edu.cn
Bo Li |  |  |  | libo.npu@nwpu.edu.cn
Mao Yang |  |  |  | yangmao@nwpu.edu.cn
Date: 2022-11-10
doc.: IEEE 802.11-22/1949-00-0wng

## Slide 2: Introduction
Several contributions were proposed for WNG in previous meetings.
Before proceeding, it is time to think about the need to separate MAC into the data and control planes.
  In Ref. [1], Std 802.11-2020 Fig. 5.1 shows the MAC data plane architecture, i.e., the transports of all or part of an MSDU.
  Here, MAC control plane involves the processes to establish the wireless link by using MAC control frames.
In this contribution, the necessaries to separate the MAC protocols into the data plane (DP) and control plane (CP) are discussed.
  Details are referred to Ref [4].
doc.: IEEE 802.11-22/1949-00-0wng

## Slide 3: MAC CP-DP features and relationships
Features
  Reliable CP: using low MCS, a few of spatial streams, usually maximum transmission power
  High rate DP: higher MCS, many spatial streams
Coupled relationships
  Time dependence: Immediately data transmission after successful channel access on the same channel, i.e., handshake of RTS-CTS, or directly data transmission without RTS-CTS
  Casual dependence: high rate DP depends on reliable CP
doc.: IEEE 802.11-22/1949-00-0wng
doc.: IEEE 802.11-22/1949-00-0wng

## Slide 4: MAC CP-DP in DCF and EDCA
Problem 1: collisions
  Collisions in CP, e.g., in Fig. (a) hidden terminal problems caused collision between node B’s CTS and node D’s RTS.
  Collides between CP and DP, e.g., in Fig. (a) node A’s data collides with node C’s CTS at node B, and in Fig. (b) node B’s ACK collides with node D’s Data
doc.: IEEE 802.11-22/1949-00-0wng
doc.: IEEE 802.11-22/1949-00-0wng

## Slide 5: MAC CP-DP in DCF and EDCA
Problem 2: blockings
  At t1, low rate CP blocks low latency DP
  At t2, long DP blocks Beacon, i.e., the control or management frames,
  At t3, long DP blocks low latency DP.
doc.: IEEE 802.11-22/1949-00-0wng
doc.: IEEE 802.11-22/1949-00-0wng

## Slide 6: MAC CP-DP in channel binding
Problem 3: bottleneck of primary channel
  Busy primary channel becomes the bottleneck to utilize the secondary ones, since both CP and DP are both evolved in.
  Even though the bandwidth of the channel bonding increases from 40MHz in 11n to 320MHz in 11be, it results in low usage of channels.
doc.: IEEE 802.11-22/1949-00-0wng
doc.: IEEE 802.11-22/1949-00-0wng

## Slide 7: MAC CP-DP in channel binding
Problem 4: lower usage of secondary channel
  More channels, lower usage.
  Except of bottleneck problem, other reasons include STA capability, channel state and restricted binding rules.
1. STA is capable of 40MHz channel binding.
2. Busy state of secondary channel
3.
doc.: IEEE 802.11-22/1949-00-0wng
doc.: IEEE 802.11-22/1949-00-0wng

## Slide 8: MAC CP-DP in data rate increasing
Problem 5: relatively reduced efficiency of CP
  More binding channels, higher data rate of DT.
  PHY rate increases with MCS, e.g., from 64QAM to 4096QAM.
doc.: IEEE 802.11-22/1949-00-0wng
doc.: IEEE 802.11-22/1949-00-0wng

## Slide 9: MAC CP-DP in fragmented access interval
Problem 6: reduced efficiency of DCF and EDCA
  rTWT is proposed in 11be draft, which separates the timeline into fragmented access intervals.
  Fragmented access intervals decrease the efficiency of CP, e.g., DCF and EDCA.
doc.: IEEE 802.11-22/1949-00-0wng
doc.: IEEE 802.11-22/1949-00-0wng

## Slide 10: Conclusions
No. | Problems | Reasons
1 | Collisions of intra CPs and between CP and DP | Hidden terminals loss of NAV
2 | Blockings of intra DPs and between CP and DP | Low rate CP and long time DP exist on the same channel or link.
3 | Bottleneck of primary channel | 
4 | Low usage of secondary channels | Bottleneck of primary channel Channel binding capabilities/rules Independent secondary channels’ states
5 | Relatively reduced efficiency of CP | Increased bandwidth of DP Increased PHY rate
6 | Reduced efficiency of DCF and EDCA | Fragmented access intervals caused by new schemes, e.g., rTWT
doc.: IEEE 802.11-22/1949-00-0wng
doc.: IEEE 802.11-22/1949-00-0wng

## Slide 11: Suggestions
Useful clues can be found from related works [2-3].
  In Ref. [2], we propose an efficient MAC protocol with multiple-step distributed in-band channel reservation.
  In Ref. [3], we propose a reservation based multi-channel MAC protocol for single radio.
doc.: IEEE 802.11-22/1949-00-0wng
doc.: IEEE 802.11-22/1949-00-0wng

## Slide 12: Reference
IEEE Std 802.11-2020 (Revision of IEEE Std 802.11-2016) , vol., no., pp.1-4379, 26 Feb. 2021, doi: 0.1109/IEEESTD.2021.9363693.
Bo Li, Wei Li, and F. Valois, et al. Performance analysis of an efficient MAC protocol with multiple-step distributed in-band channel reservation[J]. IEEE Transactions on Vehicular Technology, 59, 368-382, 2010.
Bo Yang, Bo Li, Zhongjiang Yan, Mao Yang, Der-Jiunn Deng, Performance Analysis of Multi-channel MAC with Single Transceiver for the Next Generation WLAN, J. Network and Computer Applications 146 (2019)
http://arxiv.org/abs/2210.08492
doc.: IEEE 802.11-22/1949-00-0wng