## Slide 1: UHR Operation in Lightly Licensed Spectrum
Date: 2022-11-##
Authors:

## Slide 2: Topics
Introduction
Potential Benefits
Considerations
Preliminary Design Principles
Implications for UHR effort
Rolf de Vegt (Qualcomm Technologies, Inc.)

## Slide 3: Introduction
In multiple geographies, governments are considering making spectrum available for Lightly Licensed Operation e.g. for Private Networking
Some preliminary examples:
  Germany: 3700 - 3800 MHz for industrial applications
  Europe: 3800 - 4200 MHz per a new draft mandate
  US: 3550 – 3700 MHz for CBRS
  Japan: 4.6 – 4.9 GHz (targeting 5G PN)
Often the originally pursued use is by 5G cellular technologies, however adoptions is relatively slow and regulations are typically ‘technology neutral’*; i.e. 802.11 technologies could be deployed, assuming regulatory parameters are met
* e.g. the draft EU mandate on 3.8 – 4.2 for terrestrial wireless broadband systems calls for: “……support the principles of service and technological neutrality, non-discrimination and proportionality insofar as technically possible”.
Rolf de Vegt (Qualcomm Technologies, Inc.)

## Slide 4: Potential benefits of 802.11 technologies for lightly licensed spectrum
Ease of integration into existing WLAN network infrastructure
  Existing back-end infrastructures
  Networking expertise present
  Ease of integration into existing multi-radio AP designs, where appropriate for use case (e.g. robotics manufacturing environment)
No ‘rogue’ Wi-Fi devices impacting network performance
No foreign OBSS’s
Benefits resulting from the ability to run fully scheduled and infrastructure controlled modes
Potential ability to leverage 6GHz AFC system infrastructure for licensing management
May provide a pathway for regulators to gradually make spectrum available to unlicensed operation in a more controlled manner
Rolf de Vegt (Qualcomm Technologies, Inc.)

## Slide 5: Key Considerations on Viability for 802.11
For this opportunity to be viable there are a number of factors to consider:
Minimum amount of spectrum availability
  100 MHz minimum?
Frequency band alignment amongst geographies making lightly licensed spectrum available
  Need for ability to cover multiple geographies with a single RF Receiver design
OOB emissions requirements, channel spectrum masks and output power limits that are economically feasible for 802.11 technology
Rolf de Vegt (Qualcomm Technologies, Inc.)

## Slide 6: Applications Considerations
Current ‘Lightly licensed’ regimes currently typically target licensing to enterprises, research institutes and government entities for specific geographic locations
Some potential usages enabled:
  Deterministic and ultra low latency applications with relatively low payload/throughput requirements such as robotics and manufacturing control
  Support for large numbers of low power IOT devices, e.g. ESL in retail
  Effective load balancing and seamless hand off between AP’s enabled by strict infrastructure control
  Open to further security enhancements
Rolf de Vegt (Qualcomm Technologies, Inc.)

## Slide 7: Why part of UHR
The timing is right now that Regulators worldwide are making spectrum available for ‘Lightly Licensed operation’ typically on a ‘Technology Neutral’ basis
Embracing ‘Greenfield’ Lightly Licensed spectrum has a strong potential to achieve further benefits regarding the following four UHR targets:
  Improve reliability of WLAN connectivity
  Predictable latency
  Increase manageability
  Reduce device level power consumption
Including lightly licensed spectrum operation increases the potential for 802.11 UHR to match or exceed competitive benchmark KPI’s
Rolf de Vegt (Qualcomm Technologies, Inc.)

## Slide 8: Design Principles - Preliminary
Reuse baseline Wi-Fi as much as possible
  Operate in fully scheduled trigger-based mode using baseline scheduling techniques with added rules (say, MU EDCA=0)
    Allows predictable latency
  Minimize the management frames in this band, by taking advantage of 11be MLO operation
    Conduct discovery, authentication, and other management procedures on other bands
    Helps to fully utilize the spectrum for delivering the payload
  Also include the definition of a ‘fully stand-alone mode’
    E.g. for vendors or network owners who prefer to only operate on the lightly licensed frequencies
  Should be able to use baseline QoS framework, with some extensions
    Example, QoS for IIoT requirements
Other changes TBD
  For example, PHY changes TBD
Rolf de Vegt (Qualcomm Technologies, Inc.)

## Slide 9: Implications for the UHR efforts
Leave open the possibility in the PAR to cover ‘lightly licensed’ spectrum frequencies
PAR not to exclude fully scheduled MAC mode and consider technology for inclusion in UHR standard
Rolf de Vegt (Qualcomm Technologies, Inc.)