## Slide 1: ID encoding in “pre-schemes”
Date: 2022-11-16
Authors:

## Slide 2: Abstract
Multiple mechanisms to address “pre-association” use cases have been presented in TGbh discussions (MAAD, IRMA, RRCM, ..).
The proposals discussed so far have used the MAC address fields (mainly, the Address 2/TA field).
This contribution discusses an alternative approach for encoding this type of information without an impact to the actual MAC address use in the frame header.

## Slide 3: MAC address encoding
Already existing field in the frames
  No length impact
Use not trivial to determine for passive 3rd parties
  Though, this has an impact for the intended target AP as well since it needs to assume all locally administered MAC addresses might be using a mechanism and as such, need to try to process TA in each received frame.
Limited to 46 bits of information
Impact to non-AP STA implementation for MAC address assignment

## Slide 4: A new information element
A new information element could be defined to encode similar, or expanded, information
  Could be included in various Management frames (Probe Request, GAS, Authentication, (Re)Association Request, etc.)
In the simplest case, the payload could be six octets to match the size of the existing proposals
Allows non-AP STAs to use existing random MAC address selection mechanisms as-is
AP can easily determine which frames need additional processing to check for known identity
  But would allow 3rd parties to recognize use of the mechanism

## Slide 5: ID length
Since an information element can include more octets, no limitation to just 46 bits
Possibility to reduce the likelihood of collisions
Could still be mapped to a MAC address by the AP, if a MAC address is needed for some existing use cases that RCM broke

## Slide 6: Encrypted information
Larger container would allow use of public key encryption of the ID
  Public key from the AP/ESS received in 4-way handshake
  AP does not need to check against potentially large set of IDs; single private key to decrypt
  Information protected from 3rd party observation
For example, using HPKE
  HPKE base mode with single-shot API; see RFC 9180
  Used in Wi-Fi Easy Connect (DPP) for privacy protection
  Generates different encrypted payload for each instance/frame

## Slide 7: Additional optional protection
If needed for some use cases, could also use a keyed hash with per-STA key
  Per-STA key derived in 4-way handshake (or FILS association) from KDK
For example: HPKE(<info> | HMAC(key, <info | A2>)
  where <info> = ID [|real time] [| BSSID | Timestamp from a recent Beacon frame]
Limits possibilities for attacks replaying frames in a different location or at a different time

## Slide 8: Needed protocol extensions
Definition of a new information element and description on its use in various Management frames
  Including optional use of HPKE
New KDE/IE to deliver AP/ESS public key in 4-way handshake/FILS association response, if HPKE is used
Rules to derive a key from KDK for HMAC (if used)
Rules for ID generation
  Could use a design from existing proposals or something based on them
  Could also use the baseline Device ID since this is encrypted