## Slide 1: Discussion on the scope of AMP in WLAN
Date: 2022-11-16
Authors:
Name | Affiliation | Address | Phone | Email
Weijie Xu | OPPO |  |  | xuweijie@oppo.com
Yinan Qi |  |  |  | v-qiyinan@oppo.com
Doc.: IEEE 802.11-22/2017r0
November 2022

## Slide 2: Outline
Background
Scoping for AMP in WLAN
Doc.: IEEE 802.11-22/2017r0
November 2022

## Slide 3: Background
In previous submission[1], the state-of-the-art AMP communication in WLAN is summarized, including the use cases, requirements, gap analysis, device types, candidate techniques, ambient power and energy storage, feasibility, prototype etc.
In addition, the contribution [1] gives the design target and the recommendations.
Doc.: IEEE 802.11-22/2017r0
November 2022

## Slide 4
Scope discussion for AMP in WLAN(1)
  1: Goal of AMP in WLAN: To specify an ultra-low-power-consumption WLAN device supporting AMP communication, e.g. lower than 1mw.
  2: Energy harvesting is based on implementation and is out of the scope of the specification.
    If RF power is used as the power resource by a WLAN device supporting AMP, how the WLAN device transfers the received RF power into transmitting RF power is also based on implementation.
Doc.: IEEE 802.11-22/2017r0
November 2022
Weijie Xu (OPPO)
Slide 4

## Slide 5
Scope discussion for AMP in WLAN(2)
  3: Potential approaches
    3.1 Downlink: WUR-similar design could be as the starting point
        Similar channel structure, waveform, PPDU formats, etc.
        Some re-design may be necessary if AMP in WLAN is implemented in frequency band other than 2.4GHz, e.g., S1G.
Doc.: IEEE 802.11-22/2017r0
November 2022
Weijie Xu (OPPO)
Slide 5

## Slide 6
Scope discussion for AMP in WLAN(3)
  3: Potential approaches
    3.2 Up Link:
      Simplified UL PHY with simple waveform such as OOK/FSK
        Both Active OOK/FSK transmitter and backscattered OOK/FSK should be considered.
      The carrier and bandwidth of backscattering signal to be specified
        Signal of narrow bandwidth or wide bandwidth
Doc.: IEEE 802.11-22/2017r0
November 2022
Weijie Xu (OPPO)
Slide 6

## Slide 7
Scope discussion for AMP in WLAN(4)
  3: Potential specification impact
    3.3 MAC: Simplified MAC + Enhanced power saving/ power management.
Doc.: IEEE 802.11-22/2017r0
November 2022
Weijie Xu (OPPO)
Slide 7

## Slide 8
Scope discussion for AMP in WLAN(5)
  4: Frequency band
    Support S1G, and
    2.4 GHz frequency band can be considered
Doc.: IEEE 802.11-22/2017r0
November 2022
Weijie Xu (OPPO)
Slide 8

## Slide 9: Summary
This submission discusses the scope for AMP in WLAN.
Doc.: IEEE 802.11-22/2017r0
November 2022

## Slide 10: Reference
11-22-1960-00-0amp-summary-and-recommendation-for-AMP-IoT
Doc.: IEEE 802.11-22/2017r0
November 2022