## Slide 1: Summary of EDT discussion in ETSI BRAN
17 Nov 2022
Authors:
Name | Company | Phone | email
Andrew Myles | Cisco | +61 418 656587 | amyles@cisco.com

## Slide 2: The 5 GHz EDT issue in BRAN …
  The following slides provide a summary of the 5 GHz EDT issue and discussions in ETSI BRAN
    How did we get to this point?
    What are options, with pros/cons?
    What are the viable options?
  The views expressed are those of Andrew Myles (Cisco) but they are generally consistent with previous discussions in the Coex SC
    … but feel free to disagree
    … and propose alternate views

## Slide 3: It was difficult to find an acceptable compromise for EN 301 893 that met the needs of all stakeholders
  ETSI BRAN has spent many years discussing appropriate rules for channel access to enable fair & efficient use of 5 GHz spectrum between many technologies
  The challenge has been to define requirements in EN 301 893 that meet the needs of all stakeholders
    Wi-Fi stakeholders want to ensure the rules continue to allow Wi-Fi to deliver the economic & social benefits demonstrated over the last 20+ years, particularly in light of potential (real/imagined?) coex threat of LAA/NR-U
    LAA/NR-U stakeholders want to enable fair access to the band using ED-only, rather than the multi-dimensional PD/ED & NAV methods used by Wi-Fi
    Regulators want to promote innovation as well as tested efficient/fair use of spectrum
  It has proven very difficult to find a good middle ground between these needs … with the status quo in the current draft EN 301 893 clearly representing a compromise rather than an ideal solution

## Slide 4: A compromise was eventually found that balanced the needs of proponents of both legacy & new technologies
  The compromise in the current draft of EN 301 893 is
    Any technology may use EDT @ -72 dBm (scaled)
    As an exception, an 802.11a/n/ac/ax compliant device may use EDT @ -62 dBm to account for these devices also using PD @ -82 dBm
  This status quo was the result of a hard fought compromise between diverse stakeholders in which everyone was a little unhappy
  The most important aspect of the compromise is that, on average, it was believed to provide fair & efficient spectrum access to:
    Legacy Wi-Fi equipment using traditional PD/ED mechanisms
    Other equipment (inc 802.11be) using ED-only mechanisms
  The access is not ideal in other ways but it appears to be reasonable overall, based on many simulations over many years in 3GPP RAN, ETSI BRAN, etc

## Slide 5: The discussion that led to this compromise has had positive outcomes for Wi-Fi & coexistence generally
  The discussions over the years in ETSI BRAN and elsewhere that led to this compromise in Europe have had positive outcomes for Wi-Fi & coexistence in the 5 GHz band globally
  By direct & indirect influence, the discussions caused 3GPP RAN to specify LAA/NR-U use EDCA-like access with Wi-Fi compatible timing parameters
    Albeit with LAA & NR-U using the one dimensional “listening” approach based on ED-only @ -72 dBm…
    … rather than Wi-Fi’s multi-dimensional “listening” approach with PD/ED @ -82/-62 dBm along with NAV based reservations (including RTS/CTS)
  This means Wi-Fi & LAA/NR-U can coexist reasonably well “on average”
    Heterogenous access means that there are some undesirable edge conditions
    The non-use of NAV by LAA/NR-U causes hidden station issues, as shown by the University of Chicago measurements (11-20-1973, 11-21-1858-01)

## Slide 6: Qualcomm et al are now challenging that compromise because of a perceived 802.11ax/be coex issue
  An important element of the compromise is that 802.11be will be unable to make use of the exception, forcing it to use EDT @ -72 dBm (scaled)
    This came about because some stakeholders were not happy that new 802.11 equipment would continue to have the, so called, “10 dB advantage” over LAA/NR-U despite there being no evidence any advantage exists in practice
    Most Wi-Fi stakeholders accepted this constraint on 802.11be in the knowledge that EN 301 893 could be changed as more information became available
  However, recently Qualcomm et al expressed a concern that the compromise would result in 11ax having an “advantage” over 11be
    The simulation evidence used to make this assertion is contentious ...
    … contradicting evidence over some years in 3GPP RAN & ETSI BRAN simulations, and recent HPE & CableLabs submissions
  In an attempt to avoid their feared outcome, Qualcomm et al proposed that the constraint in current draft of EN 301 893 be relaxed to an EDT @ -62 dBm for all technologies, at all times

## Slide 7: Qualcomm et al’s proposed solution fixes the 11be/ax issue but ignores the original Wi-Fi/NR-U/LAA coex issue
  The issue with Qualcomm et al’s proposal for EDT @ -62 dBm is that it is believed by many that EDT @ -62 dBm results in poor sharing
    This assumes multiple technologies are attempting to share a 5 GHz channel …
    … because there would be no problem if Wi-Fi was the only technology used …
    … but that seems unlikely, with LAA/NR-U/SL-U/etc in the pipeline
  As BRAN(20)1070321 (9/2020) noted, EDT @ -62 dBm is a bad idea:
    Many 3GPP simulations show that another system using ED-only @ -62 dBm while Wi-Fi uses PD/ED @ -82/-62 dBm is bad for sharing!
    UofChicago/UoW results show the best use of spectrum occurs with symmetric detection between devices at -82 dBm (using some sort of common detection)
    Various simulations from Ericsson & Nokia (in BRAN) confirm better coexistence and spectrum use generally occurs at EDTs well below -62 dBm
  The positive attributes of Qualcomm et al’s proposal are it is simple & treats all technologies uniformly … potentially at the cost of efficient spectrum use, effective sharing & technology neutrality

## Slide 8: A revaluation suggests various viable options, but they probably exclude Qualcomm et al’s proposal
  At this point, it seems useful to compare & contrast the pro/cons & unknowns of various options for access requirements in EN 301 893
  The main options discussed by various groups over the years and recently are:
    Status quo in draft version of EN 301 893
    Adopt EDT @ -62 dBm for all technologies (Qualcomm et al proposal)
    Expand the exception to cover 802.11be
    Status quo in draft version of EN 301 893, with an expiry date on the HS to force BRAN to continue considering new information for a new revision
    Transition to EDT @ -72 dm (scaled) for all technologies with an expiry date within the HS for the use of the exception by 802.11a/n/ac/ax
  The following pages suggest the options marked in:
    Green options are probably viable
    Orange options may not be viable

## Slide 9: The status quo provides a balance of sharing, efficient spectrum use & technology neutrality
Status quo
EDT @ -72 dBm (scaled)
EDT @ -62 dBm exception for 802.11a/n/ac/ax equipment
Pro
Con
Unknown
Good sharing between LAA/NR-U vs 802.11a/n/ac/ax
Promotes spectrum efficiency via lower EDT
Enables continued operation of legacy 802.11
Promotes technology neutrality by enabling multiple sharing mechanisms
Consistent with exception for 802.11 that has existed in EN 301 893 for years
No testing of 802.11a/n/ac/ax compliance
Contrary to desire of some regulators to avoid exceptions
Disagreement on sharing between 802.11be & 802.11a/n/ac/ax
  Evidence has been provided that shows here is a problem …
  … and also there is not a problem!
VIABLE
Status quo

## Slide 10: EDT @ -62 proposal results in inefficient spectrum use & unfair access across technologies
Adopt EDT @ -62
Adopt EDT @ -62 dBm for all technologies
Pro
Con
Unknown
Simple, including simple testing
Uniform rules for all technologies
Guarantees fair access between 802.11 technologies (11ax/be)
Inefficient use of spectrum
Other technologies (including LAA/NR-U) will have better access compared to Wi-Fi
Not technology neutral because biased against sophisticated, multi-dimensional access methods (used by Wi-Fi)
Explicitly violates agreement that resulted in status quo compromise – breach of trust!
Difficult to reverse!
Will LAA/NR-U or other technologies be deployed?
If not then this is a great solution!
If so then this is a terrible solution
Will LAA/NR-U or other technologies use EDT @ -62?
If not then this is a great solution
If so then this is a terrible solution
… but who knows for either question?
Qualcomm et al proposal
VIABLE?

## Slide 11: Various submissions have been made to Coex SC about ED-only @ -62 dBm viability
Submissions to IEEE 802.11 Coex SC
  Not viable: 11-21-0705-00 (May 2021) - Gaurav Patwardhan (HPE) et al
  Viable: 11-21-0851-00 (May 2021) - Menzo Wentink (Qualcomm)
    The underlying concern is that 802.11be using EDT @ -72 dBm will be disadvantaged compared to 802.11ax using PD/ED @ -82/-62 dBm
    The LAA/NR-U proponents are similarly concerned that 802.11ax will have a “10 dB advantage”, despite all the evidence from 3GPP sims
  Not viable: 11-21-1179-00 (July 2021) - Stuart Strickland (HPE)
  Not viable: comments included in agenda (Sep 2022) - Stuart Strickland (HPE)

## Slide 12: Various submissions have been made recently to ETSI BRAN about ED-only @ -62 dBm viability
Recent submissions to ETSI BRAN suggesting viability
  BRAN(22)114022 (Jun 2022) – Wentink (Qualcomm)
  BRAN(22)115019 (Sep 2022) – Wentink (Qualcomm)
  BRAN(22)115020 (Sep 2022) – Wentink (Qualcomm)
  BRAN(22)115021 (Sep 2022) – Wentink (Qualcomm)
  BRAN(22)116014 (Oct 2022) – Wentink (Qualcomm)
  BRAN(22)116015 (Oct 2022) – Wentink (Qualcomm)
  Proposal: BRAN(22)116001r2 (Nov 2022) - Qualcomm, Meta, Vivo, BMWK, Huawei, Sennheiser, MaxLinear
  BRAN(22)116b003 (Oct 2022) – Menzo Wentink (Qualcomm)
    Issues with 5 GHz EDT clauses
    11 issues with current version of EN 301 893 asserted, mostly related in some way with the EDT issue

## Slide 13: Various submissions have been made recently to ETSI BRAN about ED-only @ -62 dBm viability
Recent submissions to ETSI BRAN suggesting lack of viability
  BRAN(22)116b003 (Nov 2022) – Strickland (HPE)
    Examination of conditions under which a compromise may be achievable on EDT in 5 GHz,
  BRAN(22)116b004 (Nov 2022) – Myles (Cisco)
    Should EN 301 893 adopt EDT @ -62 dBm?
    Outlines various options and proposes some version for status quo
  BRAN(22)116c005 (Nov 2022) - Verma et al (Broadcom)
    Choice of detection mechanisms and thresholds in EN 301 893
    Critique of simulations underlying the claim for EDT @ -62 dBm
  …

## Slide 14: Various submissions have been made recently to ETSI BRAN about ED-only @ -62 dBm viability
Recent submissions to ETSI BRAN suggesting lack of viability
  …
  BRAN(22)116c006 (Nov 2022) – Boldy (Broadcom)
    Proposals for 5 GHz EDT
    Proposed two paths to eventually achieve EDT @ -72 dBm
  BRAN(22)116c007 (Nov 2022) - Leisse (CableLabs)
    Scaling parameter for EDT
    Proposes fix for scaling issue
  BRAN(22)116c008 (Nov 2022) - Verma et al (Broadcom)
    Summary of detection mechanisms and thresholds in EN 301 893
    Discusses the choice of an appropriate detection mechanism and threshold in EN 301 893

## Slide 15: Expanding the status quo to include an 802.11be exception works well but is a breach of trust!
Expand exception
Expand the exception in the status quo to cover 802.11be
Pro
Con
Unknown
Same as status quo
Resolves Qualcomm’s concerns related to coex between 802.11ax & 802.11be
Same as status quo
Explicitly violates agreement that resulted in status quo compromise – breach of trust!
Contrary to desire of some regulators to avoid more exceptions
Same as status quo
Note: this option is not possible at this time because 802.11be spec does not exist in a form that can be referenced
VIABLE?
Previous proposed compromise

## Slide 16: An expiry date on the status quo forces BRAN to evaluate incoming evidence in a timely manner
Status quo with expiry
Same as status quo with an expiry date for HS to force BRAN to continue considering new information for a new revision
Pro
Con
Unknown
Same as status quo
Forces BRAN to revise EN 301 893 by expiry date based on new info as 802.11be is defined & various LAA/NR-U/SL-U/etc systems are deployed, inc.:
  Further simulations
  Measurement data
Same as status quo
Same as status quo
Note: there is precedent for expiry dates on HS’s
Note: an expiry date probably need to be 3 years to provide sufficient time to gather data & act upon it
VIABLE
Proposal for new compromise

## Slide 17: A transition to EDT @ -72 dBm (scaled) is a balanced approach that focuses on simplicity & consistency
Transition to EDT @ -72
Transition to EDT @ -72 dm (scaled) for all technologies, timing out the 802.11a/n/ac/ax exceptions in HS after a certain date
Pro
Con
Unknown
Good sharing between LAA/NR-U vs 802.11 before & after transition
Simple, including simple testing after transition
Consistent rules for all technologies after transition
Promotes less interference via lower EDT
Consistent with 6 GHz rules
No testing of 802.11a/n/ac/ax compliance before transition
Forces complicated & potentially risky changes to new 11a/n/ac/ax products after transition (but this has advantage of encouraging shift to 802.11be)
When is an appropriate date? Maybe 3 years to provide sufficient time
VIABLE
Proposal for new compromise

## Slide 18: Conclusion: some version of the status quo for EN 301 893 is probably the best starting point
  Most of the options discussed on the previous pages:
    Enable good coexistence between new & old technologies
    Enable good spectrum efficiency
    Provide a future path for revision as new information becomes available
  In contrast, Qualcomm et al’s proposal
    Guarantees good coex between 11ax/11be
    Provides poor coexistence between new & old technologies
    Provides poorer spectrum efficiency
    Closes the door to future revision (at least without significant pain)
  Each of the various options have pro/cons but the best choice at this time is probably to maintain some version of the status quo as a starting point
    In addition to the positive attributes above …
    … it maintains the trust between everyone who developed it

## Slide 19: Discussion during ETSI BRAN#116c was contentious with no immediate consensus
  The discussion about the EDT @ -62 dBm proposal was contentious
  Some want to take it to vote in ETSI BRAN
    Votes are very unusual in BRAN
    Most people are unenthusiastic about a vote, although one has been pre- announced for BRAN#117
    A report is being written (by Chair) to provide evidence of lack of consensus, and so the need for a vote
  Other discussions suggested an alternative that focuses on getting to EDT @ - 72 dBm ASAP

## Slide 20: The SC will (hopefully) discuss the ETSI BRAN issue related to EDT @ -62 dBm
Some potential questions to discuss:
  Will 802.11ax (using PD/ED @ -82/-62 dBm) have an advantage over 802.11be (using EDT @ -72 dBm) under the current rules in the draft of EN 301 893?
    Continuation of Coex SC discussions from last year
  Will LAA/NR-U (or any other technology) ever take advantage of EDT @ -62 dBm in 5 GHz?
    Requires predicting working in 3GPP RAN, and other forums
    Requires predicting market direction
  Would it be better to transition the 5GHz band in Europe to EDT @ -72 dBm (like 6 GHz) for all technologies?
    Increased spectrum efficiency and more equitable access
  …