## Slide 1: Timestamp Discussion
Date: December 05, 2022
Author:
Notes: This presentation is making the assumption that a sensing measurement timestamp is necessary. Contribution 3 of the memo was the “Should vs Shall” discussion. If you believe that it will take several slides to illustrate what is lost by not having a timestamp at all, or by the timestamp being optional, then it would be better to have a second contribution about the “what if we didn’t have any timestamp”.
This contribution combines the TX discussion with the RX discussion, which was contributions 1 and 2 from the memo. https://qipworks.box.com/s/ccsiiwcbcl413byixdyd06emmr0e0963

## Slide 2: Abstract
Collect member feedback for PDT development on:
  Need for measurement timestamp
  Timestamping at Receiver vs Transmitter
  Timestamp Generation

## Slide 3: Topic 1: Need for Measurement Timestamp

## Slide 4: Topic 1: Need for Measurement Timestamp
TB measurement instance schedule based on Availability Window, which can occur anywhere within negotiated 10ms interval.
non-TB measurement instance schedule based on whenever the medium is available with constraint of “a minimum time interval”
Timestamp is useful to accurately place measurements on time axis, which will improve ability for application to measure doppler [1].

## Slide 5: Topic 1: Need for Measurement Timestamp
For DMG “reference timestamp” field always present in Sensing Report Header sub element
Design options for non-DMG:
    Timestamp is always present in report
    Application negotiates optional presence of timestamp
    Inclusion is implementation decision, signaled through capability bits
If timestamp is always present, no complexity added to signal or negotiate its inclusion, and we align DMG and non-DMG reports
Sensing Measurement Report field can be as large as 40416 bytes [3], so tradeoff of overhead of (1) vs (2)/(3) is small
Given application benefits from timestamp, preference is (1)

## Slide 6: Topic 2: Timestamp at Transmitter or Receiver
(b.1) Timestamp Derived by Receiver
(b.2) Timestamp Derived by Transmitter
Sensing Receiver
Sensing Transmitter
Sensing Receiver
Sensing Transmitter
1
2
3
1
2
(1) Build Measurement Report
- Add corresponding RX Timestamp
(2) Output Received Report
- Deliver output to Sensing Application
(1) Record TX timestamp
- Maintain lookup table mapping identifier to TX timestamp
(2) Build Measurement Report
- NO Timestamp in report
(3) Obtain TX timestamp from (1) given identifier in report
- Deliver output to Sensing Application

## Slide 7
Evaluation | RX Timestamp | TX Timestamp
No over-the-air report | Sensing Receiver must generate timestamp | Sensing Transmitter unable to generate timestamp
Report Overhead | Extra overhead required in report, however report size is already LARGE. | Overhead saved in report, however report size is LARGE, resulting in negligible savings
SBP Handling | No extra processing or manipulation of Sensing Measurement Report by AP to add timestamp. | AP will need to manipulate Sensing Measurement Report to insert timestamp before sending to SBP Initiator.
R2R Handling | Extra overhead required in report, however report size is already LARGE. | Report will be generated by R2R receiver and delivered to AP. AP will need to manipulate Sensing Measurement report to insert timestamp.
In cases where no over-the-air report is required, Sensing Receiver will generate timestamp
Adding complexity to timestamp on Sensing Transmitter saves overhead of including timestamp in report, however savings is minimal given total report may span multiple MPDUs.
In SBP cases where AP is Sensing Transmitter, a TX timestamp would require AP to manipulate received report and insert timestamp before forwarding to SBP initiator.
In R2R case, Sensing Transmitter may not have opportunity to add timestamp into report. As a result, AP would need to manipulate report to insert timestamp before forwarding to application.
Topic 2: Timestamp at Transmitter or Receiver
To unify all reporting flows, having the receiver timestamp the measurement and include it in the report is the simplest and most consistent.

## Slide 8: Topic 3: Timestamp Generation
It is not required that the sensing application receive timestamps fully synchronized among all participants
For measuring the doppler, the delta timestamp from each STA is important
An additional level of clock synchronization beyond the TSF clock management is NOT required for participating STAs
  Existing mechanisms already defined in .11 specs for both associated and non-associated STAs

## Slide 9: Topic 3: Timestamp Generation
Proposal:
  The timestamp can be derived from the STAs local clock with the same resolution and accuracy/drift as its existing TSF clock
    1us resolution, and +/- 100ppm accuracy
  A 4-byte timestamp can be used like the DMG report format
  Associated STAs may synchronize their timestamp relative to the AP’s clock by using the TSF in Beacon frames
  Non-Associated STAs may synchronize their timestamp relative to the AP’s clock by using the Partial TSF in the Trigger/NDPA (defined in 11az and required to keep synchronization with the Availability Window)
    Initial AP TSF may be obtained via beacon or probe request.
    The Partial TSF defined in 11az is 16-bits and represent TSF[21:6], which provides a resolution of 32us.
    Partial TSF may be used to help maintain synchronization to AP time

## Slide 10: SP1
Do you agree to the following design approach:
  Timestamp is always present in Sensing Report
  Timestamp is generated by Sensing Receiver
  Timestamp is generated from local clock of STA:
    Same resolution, and accuracy/drift requirements as TSF
      1us resolution with +/- 100ppm
    Same width as DMG reported timestamp (4 bytes)
    Associated STAs may synchronize their timestamp relative to the AP’s clock by using the TSF mechanisms
    Non-Associated STAs may synchronize their timestamp relative to the AP’s clock by using the Partial TSF in the Trigger/NDPA
Yes/No/Abstain

## Slide 11: References
[1] D. Yang, T. Wang, Y. Sun and Y. Wu, "Doppler Shift Measurement Using Complex-Valued CSI of WiFi in Corridors," 2018 3rd International Conference on Computer and Communication Systems (ICCCS), 2018, pp. 367-371, doi: 10.1109/CCOMS.2018.8463285.
[2] 11-20-1712-02-00bf-wifi-sensing-use-cases.xlsx
[3] 11-22-1020-05-00bf-pdt-formatting-of-csi.docx