## Slide 1: Re WUR, MC-OOK, and multicarrier signals
Date: 2022-11-30
CIDs addressed: LB 270 CIDs 3067-3068, 3070-3072, 3095-3096, 3283, 3458
r0 (November 30, 2022): Initial draft

## Slide 2: Abstract
Clause 30 (Wake-Up Radio PHY specification) requires a WUR non-AP STA to be able to receive WUR PPDUs at given power levels.
But what is a WUR PPDU? This is not clear.
In particular:
  A WUR PPDU contains a component that is called “MC-OOK”
  “MC-OOK” stands for “multicarrier on-off keying”
  But the normative requirements say only that “MC-OOK” should be generated as (one kind of) a multicarrier signal—implying that other choices are permissible
  Other sections say that MC-OOK is a multicarrier signal, but without corresponding normative language saying that it shall be
  WUR non-AP STAs are required to be able to receive any compliant WUR PPDU, including PPDUs that do not follow the multicarrier format—even though the spec strongly suggests that this is the only format required to be received
It is essential for the specification to provide adequate notice to potential implementers on what is required of a compliant portion; the current draft does not do this.

## Slide 3: Summary
Slides 4-6 review what is (or seems to be) required under the spec as it is
Slides 7-9 review MC-OOK and its associated “should” statements
Slides 10-11 review MC-OOK and “multicarrier” and their associated descriptive statements
Slide 12 reviews Annex AC
Slides 13-21 review the CIDs and the proposed resolutions
Slide 22 provides a (brief) summary
Note—for slides 4-12, cf. doc. IEEE 802.11-22/1035r1, “Proposed TGme Comment Resolution CID 2346”, J. Levy, September 2022 (similar and consistent, but not identical)

## Slide 4: Requirements—I
A WUR non-AP STA is required to be able to receive WUR PPDUs at given power levels:
(D2.0 4608)
Other WUR non-AP STA requirements are in the following subclauses (adjacent channel rejection, nonadjacent channel rejection, receiver maximum input level, CCA sensitivity)

## Slide 5: Requirements—II
A WUR PPDU is required to satisfy several transmit requirements (D2.0 4604 →):
“30.3.12 WUR transmit specification
30.3.12.1 Transmit spectrum mask
… For operation using 20 MHz channel spacing, the transmitted spectrum of the WUR-Sync and WUR-Data fields shall have a 0 dBr […] bandwidth …
The transmitted spectral density of the WUR-Sync and WUR-Data fields of the transmitted signal shall fall within the spectral mask … [Similar requirements for 40 MHz, 80 MHz, & preambles]”
“30.3.12.2 Spectral flatness
… The requirement is that the power in any 1 MHz segment, within the center 4 MHz, is in the range of [Pave – 6 dB, Pave + 3 dB]”
30.3.12.3 Transmit center frequency and symbol clock frequency tolerance
The symbol clock frequency and transmit center frequency tolerance shall be ±20 ppm maximum. The transmit center frequency and the symbol clock frequency for all transmit antennas and frequency segments shall be derived from the same reference oscillator.”

## Slide 6: Requirements—III
Transmit requirements, contd.:
“30.3.12.4 Transmit On and Off Symbols power ratio
For each input bit of the WUR-Data field transmitted at WUR HDR, the ratio between the averaged power of the On Symbol and the averaged power of the Off Symbol of the transmit signal in the WUR-Data field shall be at least 20 dB.
For each input bit of the WUR-Data field transmitted at WUR LDR, the ratio between the averaged power over On Symbols and the averaged power over Off Symbols of the transmit signal in the WUR-Data field shall be at least 20 dB.
For the WUR-Sync field transmission, the ratio between the averaged power over all On Symbols and the averaged power over all Off Symbols in the WUR-Sync field shall be at least 20 dB.
For FDMA transmission, the above requirement on the transmit On and Off Symbols power ratio applies to each 20 MHz channel.”
It seems that these are the only “shall” requirements on the transmitted signal.
Note that none of these requirements refer to a multicarrier format.

## Slide 7: MC-OOK “should” statements—I
“30. Wake-Up Radio (WUR) PHY specification(11ba)
30.1 Introduction
… The multicarrier signal should be generated using contiguous 13 subcarriers, centered within a 20 MHz channel, with a subcarrier spacing of 312.5 kHz and the center subcarrier (#1131)being null. The subcarrier coefficients may take values from the BPSK, QPSK, 16-QAM, 64-QAM, or 256-QAM constellation symbols …”
“30.3.4.1 WUR Basic PPDU waveform generation for WUR-Sync field and WUR-Data field with WUR HDR
For a single 20 MHz WUR channel, the 2 µs duration MC-OOK On Symbol should be constructed by the On-WG using (#1137)the center 13 subcarriers of a 64-point IDFT, sampling at 20 MHz as follows:
For a single 20 MHz WUR channel, the 2 µs duration MC-OOK Off Symbol should be constructed by the Off-Waveform Generator (Off-WG) as zero for 2 µs.
With the 2 µs duration MC-OOK On and Off Symbols, the PPDU should meet the Correlation test defined in 30.3.12.5 (Correlation test on MC-OOK symbols).”

## Slide 8: MC-OOK “should” statements—II
“30.3.4.2 WUR Basic PPDU waveform generation for WUR-Data field with WUR LDR
For a single 20 MHz WUR channel the 4 µs duration MC-OOK On Symbol should be constructed by the On-WG using (#1139)the center 13 subcarriers of a 64-point IDFT, sampling at 20 MHz as follows:
— The 12 subcarriers with subcarrier indices k = (–6, –5, … –1, 1, 2, … 6) are used with nonzero input. Other subcarriers are null. …
For a single 20 MHz WUR channel the 4 µs duration MC-OOK Off Symbol should be constructed by the Off-Waveform Generator (Off-WG) as zero for 4 µs.
With the 4 µs duration MC-OOK On and Off Symbols, the PPDU should meet the Correlation test defined in 30.3.12.5 (Correlation test on MC-OOK symbols).”

## Slide 9: MC-OOK “should” statements—III
“30.3.4.3 WUR FDMA PPDU WUR-Data field waveform generation
The MC-OOK On Symbol for the 20 MHz WUR waveform should be generated according to 30.3.4.1
(WUR Basic PPDU waveform generation for WUR-Sync field and WUR-Data field with WUR HDR) or
30.3.4.2 (WUR Basic PPDU waveform generation for WUR-Data field with WUR LDR) depending on
WUR_DATARATE. The 40 MHz or 80 MHz WUR FDMA PPDU should be generated by multiplexing
multiple 20 MHz WUR waveforms in the corresponding channel as shown in Figure 30-8 (An example of a WUR-Data field signal generator for the FDMA transmission(11ba)).
“30.3.8 Mathematical description of signals
For the MC-OOK On Symbols in the WUR-Sync field (WUR-Sync On Symbols) and the MC-OOK On Symbols in the WUR-Data field (SymLDROn and SymHDROn), the baseband signal should be obtained by taking the Inverse Discrete Fourier Transform (IDFT) of a set of subcarrier coefficients, which is described by Equation (30-3).”
“3.10.2 WUR-Data field for WUR LDR and WUR HDR
… SymLDROn and SymHDROn should be generated using contiguous 13 subcarriers …
…The subcarrier coefficients may take values …”

## Slide 10: MC-OOK descriptive statements—I
“3.2 Definitions specific to IEEE Std 802.11
… multicarrier on-off keying (MC-OOK) symbol: (#2242)Either an MC-OOK On Symbol where the multicarrier signal is present or an MC-OOK Off Symbol where no signal is present.(11ba)
multicarrier signal: A(#2242) signal that is constructed with multiple subcarriers.(#2241)(11ba)
“30. Wake-Up Radio (WUR) PHY specification(11ba)
30.1 Introduction
The WUR PHY uses the multicarrier on-off keying (MC-OOK) modulation for (#1128)WUR-Sync and
WUR-Data fields. … MC-OOK is on-off keying, modulated with a multicarrier signal.”
“30.3.7 Timing related parameters
Table 30-3 (Timing-related constants(11ba)) defines the timing-related parameters for WUR PPDU formats. …
Parameter Value Description
F,WUR 312.5 kHz Subcarrier frequency spacing for WUR PPDU

## Slide 11: MC-OOK descriptive statements—II
“30.3.8 Mathematical description of signals
… This general representation holds for WUR-Sync and WUR-Data fields, and the field specific parameters are provided in Table 30-5 (Field specific parameter values for the MC-OOK symbols in WUR-Sync and WUR-Data fields(11ba)) …
{ XField(k), -6  k  6 } are the field specific subcarrier coefficients,
Table 30-5—Field specific parameter values for the MC-OOK symbols in WUR-Sync and
WUR-Data fields(11ba)
Parameter WUR-Sync field WUR-Data field
SymLDROn SymHDROn
NToneField 6 12 6”

## Slide 12: Annex AC
“Annex AC(11ba)
(informative)
Examples of WUR MC-OOK Symbol Design and CSD Design
Subclauses 30.3.4.1 (WUR Basic PPDU waveform generation for WUR-Sync field and WUR-Data field with WUR HDR), 30.3.4.2 (WUR Basic PPDU waveform generation for WUR-Data field with WUR LDR), and 30.3.4.3 (WUR FDMA PPDU WUR-Data field waveform generation) provides a description of how the 2 µs duration MC-OOK and 4 µs duration MC-OOK On and Off Symbols might be constructed but does not provide the actual frequency domain sequences for those symbols. This annex provides example sequences for the construction of these symbols.”

## Slide 13: CIDs—I
CID (Commenter) | Clause/ Page | Comment | Proposed Change
3067 (John Coffey) | 30.1 / 4579.7 | "Clause 30 ... specifies the PHY entity for ... Multi-Carrier On-Off Keying (OOK)". But does Clause 30 do this? Clause 30 defines the PHY entity for wake-up radio (WUR), and the rest of this introductory subclause mentions only "WUR PHY", until we get to 4579.53: "The WUR PHY uses the multi-carrier on-off keying (MC-OOK) modulation for WUR-Sync and WUR-Data fields". But this bare assertion is not supported by the rest of the clause. The same paragraph goes on to say that the "multicarrier" signal "should" be generated using 13 contiguous subcarriers, but (as far as I can see) never specifies that the WUR PPDU is required to use a multicarrier signal. Instead the detailed version of MC-OOK is offered as an example of a WUR format. This setup causes problems throughout the clause, but the immediate issue on 4579.8 is that the clause isn't specifying the PHY entity for MC-OOK: it is specifying (rather loosely!) the PHY entity for WUR. | Change "multi-carrier on-off keing (MC-OOK)" to wake-up radio (WUR)".

## Slide 14: CIDs—II
CID (Commenter) | Clause/ Page | Comment | Proposed Change
3068 (John Coffey) | 30.1 / 4579.54 | ""The WUR PHY uses the multi-carrier on-off keying (MC-OOK) modulation for WUR-Sync and WUR-Data fields. MC-OOK is on-off keying, modulated with a multicarrier signal". This is descriptive, not normative.Is there any normative statement that says that the WUR PHY shall use a multicarrier signal? The following sentence says that the multicarrier signal "should" be generated by using 13 contiguous carriers. But "should" implies that it is permissible to generate the signal some other way, i.e., that a compliant WUR PHY might not use 13 contiguous carriers, and indeed (it seems) might not use multicarrier keying at all. If so, the first sentence here is misleading. (Note that the proposed change mirrors the last sentence in the paragraph: "The subcarrier coefficients may take values from the BPSK, QPSK, 16-QAM, 64-QAM, or 256-QAM constellation symbols.") | Change "The WUR PHY uses" to "The WUR PHY may use".

## Slide 15: CIDs—III
CID (Commenter) | Clause/ Page | Comment | Proposed Change
3070 (John Coffey) | 30.3.10.2 / 4603.51 | "The encoded binary data shall be modulated using MC-OOK, i.e., encoded bits 0 and 1 shall be represented by Off and On Symbols, respectively." Taken together with the rest of the clause, this is confusing. What are the full requirements for MC-OOK? In particular, how can it be determined that a given device does *not* use MC-OOK? Most of the discussion of MC-OOK is by example of an implementation. The cited sentence has something approaching a definition, if we take the "i.e.," to mean "this is the same thing". But is the intention really that any modulation in which encoded bits 0 and 1 are repreemted by Off and On symbols, respectively is therefore, by definition, an MC-OOK system? Or are there other requirements (e.g., does it even have to be--as specified by a shall statement, not a description--multi-carrier?)? The cleanest definition seems to be in 30.3.12.4 (concerning required power ratio). But that does not involve the (murky) concept of MC-OOK. Regardless of the intention, it seems the middle words don't contribute anything concrete, and could be deleted. | Change "using MC-OOK, i.e.," to "so that".

## Slide 16: CIDs—IV
CID (Commenter) | Clause/ Page | Comment | Proposed Change
3071 (John Coffey) | 30.3.8 / 4596.46 | "This general representation holds for WUR-Sync and WUR-Data fields, and the field specific parameters are provided in Table 30-5". Again, this is descriptive, i.e., it describes something as being true, but not normative, i.e., saying that it has to be true. There do not seem to be normative statements anywhere in the clause that say this has to be true. The previous sentence says that the baseband signal "should" be obtained by taking the IDFT of a set of subcarrier coefficients. This implies that it is permissible for a compliant device to obtain the baseband signal some other way. This is very confusing, bordering on misleading. | Change " This general representation holds for WUR-Sync and WUR-Data fields, and the field specific parameters are provided in Table 30-5 (Field specific parameter values for the MC-OOK symbols in WUR-Sync and WUR-Data fields(11ba))" to "When the baseband signal is generated in this way, the field specific parameters are as shown in Table 30-5 (Field speciifc parameters for the MC-OOK symbols in WUR-Sync and WUR-Data fields when the baseband signal is generated by taking the IDFT of 13 contiguous subcarriers)". Also, change the title of Table 30-5 (4597.37) to "Field speciifc parameters for the MC-OOK symbols in WUR-Sync and WUR-Data fields when the baseband signal is generated by taking the IDFT of 13 contiguous subcarriers".

## Slide 17: CIDs—V
CID (Commenter) | Clause/ Page | Comment | Proposed Change
3072 (John Coffey) | 30.3.8 / 4598.1 | The discussion in this section up to here is very unclear on what a WUR signal is. Elements of the signal are called MC-OOK, without any requirement that they are generated by a multi-carrier signal. A mathematical description of a multi-carrier signal is provided, without any requirement that the WUR sugnal is constructed in this way (there's a "should", but this implies "may do something else"). This is an important issue, because subclause 30.3.13.1 (Receiver minimum input sensitivity) imposes normative requirements on the receiver: it has to be able to receive (any) WUR PPDU with specified reliability at the given levels. For that requirement to have any meaning, there has to be adequate notice of the range of different transmitted signals that the receiver might encounter. This should (at the very least) be spelled out in a note. | Add a second note: "NOTE 2--The transmitter's baseband signal is not required to correspoind to the IDFT of subcarrier coefficients derived from the stated constellations, and is not required to match the descritpion in Equation (30-3). The only normative requirements that apply to the WUR-Sync and WUR-Data fields are provided in subclauses 30.3.12.1 (Transmit spectrum mask), 30.3.12.2 (Spectral flatness), 30.3.12.3 (Transmit center frequency and symbol clock frequency tolerance) and 30.3.12.4 (Transmit On and Off Symbols power ratio). For the avoidance of doubt, elements of WUR PPDUs that are labeled "MC-OOK" in this clause are not required to be "multi-carrier".

## Slide 18: CIDs—VI
CID (Commenter) | Clause/ Page | Comment | Proposed Change
3095 (Joseph Levy) | 3.2 / 2018.43 | The definition of MC-OOK symbol is confusing and is not sufficient: The definition is self referential and MC-OOK symbols are not normatively defined. The 802.11 specification normatively defines the OOK modulation that may be generated using an MC-OOK implementation. But calling these symbols these symbols "MC-OOK symbols" is confusing and incorrect. | Delete the definition

## Slide 19: CIDs—VII
CID (Commenter) | Clause/ Page | Comment | Proposed Change
3096 (Joseph Levy) | 3.2 / 2018.43 | The term MC-OOK is used inconsistently in specification. MC-OOK is used to describe an implementation that can generate the OOK symbols used by WUR using a multi-carrier transmitter. In addition these WUR OOK symbols are referred to as MC-OOK symbols in several locations.in the specification. using the same term to refer to and implementation technique and the modulation symbols is confusing and incorrect. | Use term MC-OOK when referring to the multi-carrier implementation technique for generating the OOK symbols used in WUR. Do not refer to these OOK symbols or modulations using the term MC-OOK as this confuses the implementation technique with the normatively defined symbols and modulations used in WUR. Make the changes provided in 11-22/1035.

## Slide 20: CIDs—VIII
CID (Commenter) | Clause/ Page | Comment | Proposed Change
3283 (Mark Rison) | 30 / - | MC-OOK is just an example way of generating waveforms, but the actual requirements on the OOK used for WUR are not specified | Add a subclause defining the "shall"s for WUR PPDUs, and then give MC-OOK as the "should" way to generate them

## Slide 21: CIDs—IX
CID (Commenter) | Clause/ Page | Comment | Proposed Change
3458 (Mark Rison) | 30 / 4579.1 | MC-OOK is a strange definition. Is MC-OOK symbol different than regular OOK symbols, particularly the definition of MC-OOK OFF symbol sounds rather strange. | Make the changes shown in 22/1035r1

## Slide 22: Summary
The comments raise broadly similar concerns.
The proposed resolutions differ in some ways. Roughly, we can distinguish between two main choices:
(1) Retain the definition of MC-OOK as a defined component of WUR PPDUs, but clarify that “MC-OOK” does not necessarily mean “multicarrier”, or
(2) redefine terms so that “MC-OOK” necessarily means “multicarrier”, but a WUR PPDU does not necessarily contain “MC-OOK” components
In addition, the CIDs point out several instances where the current draft is incorrect, or inconsistent, or confusing, or misleading, or contains superfluous text that muddles distinct concepts together.