## Slide 1: mmWave Phase Feedback
Date: 2022-12-06
Authors:
Name | Affiliation | Address | Phone | Email
Kevin Tsunghan Tsai | Mediatek Inc | 2840 Junction Ave, San Jose, CA 95134, USA |  | kevin.tsai@mediatek.com
Dennis Liu |  |  |  | dennis.liu@mediatek.com
Shuling (Julia) Feng |  |  |  | julia.feng@mediatek.com

## Slide 2: Introduction
Vital sign det. including breathing rate and heart rate detection and can be used in many health applications
Vital sign is one of 11BF use cases [1]
  Health case - remote diagnostics measurements
  of breathing rate, heart rate etc.
STA1
STA2
STA3
AP: Initiator
feedback
feedback
feedback
detection
detection
detection

## Slide 3: Vital Signs Detection
Chest up and down is a small distance variation
  Small distance variations cause radar signal travel different distances and result in phase variations at target bin
  Hence, we propose to add target bin phase as a report type for vital sign detection
velocity
time
Distance
inhale
exhale
Freq
FMCW
time
Range
Mag.
Phase=
Phase=
Phase=
Phase=
time
Phase of bin
inhale
exhale
  FMCW , ,
  =
Find the variation period of target bin can get breathing rate
TX chirp
RX chirp
= ,=
frame0
frame1
frame2
frame3
velocity
Range
Mag.
velocity
Range
Mag.
velocity
Range
Mag.

## Slide 4: mmRadar for Breathing/Heartbeat[2]
This page describe the equation for radar T/Rx Signal for next page’s
The transmitted signal of the FMCW radar can be expressed as
  is the starting frequency of the chirp signal, is the bandwidth, TX is the amplitude of the transmitted signal, (t) is the phase noise, is the width of chirp signal pulse
The distance from the chest to the radar is , is the motion displacement of the chest , d0 is the distance from the radar sensor to the human body ,and the time delay is ,causing by the distance ,where c is the light speed. Then, the received signal is

## Slide 5: mmRadar for Breathing/Heartbeat[2]
The echo signal and the transmission signal are mixed by two orthogonal I/Q channels, and then passed through a low-pass filter to obtain an IF signal
  Detect can get distance
  (t) varies with R(t) phase varies with R(t), the displacement of chest
R(t) will be very small, and it approximates a constant in a single chirp
Multiple chirps should be transmitted in sequence to obtain the chest displacement information, which is equivalent to sampling R(t)

## Slide 6: Vital Sign Report
Vital signs or target bin phase have not yet been defined in 11bf mmWave target report
  Vital sign detections may be obtained by FFT operations on phases of target range bins during a Range-Doppler like processing.
  The processing result is different from the Range-Doppler bitmap report defined in current 11bf mmWave.
    SPEC 9.4.2.326.4 DMG Sensing Targets Report Data subelement
NO | Feedback inform
1 | Range in mm
2 | Range Span
3 | Azimuth in 360/2048 degree
4 | Azimuth Span
5 | Elevation in 360/2048 degree
6 | Elevation Span
7 | Radial Velocity in mm/sec
8 | Azimuth Velocity in (360/2048 degree)/sec
9 | Elevation Velocity in (360/2048 degree)/sec

## Slide 7: mmRadar for Breathing/Heartbeat
Breathing Detection test
  Using phase variation to calculate breathing rate
FFT
Breathing rate~=17 per min

## Slide 8: Summary
Vital sign detection is one of 11BF use cases
Propose to add (E)DMG report elements for vital sign detection
  Add phase or vital sign(breathing rate or heartbeat) feedback in target report

## Slide 9: Reference
[1] 11-20-1712-01-00bf-wifi-sensing-use-cases
[2] Y. Wang, W. Wang, Mu Zhou, A. Ren, Z. Tian, “Remote Monitoring of Human Vital Signs Based on 77-GHz mm-Wave FMCW Radar”, Sensors, 2020