## Slide 1: TG bh Clarification of Requirements
Date: 2022-12
Authors:
Name | Company | Address | Phone | email
Graham Smith | SRT Group | Sunrise , FL |  | gsmith@srtrl.com

## Slide 2: PAR
This amendment specifies modifications to the medium access control (MAC) mechanisms to preserve the existing services that might otherwise be restricted in environments where STAs in an Extended Service Set (ESS) use randomized or changing MAC addresses, without affecting user privacy. User privacy includes exposure of trackable information to third parties or exposure of an individual's presence or behavior.
This amendment introduces mechanisms to enable session continuity in the absence of unique MAC address-to-STA mapping. For STAs in an ESS that use randomized or changing MAC addresses, this amendment preserves the ability to provide customer support, conduct network diagnostics and troubleshooting, and detect device arrival in a trusted environment.

## Slide 3: Part 1 – RCM solved what?

## Slide 4: What can we take from the PAR?
The “privacy” requirement is basically what was improved by introducing RCM.
Tracking
Exposure of user identity.
Bottom line is
TGbh solutions must provide, at least, the same privacy that RCM does.

## Slide 5
Tracking and User Identity
Back to the beginning
Presentations were given in WNG back in 2014
These give insight as to the problems that needed solving and as to why RCM happened.

## Slide 6: Wi-Fi Privacy Concerns
Seattle Police Deactivate Wi-Fi Spy Grid After Privacy Outcry (Nov 2013)
  A DHS and Seattle police network collecting location information
CreepyDOL WiFi surveillance project debuts at Blackhat/DEFCON (Aug 2013)
  DIY surveillance with low-cost Wi-Fi based sensors that capture MAC addresses
Wi-Fi Trashcans Now Silently Tracking Your Smartphone Data (Aug 2013)
  ... the company boasted that the cans, which included LCD advertising screens, "provide an unparalleled insight into the past behavior of unique devices"—and hence of the people who carry them around
"Technopanic" mounts over Google's Wi-Fi Privacy violations (Mar 2013)
  A DHS and Seattle police network collecting location information

## Slide 7: Privacy Threats
Source of Threats:
  Hackers, private investigators, stalkers, paparazzi
  Marketing firms and retail outlets
  Police, Government Agencies
Non-threats:
  Marketing firms and retail outlets (with user approval)
  Personal home automation (of home user)
  ... Etc.
It is very important to identify ways to enable tracking when it is a “service”, but prevent unauthorized tracking

## Slide 8: Trash Can Tracking
“…an analytics tool that tracks consumers via their Wi-Fi connected devices... Embedded in the trash cans, the system can detect devices and observe their behavior, using a unique ID code called a MAC address that is embedded in every Wi-Fi enabled gadget. … is accurate down to a 50th of a second, and tracks everything from the speed of pedestrians to what make of phone they’re using.”
“For example, if it knows you're a regular at a certain bar, the cans might show you an ad for a different happy hour at a bar nearby.”
(But maybe the user might like that info? RCM stopped that!)

## Slide 9: RCM solved Trash Can tracking
Not sure if the scheme(s) somehow triggered the STAs to transmit probes, or that STAs just do it anyway OR STAs using local Wi-Fi for ‘normal’ traffic.
Anyhow, RCM solved this
  Changing MAC Address stopped any relationship to user and tracking over a long period.
Bottom line:
A STA should not use a single MAC address for long periods when simply “roaming”
BUT
Returning to a site using the same MAC address
  is “trackable” (11aq?)
  This is present solution for many use cases

## Slide 10: User Identity
Pre-RCM
Long term tracking of phones revealed “the past behavior of unique devices"—and hence of the people who carry them around
BUT Did not directly provide the User Identity unless MAC Address specifically targeted and followed.
  Noting places frequented, including home.
RCM solved this in general but using same MAC Address when returning to ESS (as per 11aq) is a slight breach.
  Take photo of user when MAC Address enters store, (“CreepyDOL”). Tougher if different MAC Address each time.

## Slide 11: Spoof AP attack – Paparazzi
Originally paparazzi set up sniffer(s) at locations to look for known MAC Address(es) of celebrities.
  RCM prevents this
Paparazzi could set up a spoof AP to tempt celebrity to associate.
  Have to know SSID of an ESS that has restricted membership
  Mere attempt to associate is enough to advertise presence
Is it a real privacy problem?
For “paparazzi” maybe substitute Government or criminal concern? But is this a good way to track someone? – Not really

## Slide 12: Spoof AP attack – with RCM
Spoof AP, located at a night club or restaurant, advertises SSID “I’m an Important VIP”
VIP arrives, and phone sends an Association request.
  Association fails - Password does not match
Spoof AP says “Aha, the VIP is here”.
IS this a real problem?
Does NOT provide access, in any way, to the ‘Home” network.
IF (as 11aq) phone uses same MAC Address as last time, makes the paparazzi job easier, but still no real difference.

## Slide 13: Spoof AP
If Spoof AP is a more general “attractive” SSID, still no way to tell who owns what MAC Address.
Then RCM does not solve the general snooping problem if returning STAs using same MAC Address
Note: For a pre-scheme, the “attractive” SSID would have to be one that a STA would want to be pre-recognized. Difficult to imagine a scenario that makes any sense for an attacker.

## Slide 14: Spoof AP
As Spoof AP only partially solved by RCM, does TGbh have to solve it?
  How important is this to the public? i.e., non-celebs.
  How important to celebs?
Presentation in TGbi on possible solution(s) had strong feedback that this is not a problem worth solving.
Hence, TGbh needs to decide how to address “Spoof AP” when considering the pre-schemes.
How important is it?
How much added complexity is justified?

## Slide 15: Summary
RCM :
Solved general tracking of a MAC Address
Made simple sniffers obsolete
RCM did not solve specific “paparazzi spoof AP”, but no-one worries about that?
No scheme, Device ID or Pre-Scheme, solves it.
Break for questions

## Slide 16: Part 2 – Pre-Schemes
How complicated do they need to be?

## Slide 17: Pre-Schemes
Basically 2 basic schemes:
No computations
  MAAD, IRM
  MAC address assigned each association by each ESS.
Computations
  RRCM, IRMA, ID Encoding
  Use a key
  Basically, a random MAC Address and the ID is in an IE.

## Slide 18: Pre-Schemes
Q - Is there any need to encrypt?
e.g., IRMA and ID Encoding
A - Only if Spoof AP is countered
  Which it isn’t
Tracking is solved because random MAC addresses used unless STA is trying to associate to a ‘wanted’ ESS.

## Slide 19: So what is the difference?
MAAD uses MAC Address as the ID
  MAAD is network allocated, IRM is STA allocated.
ID Encoding uses an IE as the ID
  Option to encrypt it.
IRMA uses a Hash in an IE and a key as the ID
RRCM uses encrypted MAC Addresses as IDs.

## Slide 20: MAAD and Spoof AP
A MAAD STA only uses the MAAD MAC Address when it wants to be recognized.
Spoof AP mimics what?
  “home” AP? (Paparazzi)
  “attractive” AP?
Spoof AP knows the MAC Address but does not know the password. What use is it?
The only use is the Paparazzi attack,
  which is easily avoided if you are a celeb.
A MAAD STA may have several MAAD MAC Addresses, they change all the time and do not identify the user.

## Slide 21: Decision?
Why do we need encryption and computation complexity?
If we did, then why did we not just go with IRMA which was almost the first proposal in TGbh?
Tracking is countered by all schemes
  No need for any probing with the ID
Spoof AP is not a real threat.
Simpler the better – Why not? That is the question.