## Slide 1: TG bh Clarification of Requirements
Date: 2022-12
Authors:
Name | Company | Address | Phone | email
Graham Smith | SRT Group | Sunrise , FL |  | gsmith@srtrl.com

## Slide 2: PAR
This amendment specifies modifications to the medium access control (MAC) mechanisms to preserve the existing services that might otherwise be restricted in environments where STAs in an Extended Service Set (ESS) use randomized or changing MAC addresses, without affecting user privacy. User privacy includes exposure of trackable information to third parties or exposure of an individual's presence or behavior.
This amendment introduces mechanisms to enable session continuity in the absence of unique MAC address-to-STA mapping. For STAs in an ESS that use randomized or changing MAC addresses, this amendment preserves the ability to provide customer support, conduct network diagnostics and troubleshooting, and detect device arrival in a trusted environment.

## Slide 3: Part 1 – RCM solved what?

## Slide 4: What can we take from the PAR?
The “privacy” requirement is basically what was improved by introducing RCM.
Tracking
Exposure of user identity.
Bottom line is
TGbh solutions must provide, at least, the same privacy that RCM does.

## Slide 5
Tracking and User Identity
Back to the beginning
Presentations were given in WNG back in 2014
These give insight as to the problems that needed solving and as to why RCM happened.

## Slide 6: Wi-Fi Privacy Concerns
Seattle Police Deactivate Wi-Fi Spy Grid After Privacy Outcry (Nov 2013)
  A DHS and Seattle police network collecting location information
CreepyDOL WiFi surveillance project debuts at Blackhat/DEFCON (Aug 2013)
  DIY surveillance with low-cost Wi-Fi based sensors that capture MAC addresses
Wi-Fi Trashcans Now Silently Tracking Your Smartphone Data (Aug 2013)
  ... the company boasted that the cans, which included LCD advertising screens, "provide an unparalleled insight into the past behavior of unique devices"—and hence of the people who carry them around
"Technopanic" mounts over Google's Wi-Fi Privacy violations (Mar 2013)
  A DHS and Seattle police network collecting location information

## Slide 7: Privacy Threats
Source of Threats:
  Hackers, private investigators, stalkers, paparazzi
  Marketing firms and retail outlets
  Police, Government Agencies
Non-threats:
  Marketing firms and retail outlets (with user approval)
  Personal home automation (of home user)
  ... Etc.
It is very important to identify ways to enable tracking when it is a “service”, but prevent unauthorized tracking

## Slide 8: Trash Can Tracking
“…an analytics tool that tracks consumers via their Wi-Fi connected devices... Embedded in the trash cans, the system can detect devices and observe their behavior, using a unique ID code called a MAC address that is embedded in every Wi-Fi enabled gadget. … is accurate down to a 50th of a second, and tracks everything from the speed of pedestrians to what make of phone they’re using.”
“For example, if it knows you're a regular at a certain bar, the cans might show you an ad for a different happy hour at a bar nearby.”
(But maybe the user might like that info? RCM stopped that, OR DID IT? 11aq uses same address for same ESS)

## Slide 9: RCM (11aq) solved Trash Can tracking?
Not sure if the scheme(s) somehow triggered the STAs to transmit probes, or that STAs just do it anyway OR STAs using local Wi-Fi for ‘normal’ traffic.
Anyhow, RCM solved this
  Changing MAC Address stopped any relationship to user and tracking over a long period.
Bottom line:
A STA should not use a single MAC address for long periods when simply “roaming”
BUT
Returning to a site using the same MAC address
  is “trackable”
  This is present solution for many use cases

## Slide 10: User Identity
Pre-RCM
Long term tracking of phones revealed “the past behavior of unique devices"—and hence of the people who carry them around
BUT did not directly provide the User Identity unless MAC Address specifically targeted and followed.
  Noting places frequented, including home.
RCM solved this in general but using same MAC Address when returning to ESS (as per 11aq) is a slight breach.
  Copying Address is easy (see over)
  Take photo of user when MAC Address enters store, (“CreepyDOL”). Tougher if different MAC Address each time.

## Slide 11: (11aq) Same Address for same ESS
Consider Use Cases 4.1, 4.2 , 4.3
  Steering, Parental, Automation
List of “allowed” MAC Addresses
If “Allowed” STA uses same address each time.
Then “Attacker” (child?) simply notes the MAC address and uses it.
If “attacker STA” has the password, can pretend to be the ‘higher authority”
Copying address is simple
Does this matter??

## Slide 12: Spoof AP attack – Paparazzi
Originally paparazzi set up sniffer(s) at locations to look for known MAC Address(es) of celebrities.
  RCM prevents this
Paparazzi could set up a spoof AP to tempt celebrity to associate.
  Have to know SSID of an ESS that has restricted membership
  Mere attempt to associate is enough to advertise presence
Is it a real privacy problem?
For “paparazzi” maybe substitute Government or criminal concern? But is this a good way to track someone? – Not really

## Slide 13: Spoof AP attack – with RCM
Spoof AP, located at a night club or restaurant, advertises SSID “I’m an Important VIP”
VIP arrives, and phone sends an Association request.
  Association fails - Password does not match
Spoof AP says “Aha, the VIP is here”.
IS this a real problem?
Does NOT provide access, in any way, to the ‘Home” network.
IF (as 11aq) phone uses same MAC Address as last time, makes the paparazzi job easier, but still no real difference.

## Slide 14: Spoof AP
If Spoof AP is a more general “attractive” SSID, still no way to tell who owns what MAC Address.
But RCM does not solve the general snooping problem if returning STAs using same MAC Address
Note: For a pre-scheme, the “attractive” SSID would have to be one that a STA would want to be pre-recognized. Difficult to imagine a scenario that makes any sense for an attacker.

## Slide 15: Spoof AP
As Spoof AP only partially solved by RCM, does TGbh have to solve it?
  How important is this to the public? i.e., non-celebs.
  How important to celebs?
Presentation in TGbi on possible solution(s) had strong feedback that this is not a problem worth solving.
Hence, TGbh needs to decide how to address “Spoof AP” when considering the pre-schemes.
How important is it?
How much added complexity is justified?

## Slide 16: Summary
RCM :
Solved general tracking of a MAC Address
Made simple sniffers obsolete
RCM did not solve specific “paparazzi spoof AP”, but no-one worries about that?
  No scheme, Device ID or Pre-Scheme, solves it.
Using same MAC Address every time ‘weak’ and easy to copy
Using a different, identifiable MAC address ‘stronger’ prevents simple copying.
Break for questions

## Slide 17: Part 2 – Pre-Schemes
How complicated do they need to be?
If “same MAC Address every time” effectively works, but is easily copied, then how complicated do we need to get?

## Slide 18: Pre-Schemes
2 basic schemes:
No computations
  MAAD, (IRM)
  MAC address assigned each association by each ESS.
Computations
  RRCM, IRMA, ID Encoding
  Use a key
  Basically, a random MAC Address and the ID is in an IE.

## Slide 19: Pre-Schemes
Q - Is there any need to encrypt?
e.g., IRMA and ID Encoding
A – Makes copying more difficult
But does not counter Spoof AP
Tracking is solved as Random MACs used

## Slide 20: So what is the difference?
“11aq” uses same MAC Address per ESS every time
MAAD uses different address every ESS, every association
  MAAD MAC is the identifier.
  MAAD is network allocated, IRM is STA allocated.
ID Encoding uses an IE as the ID
  ID changes every association every ESS.
  Option to encrypt it.
IRMA uses a Hash in an IE and a key as the ID
RRCM uses encrypted MAC Addresses as IDs.

## Slide 21: Spoof AP
Spoof AP mimics what?
  “home” AP? (Paparazzi)
  “attractive” AP?
Spoof AP knows the MAC Address but does not know the password. What use is it?
The only use is the Paparazzi attack,
  which is easily avoided if you are a celeb.
A MAAD STA may have several MAAD MAC Addresses, they change all the time and do not identify the user.
MAAD is one step up from 11aq, in that a difference MAC Address used each time when returning, copying is difficult.
ID encoding, IRMA and RRCM can encrypt the ID to make copying even more difficult.

## Slide 22: Decisions?
Is 11aq acceptable?
  Easy to copy
Spoof AP is not a real threat?
Do we need encryption and computation complexity?
  I.e, Is MAAD sufficient?
Agree tracking is countered by all schemes?
  11aq, MAAD, ID encoding, RRCM
How complicated do we need? That is the question.

## Slide 23: Questions/Discussion?
Is (11aq) using same MAC address every time returning to same ESS sufficient?
  No new scheme(s) required (also drop Device ID)
  Same address is easy to know STA/user returning
  Easy to copy for Use Case 4.2 for example.
Is using a different identifiable MAC address (e.g., MAAD) enough?
  Very simple scheme
  Difficult to copy
  Step up in privacy to “11aq same address”
Do we need to add encryption and computations?
  Provides extra protection against copying
  Requires computations

## Slide 24: Finale
Can we make decision?:
Do nothing – simply clarify 11aq text to be clear that every ESS STA uses same MAC Address?
  Delete Device ID
Adopt MAAD MAC scheme in addition to Device ID
  Simple to implement, no computations
  Complement each other
Adopt a more complex scheme, ID Encoding, RRCM, IRMA
  Requires computations
  Device ID? (Does ID Encoding need both?)