## Slide 1: Operation Procedure for AMP device in WLAN
Date: 2022-11-11
Authors:
Name | Affiliation | Address | Phone | Email
Yinan Qi | OPPO |  |  | v-qiyinan@oppo.com
Weijie Xu |  |  |  | xuweijie@oppo.com
Doc.: IEEE 802.11-22/2151r0
December 2022

## Slide 2: Outline
Background of energy harvesting
Energy harvesting: operation procedure, etc.
Doc.: IEEE 802.11-22/2151r0
December 2022

## Slide 3
Background
Yinan Qi (OPPO)
Slide 3
[1] IEEE 802.11-22/1562r3, Draft Technical Report on support of AMP IoT devices in WLAN
Doc.: IEEE 802.11-22/2151r0
December 2022

## Slide 4
Operation Procedure
Yinan Qi (OPPO)
Slide 4
    Solar
    Two categories: with/without energy storage capability
    With energy storage capability
      Operate during day and night
      Device activated periodically during daytime and energy storage charged periodically during daytime with period PD
      Device activated periodically, possibly with longer period with PN, during night
      Flexible configuration can be applied to keep the energy storage is not completely drained.
Day
Night
PD
PN
t
Stored Energy
Device Power
Doc.: IEEE 802.11-22/2151r0
December 2022

## Slide 5
Operation Procedure
Yinan Qi (OPPO)
Slide 5
    Solar
    Without energy storage
      Only operate during daytime
      Device activated periodically during daytime and sleep during night
    Other power sources, e.g., thermal, vibration
    Follow the same power profile characteristics
      Energy source available time, e.g., daytime for solar
      Energy source unavailable time, e.g., night for solar
Day
Night
t
Device Power
Doc.: IEEE 802.11-22/2151r0
December 2022

## Slide 6
RF Power Source
Yinan Qi (OPPO)
Slide 6
    Features
    Higher reliability
    Possible individual power link
    Consistent or periodic power transmission
    On-demand power transmission, e.g., on-demand sensor data reporting
    Procedure
    Power source transmits power signal
    Energy harvester harvests the RF power
    Energy storage is charged
    Main parts of AMP device, e.g., sensors, communication modules, are activated
    Power signal can be enhanced via , e.g., padding
PD
t
Stored Energy
Device Power
Power Source
Periodic Power Tx
On-demand Power Tx
Doc.: IEEE 802.11-22/2151r0
December 2022

## Slide 7: Summary
This submission discusses following aspects of energy harvesting
  Operation procedures of AMP devices for different power sources, e.g., solar, thermal, etc.
  Operation procedure for RF power sources powered AMP devices
Doc.: IEEE 802.11-22/2151r0
December 2022

## Slide 8: Reference
IEEE 802.11-22/1562r3, Draft Technical Report on support of AMP IoT devices in WLAN
Doc.: IEEE 802.11-22/2151r0
December 2022