## Slide 1: Joint Transmission for UHR –A Refresher and New Results
Date: 2022-12-18
Authors:
Name | Affiliations | Address | Phone | email
Ron Porat | Broadcom |  |  | ron.porat@broadcom.com
Srinath Puducheri | Broadcom |  |  | 
Karim Toussi | Broadcom |  |  | 

## Slide 2: Introduction
Joint Transmission (JT) as a candidate technology for 11be has been discussed extensively by many companies.
Investigations showing gains were carried out in various scenarios, with wireless and wired backhaul and included all anticipated synchronization errors and impairments ([1]-[12])
It was accepted for rel. 2 but later on pushed out along with all M-AP technologies.
In this contribution we aim to provide a short refresher of the technology and further show new simulation results.
Interested readers can also refer to [13] published in the IEEE Communications Standards Magazine special issue on Recent and Future Evolution of Wi-Fi whereby we summarized the work done in 11be .

## Slide 3: Joint Transmission
In JT multiple distributed APs work as one big AP.
   more antennas bigger SU/MU-MIMO gain
   signal is coming from multiple locations adds to robustness/reliability/better coverage
Requires information sharing between AP
Requires tight synchronization between AP

## Slide 4: JT – Classification of Gains in UHR
Two types of gains are possible (see also benefit matrix in [14] and discussion in [15]):
Peak Tput – this was our focus in 11be, more antennas enable high number of spatial streams than possible with each AP separately (higher MU-MIMO gains)
Improved rate at range up to the number of streams that each AP can deliver on its own (denote as N).
  As a basis, JT SU clearly benefits from array gain and diversity gain of having more antennas e.g. 2N (for STA in the overlap area in the diagram below).
  And in an extension to JT MU with up to N streams, multiple STA in one or more BSS benefit from the same gains (all STA in the diagram below).
  Furthermore, JT from two separated sources provides a more uniform area SNR
  Lastly, a soft handoff proposed in [16] also fits with this narrative of jointly transmitting to STA(s) in an overlap area
  This second type of gain helps achieve several
  of UHR goals
AP1
AP2
STA11
STA21
STA12
STA22

## Slide 5: JT High Level Operation
MAP- Main AP initiating joint sounding and joint data transmission
AAP – Auxiliary AP estimating residual CFO and timing in order to synchronize to Main AP during joint transmission

## Slide 6: Impairments
The most critical impairment is achieving tight CFO estimation between the Aux and Main APs – unlike other transmission modes, during joint transmission the Aux AP is not tracking the frequency offset relative to the Main AP  any residual estimated CFO will contribute to phase offset growing linearly with time.
Proposed solutions:
  Super fine CFO estimation e.g 20Hz offset → 7.2 degrees after 1mS. This is necessary but insufficient for longer packets (>1mS)
  Adding a mid-packet sync symbol every e.g. 1mS to enable the Aux AP to re-estimate the phase difference
  Aux AP constantly tracking master AP during JT transmission on a different band (assuming the same reference oscillator for both bands). The tracking loops output on the Rx band is used to adjust the CFO estimate on the Tx band.
Furthermore, impairment impact is reduced with link imbalance between STA and Main and Aux AP

## Slide 7: Super Fine CFO Estimation
At its core CFO estimation accuracy is proportional to the gap between two repeated symbols
  In the legacy preamble there is no gap between the LTF symbols (denote here as 0uS) but we can design for a larger gap
Below are results for the 90th percentile residual CFO error for 11nD channels, 80MHz with two 4x4 AP.
Note:
  The above results assume ideal LOs at all APs with zero phase-noise.
  In practice, the estimation accuracy will have a positive lower-bound, depending on the phase-noise characteristics of the APs, in the limit as LTF-separation  ∞.
‘fine’ CFO error [Hz]- two LTF with separation: 0us |  | 
Config | SNR=10dB | SNR=20dB
1x LTF | 678 | 211
2x LTF | 252 | 80
4x LTF | 86 | 30
‘super fine’ CFO error [Hz] - two LTF with separation: 100us |  | 
Config | SNR=10dB | SNR=20dB
1x LTF | 26 | 8.2
2x LTF | 18 | 6
4x LTF | 12 | 3.8

## Slide 8: Other Impairments
Tx gain fluctuation from sounding time to payload transmission time [6]
Phase drift:
      Timing errors (acquisition error) – Aux AP acquiring packet is not identical between the sounding and data transmission. These are manifested as a linear phase drift across frequency.
      Common phase drift due to different RF clocks and phase noise between the Main and Aux AP (this is a similar estimation problem as the mid-packet sync symbol)
      Both these issues can be readily solved by simple signal processing comparing phases of the new channel vs. ref channel (as shown in slide 5).
    The resulting residual errors of these two impairments proved less impactful than the residual CFO error and are included in our simulations

## Slide 9: Impact of Path Loss Difference – ‘X’
Based on Appendix B in ref [4].
X: additional path-loss (dB) seen between AP ‘j’ and STAs in BSS ‘i’ for
θ: Phase drift during packet
Since the precoder was designed for zero phase offset, there is now residual interference to BSS ‘i’ from BSS ‘j’ spatial streams:
    Observe that, the residual interference power:
      scales up as
      scales down by X dB, e.g.,
        =10 deg with X= 20dB is equivalent to =1 deg with X= 0dB
      vanishes for large X

## Slide 10: Simulations
2-AP (4x4), each with 2 STA (2x2), 80MHz BW, 11nD, SNR range 10:35dB
  “SNR” measured between STA and stronger AP (“serving AP”).
Baseline - single-AP + TDMA:
  Max of DL-MUMIMO Nss=[2 1], DL MU-MIMO Nss=[1 1]
    Nss=[2 1] is the best for SNR > 20dB. Nss=[1 1] is the best for SNR <= 20dB.
JT: AP maintain their power as in baseline. One big MU-MIMO
  4 spatial streams: Nss = [1 1; 1 1]  of interest for rate/range improvement
  6 spatial streams: Nss = [2 1; 2 1]  of interest for peak Tput improvement
Generic impairments:
  Channel aging (-30dBc)
  TxEVM (-35dB, i.e., Tx SNR = -38dBc)
  NDP channel estimation error (no smoothing).
  ZF precoder
  Residual timing estimation error 0.5nS or 1ns (applied as a 14.4 or 28.8 deg phase-ramp edge to edge)
  Gain error 1dB
  Phase offset maximum at 4d or 8d
Simulation output: Throughput ratio (JT/baseline) shown in a 2-D table: f(SNR, X)

## Slide 11: Throughput Ratio: (phase, timing, power) offsets = (4d, 0.5ns, 1db)
Throughput ratio for JT with [4ss, 6ss]
4ss provides best rates up to 20dB SNR
Up to 20dB SNR, low X is helpful (more power from 2AP and less impact from impairments)
At 30dB SNR and higher, impairments dominate and high X is helpful
 |  | Serving AP STA SNR (dB) |  |  |  |  | 
 |  | 35 | 30 | 25 | 20 | 15 | 10
X (dB) | 0 | 1.26, 1.57 | 1.37, 1.71 | 1.61, 1.82 | 1.92, 1.70 | 2.20, 1.65 | 2.25, 1.59
 | 5 | 1.39, 1.60 | 1.48, 1.71 | 1.61, 1.71 | 1.84, 1.46 | 1.92, 1.42 | 1.87, 1.12
 | 10 | 1.52, 1.70 | 1.63, 1.78 | 1.62, 1.74 | 1.83, 1.40 | 1.87, 1.29 | 1.74, 1.07
 | 15 | 1.57, 1.80 | 1.71, 1.87 | 1.68, 1.80 | 1.84, 1.42 | 1.84, 1.29 | 
 | 20 | 1.67, 1.90 | 1.73, 1.92 | 1.73, 1.84 | 1.84, 1.45 |  | 
 | 25 | 1.69, 1.96 | 1.74, 1.94 | 1.76, 1.86 |  |  | 
Region of interest in Enterprise.
Based on [17]

## Slide 12: Throughput Ratio: (phase, timing, power) offsets = (8d, 0.5ns, 1db)
With maximum phase offset increased to 8d the main impact is highlighted at low X
4ss provides best rates up to 20dB SNR and at 25dB with X<10
Up to 15dB, low X is helpful (more power from 2AP and less impact from impairments)
At 25dB and higher impairments dominate and high X is helpful
 |  | Serving AP STA SNR (dB) |  |  |  |  | 
 |  | 35 | 30 | 25 | 20 | 15 | 10
X (db) | 0 | 1.14, 1.33 | 1.28, 1.43 | 1.50, 1.50 | 1.77, 1.51 | 1.99, 1.58 | 2.22, 1.53
 | 5 | 1.17, 1.42 | 1.31, 1.52 | 1.57, 1.52 | 1.76, 1.38 | 1.89, 1.38 | 1.82, 1.10
 | 10 | 1.42, 1.61 | 1.50, 1.69 | 1.60, 1.65 | 1.81, 1.37 | 1.85, 1.28 | 1.73, 1.07
 | 15 | 1.54, 1.75 | 1.68, 1.82 | 1.64, 1.77 | 1.83, 1.40 | 1.84, 1.28 | 
 | 20 | 1.63, 1.86 | 1.73, 1.90 | 1.72, 1.83 | 1.84, 1.44 |  | 
 | 25 | 1.69, 1.95 | 1.74, 1.93 | 1.75, 1.85 |  |  | 

## Slide 13: Throughput Ratio: (phase, timing, power) offsets = (8d, 1ns, 1db)
With further increase of timing error to 1nS the main impact is highlighted at low X
4ss provides best rates up to 20dB SNR and at 25dB with X<=10
Up to 15dB SNR, low X is helpful (more power and less impact from impairments)
At 25dB SNR and higher, impairments dominate and high X is helpful
 |  | Serving AP STA SNR (dB) |  |  |  |  | 
 |  | 35 | 30 | 25 | 20 | 15 | 10
X (db) | 0 | 1.11, 1.26 | 1.25, 1.34 | 1.47, 1.45 | 1.73, 1.45 | 1.97, 1.57 | 2.22, 1.50
 | 5 | 1.16, 1.38 | 1.31, 1.44 | 1.55, 1.49 | 1.73, 1.35 | 1.88, 1.35 | 1.80, 1.10
 | 10 | 1.39, 1.57 | 1.47, 1.65 | 1.60, 1.60 | 1.80, 1.36 | 1.84, 1.28 | 1.72, 1.06
 | 15 | 1.53, 1.73 | 1.66, 1.79 | 1.63, 1.75 | 1.82, 1.40 | 1.83, 1.28 | 
 | 20 | 1.60, 1.84 | 1.72, 1.88 | 1.70, 1.82 | 1.83, 1.43 |  | 
 | 25 | 1.68, 1.94 | 1.74, 1.93 | 1.75, 1.85 |  |  | 

## Slide 14: Summary
We have provided insights into the challenges and potential gains of JT
Gains stem from combining transmit power, added diversity and nulling capability of having multiple AP combine their antennas and power.
It is shown that JT can help fulfil multiple objectives of UHR -
  If AP supports JT with higher Nss than it supports on its own  higher peak Tput
  If AP supports JT with same Nss that it supports on its own  increased robustness and higher rate at range.
    As shown, in certain scenarios and typically low to medium SNR this is optimal.

## Slide 15: References
“Distributed MU-MIMO” IEEE 802.11-18/1439
“Joint Processing MU-MIMO Update” IEEE 802.11-19/384
“Measurements for Distributed-MU-MIMO” IEEE 802.11-19/763
“Comparison of Coordinated BF and Nulling with JT” IEEE 802.11-19/799
“JT performance with Multiple Impairments,” IEEE 802.11-19/1597
“Joint Transmissions: Backhaul and Gain State Issues,” IEEE 802.11-19/1089
“Multi-AP backhaul analysis,” IEEE 802.11-19/1588
“Consideration on Joint Transmission,” IEEE 802.11-19/1595
“Evaluation of joint transmission” IEEE 802.11-19/1092
“Performance of JT with wireless Backhaul” IEEE 802.11-19/1909
“Joint MU Analysis & Simulations” IEEE 802.11-19/1872
“Joint Sounding for Multi-AP Systems” IEEE 802.11-19/1593
“Increasing Spatial Multiplexing Gain in Future Multi-AP WiFi Systems via Joint Transmission” IEEE Communications Standards Magazine
“Next Gen After 11be: Main Directions Proposal” IEEE 802.11-22/734
“Thoughts on Beyond 802.11be” IEEE 802.11-22/932
“Seamless Roaming for UHR” IEEE 802.11-22/1910
“a Perspective On Proposed UHR Features For Enterprise Use Cases” IEEE 802.11-22/1580