## Slide 1: AP MLD Power Management
Date: 2022-11-01
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Kiseon Ryu Huizhao Wang Hongyuan Zhang Rui Cao Yan Zhang Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Recap: Non-AP STA Power Save
Intra-PPDU power save
SM power same
  Dynamic SM power save
  Static SM power save
VHT TXOP power save
Operating mode control
Power management mode:
  Active mode
  Power save mode
    Awake state
    Doze state
U-APSD/APSD

## Slide 3: Recap: Non-AP STA Power Save (Cont’d)
WNM sleep mode
Power save under TWT
Wake TBTT and wake interval
Opportunistic power save
TDLS power save
……

## Slide 4: Recap: AP Power Management
Responder PM mode with individual TWT
S1G AP power management
  Active mode
  Power Save mode
    Doze state
    Awake state

## Slide 5: Recap: MLD Power Save
EMLSR
Link Disabling

## Slide 6: Potential Issues with AP MLD Power Management Mode
The association of non-UHR STA, non-UHR non-AP MLD
The Active probing by non-UHR STA, non-UHR non-AP MLD
Non-HE associated STAs assume that its associated AP are always available for frame exchanges except the quiet SPs

## Slide 7: BSS Deployment and Chip Shipment
An AP can control the PHY types of the associated STAs through BSS Membership Selector
  In a BSS with old PHY types being disallowed, there is higher chance to enable AP power management.
  The designed protocol should harmonize with it.
In the future, the market share of the old PHY types will become less and less.
  This can give higher chance to enable the AP power management.
  The designed protocol should harmonize with it.
Wi-Fi chipset shipment forecast by IDC towards 2023

## Slide 8: AP Device Types
Mobile/soft AP( MLD)
  Most of them are battery powered, and have single radio
NSTR mobile AP MLD
  Battery powered
Regular STR AP MLD
  Powered through ethernet cable etc.
The proposed power management proposal needs to support the power management of all these three types, especially the previous two types

## Slide 9: AP’s Intra-PPDU Power Save and Dynamic SM Power Save
Similar to STAs, an AP can stop its PPDU reception if the AP figures out the PPDU doesn’t carry the frames addressed to it.
By allowing AP’s single RF chain and/or narrower BW to monitor the medium, the AP can save its power.
  The protocol needs to address the case when non-HE STAs or non-UHR STAs associate with the AP.

## Slide 10: AP Power Management Mode
The AP power management mode includes
  Power save mode
    Doze state
    Awake state
  Active mode
The protocol needs to provide the method that non-AP STA’s buffered frame notification.
The protocol needs to address the case when non-HE STAs or non-UHR STAs associate with the AP.
Power management mode enabling/disabling per the STA type allowed to do the association with the AP.
The protocol needs to address the active probing issue
  Frequently short AP Announcement.

## Slide 11: Method to Avoid Bi-direction Awake Soliciting and Notification
Allowing the TWT based power saving at AP and STA side for both individual TWT and broadcast TWT.
  Both AP and STAs are awake within the negotiated TWT SPs.
  Outside the negotiated TWT SPs, the AP can go to power save mode.

## Slide 12: AP MLD Power Management
Different affiliated APs of an AP MLD are in different power management mode.
One simplification is that at least one affiliated AP is in active mode while the other affiliated APs are in power save mode.
  This can address the probing, association, non-UHR STA frame exchanges.
  This is less useful when the TID-to-link mapping is not equal to 3.
    Under TID-to-link mapping other than 3, if some affiliated APs are in active mode, the non-AP MLDs will transmit frames to the active affiliated APs.