## Slide 1: Single Radio MLD
Date: 2023-01-03
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Kiseon Ryu Huizhao Wang Hongyuan Zhang Rui Cao Yan Zhang Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Recap: EMLSR non-AP MLD
EMLSR non-AP MLD is proposed to
  Increase the throughput where a non-AP MLD has one full functional radio and multiple links.
  Save power through listening with single RF chain.
In 11be, some members propose EMLSR to be extended to AP MLD and P2P.

## Slide 3: Recap: NSTR AP MLD
Primary link and non-primary link are defined.
The mobile AP MLD can use the non-primary link for the frame exchange with a non-AP MLD only when the primary link is used for the frame exchanges with the non-AP MLD.
  When the backoff counters on both primary link and non-primary link are 0, the primary link and non-primary link can be used for the frame exchanges.
A multi-radio non-AP MLD can use the non-primary link for the frame exchange with a NSTR mobile AP MLD only when the primary link is used for the frame exchanges with the mobile AP MLD.
  When the backoff counters on both primary link and non-primary link are 0, the primary link and non-primary link can be used for the frame exchanges.

## Slide 4: Recap: EMLSR AP MLD and EMLSR TDLS MLDs
In [1]
  The EMLSR link used for the Beacon transmission and association are primary link.
  When the primary link is busy, the EMLSR AP MLD and its associated multi-link non-AP MLDs can use non-primary link (EMLSR link that is not used for Beacon transmission, association) to do frame exchanges until the end of the primary link’s TXOP.
    With this, the medium synchronization operation in non-primary link can be avoided.

## Slide 5: EMLSR AP MLD and P2P EMLSR non-AP MLD
When both peer P2P device support EMLSR mode, the multiple links of the P2P connection can be in EMLSR mode.
  Medium access and frame exchange method 1:
    When both peer MLDs are MLDs with links in EMLSR mode, each TXOP in the links with EMLSR mode enabled is initiated by MU-RTS/CTS handshake for the radio switch.
    The returning to listening mode is same as the DL frame exchanges of EMLSR operation in 11be.
  Medium access and frame exchange method 2:
    Primary link and non-primary link are defined where the non-primary link is used when the primary link is busy.
    Two MLDs switch back to the primary link no later than the time when OBSS’s TXOP in primary link ends.
    With method 2, the EMLSR support may not be required.
AP MLD1
Link1
Link2
Link3
EMLSR link set
EMLSR link set
Primary link
Non-Primary link
Non-primary link
(E)MLSR Non-AP MLD3
(E)MLSR Non-AP MLD2
EMLSR Non-AP MLD
EMLSR AP MLD

## Slide 6: Blindness of Non-Primary Link Medium Access
With EMLSR AP MLD or P2P EMLSR non-AP MLD, for non-primary link, blindness at one side may happen while another side still has the medium usage information.
  Under this case, the medium synchronization defined by 11be can be used.
When the EMLSR AP MLD as the TXOP holder does frame exchanges for DL Data/Management frames with an EMLSR non-AP MLD in primary link and the EMLSR non-AP MLD can’t do CCA in non-primary link, both the AP MLD and the non-AP MLD lose the medium synchronization information in non-primary link.
When the EMLSR AP MLD as the TXOP holder does frame exchanges with an EMLSR non-AP MLD in primary link with DL Data/Management frames and UL Data/Management frames in a TXOP, both the AP MLD and the non-AP MLD lose the medium synchronization information in non-primary link.

## Slide 7: Medium Access Synchronization
Option 1:
  When the primary link is busy because of the neighbor BSS’s TXOP, the EMLSR AP MLD and its affiliated non-AP MLD can do frame exchanges which ends no later than the end of the primary 20MHz channel’s TXOP with the following restriction:
    When the primary link is busy because of the neighbor BSS’s TXOP and both AP MLD and non-AP MLD in non-primary link lose the medium synchronization, transmitting RTS after backoff through ED level in non-primary link is not allowed.
Option 2:
  When the primary link is busy because of the neighbor BSS’s TXOP, the EMLSR AP MLD and its affiliated non-AP MLD can do frame exchanges which ends no later than the end of the primary 20MHz channel’s TXOP with the following restriction:
    When the primary link is busy because of the neighbor BSS’s TXOP and both AP MLD and non-AP MLD in non-primary link lose the medium synchronization, transmitting RTS after backoff through ED level is allowed.
      After receiving the RTS, if the NAV timer has 0 value and the PHY CCA per ED level indicates the medium is idle PIFS before the RTS reception, the CTS can be transmitted.

## Slide 8: Frame Exchanges between EMLSR AP MLD and MLSR/STR/NSTR non-AP MLD
When the primary link is idle, the MLSR/ STR/NSTR non-AP MLD and EMLSR AP MLD uses its primary link to do the frame exchanges.
When the primary link is busy, the EMLSR AP MLD and MLSR/ STR/NSTR non-AP MLD switch its radio to the non-primary link.
AP MLD1
Link0
Link1
Link2
Link3
Link4
EMLSR link set
EMLSR link set
Primary link
Primary link
Non-primary link
Non-EMLSR link
MLSR Non-AP MLD3
MLSR Non-AP MLD2
The frame exchanges in a non-primary link ends at the end of the TXOP owned by the neighbor BSS in the primary link.
AP MLD1
Link0
Link1
Link2
Link3
Link4
EMLSR link set
EMLSR link set
Primary link
Primary link
Non-primary link
Non-EMLSR link
NSTR Non-AP MLD3
STR Non-AP MLD2

## Slide 9: Frame Exchanges between EMLSR AP MLD and EMLSR non-AP MLD
AP MLD1
Link0
Link1
Link2
Link3
Link4
EMLSR link set
EMLSR link set
Primary link
Primary link
Non-primary link
Non-EMLSR link
EMLSR Non-AP MLD3
EMLSR Non-AP MLD2
EMLSR non-AP MLD behavior option 1:
  Within a TXOP in non-primary link initiated by the AP MLD with a EMLSR non-AP MLD as the TXOP responder, the EMLSR non-AP MLD switches to monitor multiple links when it detects a frame exchange failure or a frame/PPDU that is not addressed to it.
EMLSR non-AP MLD behavior option 2:
  Within a TXOP in non-primary link initiated by the AP MLD with a EMLSR non-AP MLD as the TXOP responder, the EMLSR non-AP MLD stays in non-primary link, when it detects a frame exchange failure or a frame/PPDU that is not addressed to it and the primary link is still busy (per the virtual carrier sensing in primary link).

## Slide 10: Frame Exchanges between EMLSR AP MLD and EMLSR non-AP MLD (Cont’d)
EMLSR non-AP MLD behavior option 3:
  When all the setup links of an EMLSR non-AP MLD that are capable doing EMLSR frame exchanges are covered by one EMLSR link set of the associated AP MLD, the EMLSR non-AP MLD is not allowed to be in EMLSR mode. Otherwise, an EMLSR non-AP MLD can be in EMLSR mode.
AP MLD1
Link0
Link1
Link2
Link3
Link4
EMLSR link set
EMLSR link set
Primary link
Primary link
Non-primary link
Non-EMLSR link
EMLSR Non-AP MLD3
in EMLSR mode
EMLSR Non-AP MLD2
in MLSR mode

## Slide 11: MLSR AP MLD
Observation: in 11be, a MLSR non-AP MLD can switch its radio to different link on TXOP basis.
A MLSR AP MLD can define primary link and non-primary link as a MLSR link set
  The primary link is used to do the frame exchanges, Beaconing, association.
  When the primary link is busy because of neighbor BSS’s TXOP, the MLSR AP MLD switches its radio to non-primary link for the frame exchanges.
    The non-primary link’s frame exchanges will end at the end of the neighbor BSS’s TXOP in primary link and the MLSR AP MLD switches its radio to the primary link at the end of the neighbor BSS’s TXOP in primary link.
  A MLSR AP MLD may have a low cost radio to monitor one link when doing frame exchanges in another link.
AP MLD1
Link0
Link1
Link2
Link3
Link4
MLSR link set
MLSR link set
Primary link
Primary link
Non-primary link
Non-EMLSR link
MLSR Non-AP MLD3
NSTR Non-AP MLD2

## Slide 12: Throughput Improvement with non-AP MLSR MLD
Observation: in 11be, a MLSR non-AP MLD can switch its radio to different link on TXOP basis.
A AP MLD can define primary link and non-primary link for MLSR non-AP MLDs
  When the primary link is busy because of neighbor BSS’s TXOP, the MLSR non-AP MLD switches its radio to non-primary link for the frame exchanges.
    The non-primary link’s frame exchanges will end at the end of the neighbor BSS’s TXOP in primary link and the MLSR non-AP MLD switches its radio to the primary link at the end of the neighbor BSS’s TXOP in primary link.
  A MLSR non-AP MLD may have a low cost radio to monitor one link when doing frame exchanges in another link.
AP MLD1
Link0
Link4
MLSR Non-AP MLD2

## Slide 13: Frame Exchanges between non-AP MLD and Mobile NSTR AP MLD
When the primary link is busy because of the TXOP of neighbor BSS/P2P, both the mobile AP MLD and its associated non-AP MLD can use the non-primary link to do the frame exchanges.
  The frame exchanges need to be finished before the end of the TXOP of neighbor BSS/P2P.

## Slide 14: Reference
[1] 11-22/2203 EMLSR AP/mobile AP operation