## Slide 1: Use cases discussion
Date: 2023-01-09
Authors:

## Slide 2: Background
OWE
  OWE (Opportunistic Wireless Encryption ,refer to RFC 8110 drafted by Dan) is an encryption method to enhance the security and privacy of users connecting to public Wi-Fi networks.
  Deployed in public place and offered over “Open” wireless network, like coffee shops, airports, hospitals, hotels, etc.
  The client and AP perform a Diffie-Hellman key exchange via association request/response and 4-way handshake to generate the PTK
  Device ID
    11bh group proposed NW generated Device ID scheme to identify each returned STA in D0.2
    Device ID is exchanged in 4-way handshake(association req/resp frame in FILS mode)

## Slide 3: Frame exchange in OWE
STA
AP
Open Auth Req & Resp
4-way handshake
Association req(STA pub key)
Association resp(AP pub key)
Generate PMK
Generate PTK
No password input by end user

## Slide 4
  Device ID approach applied in OWE(normal case)
STA
AP
Open Auth Req & Resp
Association req & resp (STA & AP pub key)
Generate PMK
Key 3: device ID granted
Second association
Association req & resp (STA & AP pub key)
Open Auth Req & Resp
Key 2: provide old device ID for identification
Key 3: grant new device ID
No password input by end user

## Slide 5: Fake AP issue in public place
Several AP nodes deployed in the public place to enlarge Wi-Fi coverage
3rd party easy to mimic a legitimate AP around them(no password)
STA doesn’t have the ability to distinguish fake AP from legitimate AP
Fake AP

## Slide 6
  Middle man attack based on device ID approach
Returned STA
Fake AP
(Middle man)
Open Auth Req & Resp
Association req & resp (STA & AP pub key)
Key 2: provide old device ID(ID1) from
the legitimate AP for identification
Key 3: grant a garbage device ID
Mimics as a returned STA
Legitimate AP
Association req & resp (STA & AP pub key)
Key 2: provide ID1 for identification
Key 3: grant a new device ID
Open Auth Req & Resp

## Slide 7: Possible approach for OWE mode
The returned STA should identify the AP before providing its device ID
identify the AP via auth/association request/response frame exchange

## Slide 8: SP1
Do you agree the returned STA shall identify AP/ESS in OWE mode via auth/association request/response frame exchange?