## Slide 1: UHR Feature to Overcome PSD Limitations: Distributed-Tone Resource Units
Date: 2022-12-10
Authors:
Name | Affiliations | Address | Phone | Email
Jianhan Liu | Mediatek | 2840 Junction Ave. San Jose, CA, 95134 |  | jianhan.liu@mediatek.com
Shengquan Hu |  |  |  | 
Thomas Pare |  |  |  | 
Gary Anwyl |  |  |  | 

## Slide 2: Regulations Put Limitations on Power Spectral Density (PSD) in Sub-7GHz
In 6GHz bands, PSD limitations are tougher. For a non-AP STA in LPI bands, the PSD limitation is -1dBm/MHz.
    For a 52-tone RU, the maximum TX power now is only about 6dBm.
In different regions, regulations also put different limitations on 2.4GHz and 5GHz bands.
  For example, 10dBm/MHz PSD limitations are put on 2.4GHz bands in EU/China/ Japan/Korea.
    Note that for a 52-tone RU, the maximum TX power is about 17dBm.
  Even in 5GHz bands, we can boost transmit power if we can walk around the PSD limitations.
    For a 52-tone RU, the maximum TX power now is about 24dBm which is still 6dB away from the maximum allowed EIRP 30dBm.
If we can overcome the PSD limitations, we can enhance the transmit power and therefore enhance the spectrum efficiency or extend the range.

## Slide 3: Regulations on Power Spectral Density (PSD) in Sub-7GHz
5 GHz Power Spectral Density |  |  |  |  |  | 
Country / Geo | 5.15 - 5.25 GHz | 5.25 - 5.35 GHz | 5.47 - 5.65 GHz | 5.65 - 5.725 GHz | 5.725 - 5.85 GHz | Unit
Conductor | 11 (17 AP) | 11 | 11 | 11 | 33 | dBm / MHz
EIRP | 17 (24 AP) | 17 | 17 | 17 | 39 | dBm / MHz
Tx Power Limit |  |  |  |  |  | 
Conductor | 24 | 24 | 24 | 24 | 30 | dBm
EIRP | 30 | 30 | 30 | 30 | 36 | dBm

## Slide 4: Distributed-Tone Resource Units (dRU) Come to Rescue
Note that the PSD limitations are defined by per MHz and for each STA. If we distribute tones of a small-size RU over a wide bandwidth, then the tones for each STA become non-contiguous and therefore each tone can be transmitted with higher power.
For convenience, we call the RUs defined in 11ax and 11be with contiguous tones as regular RUs (rRU) and call the RUs with distributed tones as distributed tones RU (dRU).
For a STA transmits dRU, it can transmit much higher power compared to rRU.
  For example, for a 52-tone dRU over 80MHz, there can be just one tone per MHz. But for a 52-tone rRU, there are about 13 tones per MHz.
  With PSD limitations as -1dBm/MHz in 6GHz LPI bands, for 52-tone RU, using dRU can boost transmit power by 11dB!
  This significant transmit power boost can enable higher MCSs or reach longer range.

## Slide 5: Distributed-Tone Resource Units (dRU) in UL-OFDMA
dRU is particularly useful in UL-OFDMA.
  As shown in the following figure, STA1, STA2 and STA3 can all boost its transmit power by using dRU.
  Compared to using same size rRU, all the tones get higher transmit power and therefore overall spectrum efficiency is enhanced significantly.

## Slide 6: Power Boost of dRUs
To maximize the power boost, the tones in one dRU should be spread out as large as possible (the optimal solution is 1 tone/MHz).
dRU size should be kept same as rRU size to avoid extra complexity.
The following table shows the achievable power boost for different dRUs distributed on different bandwidths.
  We use 6GHz LPI as an example. We can also get power boost in 2.4GHz and 5GHz in different regions.
dRU Power Boost Compared to rRU in 6GHz LPI bands |  |  | 
 | BW20 | BW40 | BW80
 | Power Boost (dB) | Power Boost (dB) | Power Boost (dB)
RU26 | 8.13 | 11.14 | 11.14
RU52 | 6.37 | 8.13 | 11.14
RU106 | 3.56 | 6.37 | 8.13
RU242 | na | 2.69 | 5.12
RU484 | na | na | 2.69

## Slide 7: Power Boost of dRUs (cont’s)
We can see that dRU can overcome the PSD limitations and bring significant gain.
  For example, for an 80MHz UL-OFDMA transmission with 8 users, each user using 106-tone dRUs, compared each user using 106-tone rRU, the overall performance can be improved by 8.13dB.

## Slide 8: Summary
We pointed out the regulated PSD limitations in sub-7GHz and those PSD limitations reduce the transmit power.
We introduced the concept and idea of Distributed-Tone Resource Units (dRU) to overcome the regulated PSD limitations.
We showed the dRU can significantly boost transmit power in UL-OFDMA.

## Slide 9: Straw Poll #1
Do you agree that Distributed-Tone Resource Units (dRU) should be considered as a feature for the UHR?