## Slide 1: Notes from 3GPP Rel-18: Key Coexistence Issues
Date: 2023-01-18
Authors:

## Slide 2: Abstract
3GPP RAN1 is currently extending NR sidelink operation to 5-7 GHz unlicensed spectrum (SL-U). Several issues remain under discussion regarding SL-U channel access and physical channel design in these bands, notably:
Listen Before Talk (LBT) type for synch, feedback, and data channels, including one-shot LBT.
UE-to-UE COT sharing in pairs and groups.
Key points to track for IEEE 802.11
Coexistence simulations between SL-U and WiFi have been largely based on 3GPP TR38.889 from Rel-16, and there have been no updates to account for Wi-Fi 6E/7 operation
The use of one-shot (Type 2) LBT for multiple types of transmissions – e.g ACK/NACK, sidelink broadcast & synch etc.
Conditions where UEs are allowed to share a COT without gNB intervention.
The presentation will discuss the pertinent 3GPP developments on the above topics.

## Slide 3: 3GPP Work Item on NR Sidelink Evolution1
Objective 2: Study and specify support of sidelink on unlicensed spectrum for both mode 1 and mode 2 where Uu operation for mode 1 is limited to licensed spectrum only [RAN1, RAN2, RAN4]
Channel access mechanisms from NR-U2 shall be reused for sidelink unlicensed operation
Focus on FR1 unlicensed bands (n46 and n96/n102)
Legend
AP-1, AP-2: IEEE 802.11 Access Points
gNB: 3GPP New Radio (NR) base station
NR-U: NR operations in unlicensed band
SL Mode-1: Sidelink mode 1
SL Mode-2: Sidelink mode 2
Sidelink supports direct UE-to-UE links
Sidelink mode 1: gNB allocates resources for UEs
Sidelink mode 2: autonomous resource allocation (without gNB)
1 OPPO, "WID revision: NR sidelink evolution," RP-222806. 3GPP TSG RAN Meeting #98-e, December 12 – 16, 2022.
2 3GPP TS 37.213: "Physical layer procedures for shared spectrum channel access."

## Slide 4: Regulatory Requirements at 5 and 6 GHz Unlicensed Bands
5 GHz band: USA1, European Union2 and many countries/regions allow unlicensed operations
Access Point (AP)-to-client and client-to-client operations authorized
Table summarizes the regulations in the USA/European Union
  DFS (Dynamic Frequency Selection): protects radar operations. A different frequency channel must be selected for at least 30 minutes if a radar is detected
Legend
TPC: Transmit Power Control
EIRP: Effective Isotropic Radiated Power
1 United States Code of Federal Regulations, 47 CFR 15.407, https://www.ecfr.gov/current/title-47/chapter-I/subchapter-A/part-15/subpart-E/section-15.407
2 ECC Decision (04)08, “On the harmonised use of the 5 GHz frequency bands for Wireless Access Systems including Radio Local Area Networks (WAS/RLAN),” approved 09 July 2004, latest amended 2 July 2021.
6 GHz band: Only AP-to-client operations, not client-to-client, authorized in the USA (47 CFR § 15.407 (d)(5))
European Union: indoor and outdoor operations authorized in 5.925 – 6.425 GHz frequency band

## Slide 5: 3GPP Emission/Bandwidth Requirements1,2
n96
n102
n104
5925 MHz
7125 MHz
6425 MHz
Band | gNB max carrier BW | gNB ACLR limit | UE max carrier BW | Max aggregated CA
n96 | 80 MHz | 35 dB / 40 dB | 100 MHz | 320 MHz (80+80+80+80)
n102 | 80 MHz | 35 dB / 40 dB | 100 MHz | TBD
n104 | 100 MHz | 35 dB / 40 dB | 100 MHz | TBD
Channelization generally follows 20/40/60/80/100 MHz operation
EIRP limits are country-, region-specific
Legend
ACLR: Adjacent Channel Leakage ratio
CA: Carrier Aggregation
1 3GPP TS 38.101, 23GPP TS 38.104.

## Slide 6: Channel Access Mechanisms1,2
 | R16 NR-U | R17 FeURLLC | R18 SL-U
Access modes | Dynamic Semi-static | Semi-static + UE-initiated COT | Dynamic Semi-static (TBC)
Energy Detect | -72 dBm/20 MHz | -72 dBm/20 MHz | -72 dBm/20 MHz
Max COT | 8 ms or 10 ms | 8 ms or 10 ms | 8 ms or 10 ms
No-LBT transmissions | Responding transmissions within 25 us of end of initiating transmission | Responding transmissions within 25 us of end of initiating transmission | TBC
Short sensing transmissions | SS-PBCH, PRACH | UL to initiate COT | TBC
Semi-static access applicable when absence of other technologies is guaranteed
FeURLLC (Further enhanced URLLC) adds UE-initiated COT to the semi-static access mode
1 3GPP TS 37.213, 23GPP TS 38.212.

## Slide 7: Example: NR-U Downlink Channel Access Procedure
NR-U channel access procedures are specified in 3GPP TS 37.213
Sidelink should use these channel access procedures
Note: Uplink channel access procedures are somewhat different

## Slide 8: SL-U1 Challenge: Large Slot Size and Synchronized Transmissions
NR-U channel access mechanism uses a backoff procedure with a sensing slot size of 9 us (similar to IEEE 802.11)
Sidelink UEs are synchronized so transmissions occur at sidelink slot boundaries
  Sidelink slot sizes (): 250 us, 500 us or 1 ms depending on numerology used
  Sidelink cannot transmit until the slot boundary
    A gap results as shown
    Note: TS 37.213 allows freezing the backoff counter so that end of backoff counter coincides with slot boundary
Another radio network may gain access to the channel during the gap duration
1SL-U: Sidelink in unlicensed bands
Backoff counter ends before the slot boundary

## Slide 9: SL-U Challenge: Limited Transmissions in Contiguous Slots
In general sidelink does not support transmissions in contiguous (sidelink) time slots
Suppose each sidelink UE accesses the channel using NR-U channel access mechanism (Type 1)
  UE A has to contend for channel access again after TSL transmission time
    Overall data rate is very low because TSL very small
  UE B has to contend for channel access with other radio networks
    Transmissions in adjacent slots as shown here not possible for the UE network
Periodic resource reservations for A, B and C
Minimum periodic time in sidelink is 1 ms
Slot sizes
Sidelink resource reservations for a 3-UE network
Overall data rate for the sidelink network is very low because each UE has to contend for channel access after each time slot

## Slide 10: SL-U Challenge: Presence of Guard Symbols in Sidelink Slots
Guard symbols included in sidelink slot to accommodate switching time from transmit mode to monitor/receive mode
Guard symbol time duration: 17.8 , 36.7 or 71.3 (when TSL = 250 , 500 or 1 ms)
Another radio network could access the channel during the guard symbol time
  Feedback (ACK/NACK) information lost if another radio network gains access during Guard1 time
Example PSSCH/PSCCH slot with PSFCH
PSSCH: carries data
PSCCH: control information
PSFCH: carries feedback information
DMRS: demodulation reference signal
Last 3 symbols for feedback UE transmissions
Guard 1 symbol gives time to switch from transmit to receive mode
Guard 2 symbol gives UE time to switch from transmit to receive/monitor mode for transmissions in next slot
ACK/NACK may not be available because of loss of access to feedback channel

## Slide 11
SL-U Challenge: Absence of UE-to-UE COT1 Sharing in NR-U
NR-U channel access procedure supports COT sharing only between gNB and UEs
For efficient operation of the sidelink it is desired to support UE-to-UE COT sharing
  One of the UEs accesses the channel using NR-U access procedure
  Other UEs share this UE's COT up to a Maximum Channel Occupancy Time (MCOT)
    Use a modified mode 2 scheme to allocate resources within the COT
  This approach not adopted at 3GPP because NR-U channel access procedure does not specify COT sharing between UEs
A framework for a possible solution currently being established at 3GPP RAN1 meetings
  Only the COT initiating UE (UE0) can share the COT
1Channel Occupancy Time.
2Jing Sun, "Status Report for Rel. 16 NR-U." 2019 July IEEE 802.11 Coexistence Workshop.
COT sharing in NR-U: UEs sharing gNB COT2
COT sharing in NR-U: gNB sharing uplink UE COT2
Desired SL-U COT share
UE-to-UE COT sharing is crucial to mitigate disadvantageous channel access for SL-U

## Slide 12: SL-U Challenge: Channel Access for Synchronization Signals
Synchronization signals in SL-U have to contend for channel access
  In licensed bands synchronization signals are at known locations outside the sidelink resource pool
S-SSB2 access under consideration at RAN1
  TS 37.213 Type 2A:
    Channel idle for 25 us
    Transmission duration of a single burst at most 1 ms
    Burst duty cycle at most 1/20
S-SSB transmissions interfere with WiFi/NR-U
  Frequency of S-SSBs required for SL-U?
  Effects (collisions/delay/throughput) of S-SSBs on WiFi/NR-U systems?
Resource pool1 and S-SSB in sidelink (licensed bands)
1Z. Ali, S. Lagén, L. Giupponi and R. Rouil, "3GPP NR V2X Mode 2: Overview, Models and System-Level Evaluation," in IEEE Access, vol. 9, pp. 89554-89579, 2021.
2S-SSB – Sidelink Synchronization Signal Block

## Slide 13: Enhancements to Sidelink to Address the Challenges
Cyclic Prefix (CP) extension (CPE) (NR-U feature)
  Decreases guard periods for improved access to channel
  Applicable to PSFCH symbol (feedback UE) and UE-to-UE COT share
Multiple starting positions (NR-U feature)
  Transmissions at multiple symbol positions within a sidelink slot
    Provides enhanced access to the channel
Transmissions in contiguous sidelink slots
  Higher data rates once the channel is accessed
  May decrease the channel usage time for other UEs
CPE before the AGC of PSFCH transmission
CPE before the AGC of UE2 transmission
Half-slot starting position combined with CPE
Transmissions at half-slot boundaries
Transmissions at slot boundaries
All these enhancements are currently under consideration at RAN1 as part of the sidelink Work Item

## Slide 14: Coexistence Analyses
Rel-16 study on NR-U coexistence with 802.11ac or another NR-U network in TR 38.889 was focused on 5 GHz
Rel-17 FeURLLC did not have an extensive coexistence study
Rel-18 SL-U has 6 GHz SL-U + WiFi coexistence as optional scenario
  Coexistence simulations between SL-U and WiFi largely based on 3GPP TR38.889 from Rel-16, no updates made to Wi-Fi assumptions
Recommendations to 802.11 Coex SC:
Track coex simulation assumptions
Monitor the use of one-shot LBT (Type 2) for multiple categories of transmissions
Monitor conditions where UEs are allowed to share a COT without gNB intervention