## Slide 1: Proposal for consensus straw poll
Date: 2023-02-06
Authors:
Name | Affiliation | Address | Phone | Email
Yinan Qi | OPPO |  |  | v-qiyinan@oppo.com
Weijie Xu |  |  |  | xuweijie@oppo.com
Doc.: IEEE 802.11-23/0063r1
February 2023

## Slide 2: Outline
Overview of support AMP devices in WLAN
Consideration on forming a reasonable scope
Proposed consensus straw poll
Naming
Doc.: IEEE 802.11-23/0063r1
February 2023

## Slide 3: Overview of support AMP devices in WLAN
Based on previous discussion, we have the following concept for AMP:
  Battery-less and low-complexity devices, maintenance-free network are strongly required for many verticals.
  The required data rate is lower than 100kbps, the typically required coverage is 10~30 meters indoor and up to 200 meters outdoor and the required positioning accuracy is 1~3 meters.
  Various ambient power sources can be utilized to drive the AMP devices. Limited power storage may be needed for the device because of very limited power density (x uw~x mw) for typical ambient power sources.
  Developing ultra-low complexity and ultra-low power consumption device using ambient power is a compromising way to fulfill the requirement.
  Ultra-low power consumption reception and transmission is needed for the device.
  Coexistence with the existing devices needed to be considered when operating with the same frequency bands.
Doc.: IEEE 802.11-23/0063r1
February 2023

## Slide 4: Consideration on forming a reasonable scope
In order to have a limited and well-defined scope of work, the following have been proposed and discussed:
  WUR-similar design could be as the starting point for downlink receiver
  Simplified UL PHY with simple waveform such as OOK/FSK/PSK
  Simplified MAC (on top of existing WLAN technologies) + Enhanced power saving/ power management
  Support S1G and consider 2.4GHz and 5GHz
  How the AMP device do energy harvesting is not in the scope
Doc.: IEEE 802.11-23/0063r1
February 2023

## Slide 5: Consensus straw poll(1)
  Do you agree on the following features/requirements for AMP WLAN as the baseline for future discussion?
  Support ultra-low complexity and ultra-low power consumption transmission and reception for device using ambient power sources:
    WUR-similar design could be as the starting point for downlink receiver
    Simplified UL PHY with simple waveform such as OOK/FSK/PSK
  Simplified MAC (on top of existing WLAN technologies) + Enhanced power saving/ power management
  Support Sub-1 GHz and consider 2.4GHz and 5GHz
  How the AMP device does energy harvesting is not in the scope
  Coexistence with existing 802.11 devices when operating in the same frequency band.
  The PAR/CSD scope could be further harmonized during SG discussion.
Doc.: IEEE 802.11-23/0063r1
February 2023

## Slide 6: Consensus straw poll(2)
Do you agree to form the AMP SG, based on the discussion and the summary in the technical report[12], to develop PAR/CSD for AMP standard project?
  Y
  N
  A
Doc.: IEEE 802.11-23/0063r1
February 2023

## Slide 7: Naming of the Study Group
There has been suggestion to consider the name for the SG. It is a good chance now to consider whether there is a more suitable name that can better reflect the scope, has good readability and also is easy to be remembered. Possible candidates including:
  Battery-Less/Free Operation
  WLAN for Battery-Less/Free STAs
  WLAN for Zero-Power STAs
  Zero-Power Communication
  …
Doc.: IEEE 802.11-23/0063r1
February 2023

## Slide 8: Reference
IEEE 802.1122/1339r0, Use Cases of smart manufacturing
IEEE 802.1122/1341r1, Use Cases of Data Center Infrastructure Management.
IEEE 802.11-22/0963r0, Use Cases for AMP IoT Devices.
IEEE 802.11-22/1559, Updated Use Cases for AMP IoT Devices.
IEEE 802.11-22/0962r0, Potential Techniques to Support AMP IoT Devices in WLAN
IEEE 802.11-22/970r0, Feasibility of supporting AMP IoT devices in WLAN
IEEE 802.11-22/1560r0, Ambient powers and energy storage
IEEE 802.11-22/1561r0, Further discussion on feasibility of supporting AMP IoT devices in WLAN
IEEE 802.11-22/1799r0, On energy harvesting and the differentiation with RFID
IEEE 802.11-22/1800r0, New Use Case for AMP IoT Devices: Smart Grid
IEEE 802.11-22/1961r0, Prototype presentations for AMP IoT
IEEE 802.11-22/1562r5, Draft Technical Report on support of AMP IoT devices in WLAN
IEEE 802.11-23/0173r0，Discussion on examplary AMP use scenarios
IEEE 802.11-23/0112r0, Ambient IoT Device Demo
IEEE 802.11-23/0056r0, 802.11 compatible backscatter prototype
IEEE 802.11-22/1960r3, Summary and recommendation for AMP IoT
Doc.: IEEE 802.11-23/0063r1
February 2023