## Slide 1: 802.15 Liaison Report – Jan. 2023
Date: 2023-01-16
Authors:

## Slide 2: 802.15.16t Narrow Band Licensed Operation (NB-Lic)
What is it:
  Licensed Narrow Band (NB) Operation in channels bandwidth between 5 – 100KHz in the VHF/UHF bands such as 160MHz, 450MHz, 700MHz and 900MHz, taking advantage of the superior channel propagation properties. Targeted usages mission critical operation.
Status and main discussion topics:
  Draft amendment 0.2 in development and review by members.

## Slide 3: 802.15.4ab Next Generation UWB
What is it:
  Builds on 802.15.4z increasing footprint usefulness of the technology to additional usages beyond range measurement. Area of enhancements relates to ranging resiliency, sensing, data rates, support for additional spectrum, improved detection and many more.
Status:
  In Technical Specification Document (TSD) development phase.
  Group is taking steps forward towards draft amendment text stage.

## Slide 4: 802.15.4ab Next Generation UWB
Main discussion topics:
  Narrow Band Assisted UWB - transmission of 2MHz signal in the UNII3/5 bands to improve channel budget of the main UWB signal by providing synchronization base. Discussed channel hopping mechanism, message formats in the NB channel.
  Discovery mechanism using NB operation.
  UWB Sensing – freq. stitching; increasing the affective channel BW by using partially overlapping channels.
  Considering impact of China MIIT’s proposed regulations
  One to many ranging mechanism

## Slide 5: Privacy SG
What is it:
  New project development for increased privacy for 802.15.4-2020, baseline for 802.15.4z (UWB and Ranging) .
  Improved security and privacy to protect from user tracking and profiling attack.
  Amongst envisioned mechanism MAC address randomization and rolling MAC address.
Status:
  In PAR and CSD development stage.

## Slide 6: 802.15.13 Multi-Gbit/s Optical Wireless Communication
What is it:
  MAC and PHY project for the 10,000nm – 190nm wavelength for multi gigabit communication, with up to 10Gbps to distance of up to 200m, in LoS conditions.
Status:
  At final approval stages, document is with RevCom for publishing.

## Slide 7: 802.15.6ma - Enhanced Dependability Body Area Network (ED-BAN)
What is it:
  Enhancements to the BAN (Body Area NW) Ultra Wideband (UWB) physical layer (PHY) and media access control (MAC) to support enhanced dependability to a human BAN (HBAN) and support for vehicle body area networks (VBAN).
  This revision focuses on international operation.
Status:
  Reviewed channel model and propagation simulations result for UWB under VBAN/HBAN conditions.

## Slide 8
TG4me
Cor1 15.4 2020 Revision 1
TG4ab
Next Generation UWB
TG6ma
Body Area Networks
Revision
TG7a
Optical Camera Communications
TG13
Multi Gigabit/sec
Optical Wireless Communication
TG15
Ultra Wide-Band Ad-Hoc Networks
TG16t
Ultra Wide-Band Ad-Hoc Networks
TG3mb
TG HDR
High Data Rate
Revision
SCTHz
Standing Committee THz
SCmaint
Maintenance Group
SCWNG
Wireless Next Generation
SCIETF
IETF liaison