## Slide 1: TG bh Way Ahead Decisions
Date: 2022-12
Authors:
Name | Company | Address | Phone | email
Graham Smith | SRT Group | Sunrise , FL |  | gsmith@srtrl.com

## Slide 2
Based on presentation 22/2150r2 options and decisions were provided
This presentation simply lists those options and proposes Straw Polls and Motions

## Slide 3: Straw Polls/Motions
SMA – Same MAC Address
  Similar to “11aq-like”
  If non-AP STA wants to be identified, it uses same address at the same ESS every
  STA maintains list of ESS/SSIDs and MAC Addresses.
  Needs an “opt-in” mechanism (set a Capability bit)
ADs
  Simple, easy to implement
  Meets every Use Case
  No computations
DIS
  As same address every time, trivial to copy and masquerade.

## Slide 4: Straw Polls/Motions
IRM MAC scheme
  STA tells AP the MAC address it will use for the next association
  STA maintains list of ESS/SSIDs and latest MAC Addresses.
  Needs an “opt-in” mechanism (Capability bit)
ADs
  Simple, easy to implement.
    Very similar to the “Same MAC” for STA
  Provides good protection against copying
  Meets every Use Case
  No computations

## Slide 5: Straw Polls/Motions
Adopt non-encrypted ID in IE scheme
  STA adds ID in and IE that was provided by the AP at previous association – new ID every association
  STA maintains list of ESS/SSIDs and IDs.
  Needs an “opt-in” mechanism
ADs
  Simple, easy to implement
  Provides good protection against copying
  Meets every Use Case
  No computations
DIS
  Requires new IE
  Needs to specify some uniqueness to ID (6 octets?)

## Slide 6: Straw Polls/Motions
Adopt a more complex scheme, ID Encoding, RRCM, IRMA
  Random MAC with encrypted identifier in an IE
  Keys exchanged
  Range of computational complexity
  STA maintains list of ESS/SSIDs and latest ID/keys
  Needs an “opt-in” mechanism
ADs
  Provides highest level protection
  Meet every Use Case
DIS
  Requires computations

## Slide 7: Straw Polls/Motion
TGbh draft shall include text related to:
SMA (slide 3)
IRM (slide 4)
Non- encrypted ID in IE (slide 5)
More complex scheme (slide 6)
Take each in turn.
THEN
Motion option with highest YES vote (assuming majority).
(Hopefully members would support a majority view)