## Slide 1: TG bh Way Ahead Decisions
Date: 2023-01
Authors:
Name | Company | Address | Phone | email
Graham Smith | SRT Group | Sunrise , FL |  | gsmith@srtrl.com

## Slide 2
Based on presentation 22/2150r2 options and decisions were provided
This presentation simply lists those options and proposes Straw Polls and Motions

## Slide 3: Straw Polls/Motions
SMA – Same MAC Address
  Similar to “11aq-like” STA picks MAC to be used, as per present rules
  If non-AP STA wants to be identified, it uses same MAC address at the same ESS every association
  STA maintains list of ESS/SSIDs and MAC Addresses.
  AP maintains list of STA addresses
  Needs an “opt-in” mechanism? (set a Capability bit or MIB variable?)
ADs
  Simple, easy to implement (similar is already deployed)
  Meets every Use Case
  No computations
DIS
  As same address every time, trivial to copy and masquerade.

## Slide 4: Straw Polls/Motions
IRM MAC scheme
  STA picks MAC to be used next time, as per present rules.
  STA tells AP the MAC address it will use for the next association
  STA maintains list of ESS/SSIDs and latest MAC Addresses.
  AP maintains list of STA addresses
  Needs an “opt-in” mechanism (Capability bit or MIB variable?))
ADs
  Simple, easy to implement.
    Very similar to the “Same MAC” for STA (but more secure)
  Provides good protection against copying
  Meets every Use Case
  No computations

## Slide 5: Straw Polls/Motions
Adopt non-encrypted ID in IE scheme
  STA adds ID in and IE that was provided by the AP at previous association – new ID every association
  STA maintains list of ESS/SSIDs and IDs.
  Needs an “opt-in” mechanism
ADs
  Simple, easy to implement
  Provides good protection against copying
  Meets every Use Case
  No computations
DIS
  Requires new IE
  Needs to specify some uniqueness to ID (6 octets?)

## Slide 6: Straw Polls/Motions
Adopt a more complex scheme, ID Encoding, RRCM, IRMA
  Random MAC with encrypted identifier in an IE
  Keys exchanged
  Range of computational complexity
  STA maintains list of ESS/SSIDs and latest ID/keys
  Needs an “opt-in” mechanism
ADs
  Provides highest level protection
  Meet every Use Case
DIS
  Requires computations

## Slide 7: Straw Polls/Motion
TGbh should adopt the following scheme:
SMA (slide 3)
IRM (slide 4)
Non- encrypted ID in IE (slide 5)
More complex scheme (slide 6)
Take each in turn.
THEN
Motion option with highest YES vote (assuming majority).
(Hopefully members would support a majority view)