## Slide 1: Mechanism of simultaneous changes to SN, scrambler seed, PN, AID, and TID
Date: 2023-3-13
Authors:
Chaoming Luo (OPPO)
Name | Affiliation | Address | Phone | Email
Chaoming Luo | OPPO |  |  | luochaoming@oppo.com
Liuming Lu |  |  |  | 
Pei Zhou |  |  |  | 

## Slide 2: Introduction
A mechanism is proposed for simultaneous changes to scrambler seed, transmitted SN, transmitted PN, transmitted AID, transmitted TID while a CPE client is associated.

## Slide 3: Recap: requirements
R9: 11bi shall define a mechanism for a CPE Client and CPE AP to change the transmitted SN and the scrambler seed on downlink and uplink to uncorrelated new values in Associate STA State 4, without any loss of connection when the OTA MAC address of the CPE Client is changed.
R10: 11bi shall define a mechanism for a CPE Client and CPE AP to change the transmitted PN on downlink and uplink to uncorrelated new values in Associate STA State 4, without any loss of connection when the OTA MAC address of the CPE Client is changed.
R11: 11bi shall define a mechanism for a CPE Client and CPE AP to change the CPE Client’s AID to an uncorrelated new value in Associate STA State 4, without any loss of connection when the OTA MAC address of the CPE Client is changed.
R30: 11bi shall define a mechanism for a CPE Client and CPE AP to obfuscate the transmitted TID to an uncorrelated new value on downlink and uplink to new values in Associate STA State 4, without any loss of connection.

## Slide 4: Discussion: SN and scrambler seed
802.11aq and 802.11REVmd clause 12.2.10:
  The STA shall periodically change its MAC address to a random value while not associated to a BSS.
  Every time a MAC address is changed to a new random value, counters in all sequence number spaces used to identify each MSDU or MMPDU shall be reset (see 10.3.2.14.2 (Transmitter requirements)) and the STA shall set the TXVECTOR parameter SCRAMBLER_RESET to RESET_SCRAMBLER on the next transmitted PPDU.
Should we reset SN and the scrambler seed in associated case when the OTA MAC address of the CPE Client is changed?
  Probably YES, no other change is required so far.
  A solid mapping from obfuscated SN to the ‘true’ SN also works.
  A solid mapping from obfuscated scrambler seed to the ‘true’ scrambler seed also works.

## Slide 5: Discussion: PN
802.11REVme clause 12.5.2.3:
  Increment the PN, to obtain a fresh nonzero PN for each MPDU, so that the PN never repeats for the same temporal key.
  The PN is incremented by a positive number for each MPDU. The PN shall be incremented in steps of 1 for constituent MPDUs of fragmented MSDUs, A-MSDUs, and MMPDUs. For PV0 MPDUs, the PN shall never repeat for a series of encrypted MPDUs using the same temporal key.
  The PN values sequentially number each MPDU. Each transmitter shall maintain a single PN (48-bit counter) for each PTKSA and GTKSA.
As the spirit of using PN in CCMP/GCMP, PN shall not be reset to 0 unless PTKSA changes. A solid mapping from the transmitted PN to the ‘true’ PN is required.

## Slide 6: Discussion: TID
TID is used in many places:
  QoS Control field of a data frame header
  Control frames: BlockAckReq, BlockAck, MU-BAR Trigger
  Action frames: ADDBA Request, ADDBA Response, DELBA, Transmit Stream/Category Measurement request and report frames, etc.
Unlike SN, PN and scrambler seed, each value of TID has its unique meaning as defined in the specification.
Simply obfuscating TID may be troublesome and does not work well. A solid mapping from obfuscated TID to the ‘true’ TID is required.

## Slide 7: Discussion: AID
AID is assigned by an AP when a non-AP associates.
  Could be mapped to the MAC address of the non-AP
  Its value shall be in a valid range (e.g., 1~2007) and conflict values shall be avoided in a BSS.
It is natural and straightforward to let AP assign a new AID whenever the non-AP changes OTA MAC address, to avoid conflict.

## Slide 8: Proposal
Request AP to assign or preassign a new AID whenever the associated non-AP changes OTA MAC address.
Use the following method to obfuscate TID, SN, scrambler seed, PN whenever the associated non-AP changes OTA MAC address:
  STA and AP compute locally a common random number (RN) using the new OTA MAC address and derive OTA_TID and OTA_PN:
    RN = Hash (OTA_MAC || IV), IV is a key derived from PTK.
    OTA_TID = TID ⊕ RN(0,3)
    OTA_SN = SN ⊕ RN(4,16)
    OTA_SCRAMBLER_SEED = SCRAMBLER_SEED ⊕ RN(17,24)
    OTA_PN = PN ⊕ RN(25,73)
  By nature, the ‘true’ TID, SN, scrambler seed and PN could be recovered by the receiver using the simple exclusive OR (⊕) algorithm with the correct RN.

## Slide 9: SP 1
Do you agree 11bi should incorporate the proposed method describe in slide 8?
  Y/N/A
Chaoming Luo (OPPO)

## Slide 10: Reference
[1] P802.11REVme_D2.1
[2] 11-21-1848-16-00bi-requirements-document
Chaoming Luo (OPPO)