## Slide 1: Varying PMKID and SAE password ID
Date: 2023-2-2
Authors:
Chaoming Luo (OPPO)
Name | Affiliation | Address | Phone | Email
Chaoming Luo | OPPO |  |  | luochaoming@oppo.com
Liuming Lu |  |  |  | 
Pei Zhou |  |  |  | 

## Slide 2: Introduction
A method to vary PMKID and SAE password identifier is proposed.

## Slide 3: Recap: requirement
R1: 11bi shall define a mechanism to prevent an eavesdropper distinguishing whether authentication exchanges between CPE Clients and CPE AP use identical SAE credentials or distinct SAE credentials (where a CPE AP supports multiple SAE credentials).
R2: 11bi shall define a mechanism to prevent an eavesdropper distinguishing whether reassociation exchanges between CPE Clients and CPE APs use identical PMK or distinct PMK.

## Slide 4: Discussion: PMKID
Following full association, PMKID is transmitted by the Client in the clear prior every reassociation (until the Client performs another association) to identify the PMK.
  12.6.1.1.2 PMKSA: The PMKSA is created by the Authenticator’s SME and Supplicant’s SME when EAP authentication, SAE authentication, FILS authentication, or an OWE exchange completes successfully, or when the PSK is configured.
  12.6.1.1.2 PMKSA: The PMKID derived from the KCK during the initial 4-way handshake is not changed during the lifetime of the PMKSA.
In short, PMKID exists per tuple <AP, Client, association>. An AP may maintain multiple PMKIDs for different Clients; A Client may maintain multiple PMKIDs for different APs.
21/1697r0 proposed a good method to derive a new PMKID after every reassociation (PMK keeps no change), so that it exists per tuple <AP, Client, reassociation>.

## Slide 5: Discussion: SAE password ID
The SAE password identifier, is used to identify different passwords. By default, a BSS has one SAE password and one SAE password ID. However, it is possible that a BSS maintains multiple SAE password and SAE password IDs, and even further, each SAE password could have multiple IDs.
  Clause 12.4.4.2.3: when Hash-to-element generation of the password element with ECC groups is used, a password identifier may be used.
  Clause 12.4.4.3.3: when direct generation of the password element with FFC groups, a password identifier may be used.
  pwd-seed = HKDF-Extract ( ssid, password [ || identifier ] )
A similar method as deriving PMKID could be considered to derive SAE password ID per tuple <AP, Client, reassociation> using PTK.

## Slide 6: Proposal
PMKID: as proposed by 21/1697r0, the STA and AP generate a new PMKID at each successful (re)association. Each PMKID is derived using the PTK (detail algorithm is TBD).
SAE password ID: the STA and AP generate a new SAE password ID at each successful (re)association. Each SAE password ID is derived using the PTK (detail algorithm is TBD).

## Slide 7: SP 1
Do you agree 11bi shall incorporate the proposed method describe in slide 6?
  Y/N/A
Chaoming Luo (OPPO)

## Slide 8: Reference
[1] P802.11REVme_D2.1
[2] 11-21-1848-16-00bi-requirements-document
[3] 11-21-1697-00-00bi-mac-privacy-and-pmksa-caching
[4] 11-22-0107-02-00bi-initial-privacy-enhancement-requirements
Chaoming Luo (OPPO)