## Slide 1: Smooth Roaming
Date: 2023-01-10
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Kiseon Ryu Huizhao Wang Hongyuan Zhang Rui Cao Yan Zhang Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Recap: Roaming
11baseline defines the roaming through fast BSS transition
In UHR, the following were proposed
  Hot standby AP MLD
    When a non-AP STA/MLD is doing frame exchanges with AP MLD 1, the frame exchange context is established in AP MLD 2
      The AP MLD switch can be done smoothly.
  AP MLD method
    An AP MLD is defined to includes the APs in multiple devices.
      The AP MLD features are used for smooth switch.

## Slide 3: Optional Roaming AP MLD
The support of roaming AP MLD feature is optional for both UHR AP MLD and UHR non-AP MLD.
If roaming AP MLD is not supported, the baseline FT can be used for fast transition.

## Slide 4: Roaming AP MLD
Roaming AP MLD for smooth roaming support is defined that includes multiple AP MLDs.
  Some non-link level MAC features are at MLD level while the other non-link level MAC features are at roaming MLD level.
The roaming AP MLD is not visible to EHT non-AP MLDs. Otherwise, if an AP MLD is used for roaming operation, the following may happen
  The EHT non-AP MLD may do the multi-link association through the links in different devices since the different devices are not known to the EHT non-AP MLDs.
    The adding and removing links without interrupting the association can be used.
  The EHT non-AP MLD may refuse the multi-link association with the AP MLD since the different links may have the same channel or overlapped channels.
    Such links may have different operating BW or the other different operating parameters.
AP MLD11
MLD common MAC
5GHz
AP111
6GHz
AP112
AP MLD12
MLD common MAC
5GHz
AP121
6GHz
AP122
AP MLD13
MLD common MAC
5GHz
AP131
6GHz
AP132
AP MLD14
MLD common MAC
5GHz
AP141
6GHz
AP142
Roaming AP MLD1
Roaming AP
MLD common MAC
Visible to an EHT non-AP MLD
Visible to an UHR non-AP MLD

## Slide 5: Roaming AP MLD (Cont’d)
A MAC SAP address is defined for a roaming AP MLD.
The BA agreement is negotiated between an UHR non-AP MLD and the roaming AP MLD if the UHR non-AP MLD supports the roaming.
The PMKSA, PTK of an UHR non-AP MLD are negotiated between an UHR non-AP MLD and the roaming AP MLD if the UHR non-AP MLD supports the roaming.
AP MLD11
MLD common MAC
5GHz
AP111
6GHz
AP112
AP MLD12
MLD common MAC
5GHz
AP121
6GHz
AP122
AP MLD13
MLD common MAC
5GHz
AP131
6GHz
AP132
AP MLD14
MLD common MAC
5GHz
AP141
6GHz
AP142
Roaming AP MLD1
Roaming AP
MLD common MAC
Non-AP MLD11
with AID 10
MLD common MAC
5GHz
STA11
6GHz
STA12
To DS
To DS
Non-AP MLD11
with AID 120
MLD common MAC
5GHz
STA21
6GHz
STA22
Non-AP MLD that doesn’t support
roaming AP MLD features
Non-AP MLD that supports
roaming AP MLD features

## Slide 6: Link Level Roaming vs MLD Level Roaming
MLD level roaming
  After the roaming, all the links of a non-AP MLD use the links of a new AP MLD to do the frame exchanges.
AP MLD21
MLD common MAC
5GHz
AP111
6GHz
AP112
AP MLD22
MLD common MAC
5GHz
AP121
6GHz
AP122
Roaming AP MLD2
Roaming AP
MLD common MAC
Non-AP MLD11
with AID 10
MLD common MAC
5GHz
STA11
6GHz
STA12
MLD level
Roaming operation
AP MLD21
MLD common MAC
5GHz
AP111
6GHz
AP112
AP MLD22
MLD common MAC
5GHz
AP121
6GHz
AP122
Roaming AP MLD2
Roaming AP
MLD common MAC
Non-AP MLD11
with AID 10
MLD common MAC
5GHz
STA11
6GHz
STA12

## Slide 7: Link Level Roaming vs MLD Level Roaming (Cont’d)
Link level roaming
  After the roaming, some links of a non-AP MLD use the links of one AP MLD to do the frame exchanges while the other links of the non-AP MLD use the links of another AP MLD to do the frame exchanges.
AP MLD21
MLD common MAC
5GHz
AP111
6GHz
AP112
AP MLD22
MLD common MAC
5GHz
AP121
6GHz
AP122
Roaming AP MLD2
Roaming AP
MLD common MAC
Non-AP MLD11
with AID 10
MLD common MAC
5GHz
STA11
6GHz
STA12
Link level
Roaming operation
AP MLD21
MLD common MAC
5GHz
AP111
6GHz
AP112
AP MLD22
MLD common MAC
5GHz
AP121
6GHz
AP122
Roaming AP MLD2
Roaming AP
MLD common MAC
Non-AP MLD11
with AID 10 of AP MLD22,
AID34 of AP MLD21
MLD common MAC
5GHz
STA11
6GHz
STA12
Link level
Roaming operation
AP MLD21
MLD common MAC
5GHz
AP111
6GHz
AP112
AP MLD22
MLD common MAC
5GHz
AP121
6GHz
AP122
Roaming AP MLD2
Roaming AP
MLD common MAC
Non-AP MLD11
with AID 34
MLD common MAC
5GHz
STA11
6GHz
STA12
Temporary state

## Slide 8: Link Level Roaming vs MLD Level Roaming (Cont’d)
The link level roaming provides smooth data frame exchanges than MLD level roaming.
The BA Buffer reordering needs to be in a common place of different MLDs (i.e. roaming AP MLD level).
  The AP MLDs affiliated with the roaming AP MLD may be difficult to implement this.
The link pair at non-AP MLD that associated with APs in different AP MLDs may be NSTR link pair.
  It is difficult to do the PPDU alignment in the link pair with the APs in different AP MLDs.
UHR needs to include MLD level roaming.
If the link level roaming is also defined in UHR,
  UHR needs to allow a roaming AP MLD to announce the disablement of link-level roaming among the AP MLDs affiliated with the roaming AP MLD.
  If a non-AP MLD found that its link pair is NSTR link pair when the link pair associates with two links of two AP MLDs, the non-AP MLD can’t do the link level roaming through the link pair.

## Slide 9: Extensible Roaming AP MLD: AID
The AID space is 2008.
The AID space should not be used at roaming AP MLD level.
The AID is allocated at AP MLD level.
  Most AID related features are at AP MLD level and link level.
  If a non-AP MLD requires the global identification at roaming AP MLD, the roaming AP MLD can allocate each AP MLD affiliated with it a unique AP MLD RoamingID. The global link identification of a link can be AP MLD RoamingID of the serving AP MLD + AID.

## Slide 10: Extensible Roaming AP MLD: Link
The link space of a MLD is 15.
The link space should not be used at roaming AP MLD level.
The link ID is allocated at the AP MLD level.
  Most Link ID related features are at AP MLD level.
  If a link requires the global identification at roaming AP MLD, the roaming AP MLD can allocate each AP MLD affiliated with it a unique AP MLD RoamingID. The global link identification of a link can be AP MLD RoamingID of the serving AP MLD + Link ID.