## Slide 1: Proposal for “Polished” SG Scope
Date: 2023-02-07
Authors:

## Slide 2: Abstract
This documents presents a proposal for a polished version of the proposed study group scope defined in 11-22/1960r4

## Slide 3: Main Motivation
We are proposing a work item in IEEE 802.11
Highlight re-use of existing IEEE 802.11 technologies wherever possible to fit into the existing 802.11 eco-system
Main messages of proposed study group scope defined in 11-22/1960r4 are unchanged

## Slide 4: Proposal for “Physical Layer Downlink”
Use IEEE 802.11ba (wake-up radio) and 802.11b (DSSS) as starting point
  Offers low power decoding and part of IEEE 802.11 eco-system
Modifications and extensions if necessary to support AMP specific requirements, e.g.
  Wireless power transfer to power fully passive devices
  Additional signaling in wake-up radio to transmit additional signaling or payload data
  Additional frequency bands
Has to be covered by existing frequency regulation

## Slide 5: Proposal for “Physical Layer Uplink”
Use IEEE 802.11b (DSSS modulation) as starting point
  Offers highly effective generation of signals for active transmitters AND backscatter modulation
Modifications and extensions if necessary to support AMP specific requirements, e.g.
  Additional frequency bands
  Optimizations for full-duplex operation in case of backscatter modulation
Has to be covered by existing frequency regulation

## Slide 6: Proposal for “MAC Layer”
Use of existing 802.11 MAC wherever possible
Modifications and extensions if necessary to support AMP specific requirements, e.g.
  Limited power availability of devices
  Integration of wireless power transfer into MAC structure
  Coordination of AMP device channel access (e.g. may not be able to use CSMA-like approaches, potentially undetectable by other devices)