## Slide 1: Thoughts on Seamless Roaming Under Non-collocated AP MLD Architecture
Date: 2023-02-20
Authors:
Name | Affiliations | Address | Phone | email
Guogang Huang | Huawei |  |  | huangguogang1@huawei.com
Yuchen Guo |  |  |  | 
Yunbo Li |  |  |  | 
Yousi Lin |  |  |  | 
Ming Gan |  |  |  | 

## Slide 2: Introduction
A new roaming approach under a non-collocated AP MLD architecture is proposed in [1].
The proposed approach would enable seamless transition from the current collocated AP MLD to another collocated AP MLD without interrupting the data transmission.
In this presentation, we share some thoughts on this non-collocated AP MLD architecture.

## Slide 3: Definitions
Collocated AP MLD
  An AP MLD where all affiliated APs are co-located with each other.
Non-collocated AP MLD
  An AP MLD that is not a collocated AP MLD. And the UMAC is not co-located with the corresponding LMAC.

## Slide 4: Example Network Topology
Compatibility issue for EHT non-AP MLD and UHR non-AP MLD
  The EHT non-AP MLD only can associate with the collocated AP MLD. Otherwise, it will be confused by the same link ID but with different BSSIDs
  The UHR non-AP MLD can associate with either the collocated AP MLD or the non-collocated AP MLD
UHR non-Collocated AP MLD

## Slide 5: Example Network Topology (Cont.)
  The UHR non-AP MLD can distinguish links of the same non-collocated AP MLD through the tuple (MLD MAC Address of Collocated AP MLD, link ID)
UHR non-Collocated AP MLD

## Slide 6: Example Network Topology (Cont.)
For the UHR non-AP MLD associated with a non-collocated AP MLD, the context corresponding the following operations resides in the UHR AP MLD UMAC of the non-collocated AP MLD, which may be resided in a portal
  Authentication, Association
  SN and PN assignment
  Encryption/Decryption
  BA buffering and reordering per SN
  Replay detection Per PN
  …
Note whether the functions Duplicate Detection per SN and Block Ack Scoreboarding reside in the non-collocated AP MLD UMAC depends on whether allowing a TID to be mapped to more than one collocated AP MLD

## Slide 7: Non-collocated AP MLD Discovery
If a collocated AP MLD is affiliated with a non-collocated AP MLD, then each AP affiliated with this collocated AP MLD shall include the corresponding MLD MAC address of the non-collocated AP MLD in the Basic Multi-link element of the Beacon frame
  Similarly, if a reported AP in the Reduced Neighbor Report (RNR) element is affiliated with a non-collocated AP MLD, then a non-collocated AP MLD ID (or the corresponding MLD MAC address of the non-collocated AP MLD) shall be included within a newly defined Extended MLD Parameters subfield.
To avoid the Beacon bloating, each affiliated AP shall include the info of other APs affiliated with the same collocated AP MLD in the RNR element. And the info on other APs affiliated with a different collocated AP MLD is optionally included in the RNR element

## Slide 8: Multi-link Reconfiguration vs. BSS Transition
The BTM frames can be reused to trigger the multi-link reconfiguration with neighboring collocated AP MLDs which affiliate with the same non-collocated AP MLD.
For an UHR non-AP MLD associated with a non-collocated AP MLD, the BSS transition only happens at the junction (red part shown in the right figure) of different non-collocated AP MLDs if an ESS is divided into more than one non-collocated AP MLD.
Non-collocated AP MLD 1
Non-collocated AP MLD 2
Collocated AP MLD

## Slide 9: Open Discussion
The challenge to enable the non-collocated AP MLD architecture is to standardize the interface between the non-collocated AP MLD UMAC and the non-collocated AP MLD LMAC.
  In 802.11 organization?
  In other industry alliance?

## Slide 10: Conclusions
We have discussed the non-collocated AP MLD architecture which allows seamless roaming without interrupting the data transmission.
We covered the following aspects
  Compatibility Issue.
    The EHT non-AP MLD only can associate with the collocated AP MLD.
  Discovery of non-collocated AP MLD
  Challenge.
    Standardize the interface between the non-collocated AP MLD UMAC and the non-collocated AP MLD LMAC

## Slide 11: References
[1] Duncan, et al. Seamless Roaming for UHR, DCN 11-22/1910r1

## Slide 12: Appendix Network Topology (considering pre-EHT STA)